## Slide 1: Introduction to Clinical biochemistry
Lecture : 1
////Dr. Shaimaa Munther

## Slide 2: Topics Headlines
• What is “Clinical Biochemistry”?
• How does it fit into clinical medicine?
• The uses of clinical biochemistry tests?
• What are the biochemical tests?
• Samples, techniques, instruments
• Result interpretation & factors affect test results?

## Slide 3: What is Clinical Biochemistry?
Clinical biochemistry (clinical chemistry or chemical pathology)
Application of chemical, molecular and cellular concepts and techniques to the understanding and evaluation of human health and disease
Disease is frequently caused by, or associated with, changes in the complex biochemistry of the body, and an understanding of these changes is essential to the diagnosis and treatment of patients.
Clinical Biochemistry deals with the detection and measurement of the chemical constituents of body fluids and its excretions.

## Slide 4: The use of biochemical tests
Biochemical investigations are involved in every branch of clinical medicine. The results of biochemical tests may be of use in:
Diagnosis .
Screening for disease .
Assessing the prognosis.
Monitoring of treatment.
Research into the biochemical basis of disease
Clinical trials of new drugs
Notes: Biochemical investigations hold the key for the diagnosis and prognosis of diabetes mellitus, jaundice, myocardial infarction, gout, pancreatitis, rickets, cancers, acid-base imbalance etc. Successful medical practice is unimaginable without the service of clinical biochemistry laboratory.

## Slide 5: How biochemical tests are used

## Slide 6: Biochemical Tests
In general, biochemical tests can be broadly divided into two groups:
1. Discretionary or Selective requesting:
These tests are carried out on the basis of an individual patient's clinical situation.
2. Screening tests:
These are used to search for disease without there being any necessary clinical indication that disease is present.
Notes: discretionary or selective requesting:biochemistry tests that are designed to answer specific questions, e.g., does the patient have increased blood urea/glucose concentration? Normally, these tests are useful to support the diagnosis.
these tests are carried out on the basis of an individual patient's clinical situation.
1. Why do I request this test?
2. What will I look for in the result?
3. If I find what I am looking for, will it affect my diagnosis?
4. How will this investigation affect my manage­ment of the patient?
5. Will this investigation ultimately benefit the patient?

## Slide 7: Discretionary Testing
Category | Example
To confirm a diagnosis | Plasma (free T4) and (thyroid-stimulating hormone, TSH) in suspected hyperthyroidism
To aid differential diagnosis | To distinguish between different forms of jaundice
To asses the severity of disease | Plasma (creatinine) or (urea) in renal disease
To monitor progress | Plasma (glucose) to follow of patients with diabetes mellitus
To detect complications or side effects | ALT measurements in patients treated with hepatotoxic drug
To monitor therapy | Plasma drug concentration in patients treated with antiepileptic drugs

## Slide 8: screening tests
Programmes to detect diseases in | Chemical investigations
PKA (phenylketonuria) | Serum [phenylalanine]
Hypothyroidism | Serum [TSH] and/or [thyroxine]
Open neural tube defect (NTD) | Maternal serum [α-fetoprotein]
Industrial exposure to lead | Blood [lead]
Notes: Screening tests : These tests are commonly employed to identify the inborn errors of metabolism, and to check the entery of toxic agents (pesticides, lead, mercury) into the body.

## Slide 9: Clinical biochemical tests
Clinical biochemical tests comprise over ⅓ of all hospital laboratory investigations these divided into:
Core biochemistry tests.
Specialized tests .
The emergency lab tests.
Notes: There are over 400 different tests which may be carried out in clinical biochemistry laboratories.
They vary from the very simple, such as the measurement of sodium, to the highly complex, such as DNA analysis, screening for drugs, or differentiation of lipoprotein variants.
Many high volume tests are done on large automated machines.
Less frequently performed tests may be conveniently carried out by using commercially prepared reagents packaged in "kit" form.
Some analyses are carried out manually.
The sections of clinical laboratory are:
Clinical pathology
Hematology
Clinical biochemistry
Clinical microbiology
Serology
Blood bank
Histology and cytology

## Slide 10: Clinical biochemical tests
Core biochemistry: Most biochemistry laboratories provide the "core analyses", commonly requested tests which are of value in many patients, on a frequent basis.
Core biochemical tests include the following:
Sodium, potassium, chloride and bicarbonate
Urea and creatinine
Calcium and phosphate
Total protein and albumin
Bilirubin and alkaline phosphatase
Alanine aminotransferase (ALT) and Aspartate aminotransferase (AST)
Glucose
Amylase…….

## Slide 11: Clinical biochemical tests
2. Specialized tests:
Not every laboratory is equipped to carry out all possible biochemistry requests. Large departments may act as reference centers where less commonly asked for tests are performed.
Specialized tests include the following :
Hormones
Specific proteins
Trace elements
Vitamins
Drugs
Lipids and lipoproteins
DNA analyses

## Slide 12: Clinical biochemical tests
3. The emergency lab tests:
All clinical biochemistry laboratories provide facilities for urgent tests. An urgent test is designated as one on which the clinician is likely to take immediate action. The main reason for asking for an analysis to be performed on an urgent basis is that immediate treatment depends on the result.

## Slide 13: Steps in the Investigation of a Patient
Patient History
Physical Examination
Laboratory Tests
Imaging Techniques
Diagnosis
Therapy
Evaluation

## Slide 15: Specimens used for biochemical analysis

## Slide 17: Common tests on urine performed away from the laboratory

## Slide 18: Laboratory work flow cycle
Laboratory work flow cycle:
The flow cycle includes the entire steps of laboratory test, starting from test ordering by a doctor until reporting the results.
Three phases of laboratory testing:
Pre-analytical: test ordering, specimen collection, transport and processing
Analytical-testing: performing of the test
Post-analytical: testing results transmission, interpretation, follow-up, retesting.
Notes: Steps in obtaining a laboratory test

## Slide 19: Laboratory work flow cycle

## Slide 20: 1- Pre-analytical Phase:
Test ordering
Specimen collection
Transport and processing

## Slide 21: Test ordering
Lab request form: it fills computerize or paper filled by the doctor then send it to the lab. The lab request contains a list of tests to be performed on specimen of patient. Each lab has its specific request; for example, chemistry request, hematology request… etc.
Note: The Lab report form differ from the lab request form in that it contains the result of patient.

## Slide 22: Specimen collection
The biological fluids employed in the clinical biochemistry laboratory include blood, urine, saliva, sputum, feces, tissue and cells, cerebrospinal fluid, peritoneal fluid, synovial fluid, pleural fluid, stones.
Among these, blood (directly or in the form of plasma or serum) is frequently used for the investigations in the clinical biochemistry laboratory.

## Slide 23: Collection of blood
Venous blood is most commonly used for a majority of biochemical investigations. It can be drawn from any prominent vein (usually from a vein on the front of the elbow).
Capillary blood (< 0.2 ml) obtained from a finger or thumb, is less frequently employed.
Arterial blood (usually drawn under local anesthesia) is used for blood gas determinations.
Notes: Precautions for blood collection : Use of sterile (preferably disposable) needles and syringes, cleaning of patients skin, blood collection in clean and dry vials/tubes are some of the important precautions.

## Slide 24: Transport and processing
Blood specimens should be transported to the laboratory as soon as possible after collection.
Special arrangements are needed for some specimens (e.g. for acid-base measurements, or unstable hormones) because of their lack of stability. Most other analytes are stable for at least 3 h in whole blood, or longer if plasma or serum is first sepa­rated from the cells.
As a rule, whole blood specimens for chemical analysis must not be stored in a refrigerator, since ionic pumps that maintain electrolyte gradients across the cell membrane are inactive at low temperatures. Conversely, separated serum or plasma is best refrigerated, to minimize chemical changes or bacterial growth.

## Slide 25: 2- Analytical-testing
Analysis is the performance of the test
Large analyzers can do many tests on a single sample tube with <1 mL plasma
Typical test sample volume is 10uL or less
Analysis time vary from 1 min (electrolytes) to 15 minutes (chemistries and immunoassays)

## Slide 26: Methods of Analysis
Many methods for analysis are present e.g. :
Ion specific electrodes
Spectrophotometry
Immunoassay
Electrophoresis
Nephelometry …etc.

## Slide 27: 3- Post-analytical Phase:
Post-analytical phase includs:
Testing results transmission
Interpretation
Follow-up
Retesting.

## Slide 28: Interpretation
Is Result Normal?
Has it changed?
Does it support the clinical hypothesis?
Is it consistent & support diagnosis, or inconsistent needs explanation
Is there is any Error in sampling, patient labeling, analysis, or reporting.
Is there is any need to Repeat the test?

## Slide 29: Why Analytical Results Vary
Inter-individual Variation
Age
Sex
Race
Genetics
Long term health status
Pre-analytical Variation
Transport
Exposure to UV light
Standing time before separation of cells
Centrifugation time
Storage conditions
Intra-individual Variation
Diet
Exercise
Drugs
Sleep pattern
Posture
Time of venipuncture
Length of time tourniquet is applied
Analytical Variation
Random errors
Systematic errors
Post-analytical
Transcriptions errors
Results reported to wrong patient
Notes: Inter & intra variation are patient variation usually
Pre-analytical
•Correct: Patient, Sample, Time, Draw order
•Appropriate preservation and handling
•Transport
Other Factors affecting results Post-analytical
•Calculation errors
•Transmission errors ( Telephoning)
•Transcription errors

## Slide 30
Diet
Dietary constituents may alter the concentrations of analytes in blood significantly (e.g. plasma [glucose] and [triglyceride] are affected by carbohydrate and fat-containing meals, respectively).
Drugs
Many drugs influence the chemical composition of blood. Such effects of drug treatment, for example, antiepileptic drugs.
Diurnal variation
The concentrations of many substances in blood vary considerably at different times of day (e.g. cortisol). Specimens for these analyses must be collected at the times specified by the laboratory, as there may be no reference ranges relating to their concentrations in blood at other times

## Slide 31
Venous blood specimens should be obtained with minimal stasis
Prolonged stasis can markedly raise the concentrations of plasma proteins and other non-diffusible substances (e.g. protein-bound substances).
Posture should be standardised if possible
When a patient's posture changes from lying to standing, there may be an increase of as much as 13% in the concentration of plasma proteins or protein-bound constituents, due to redistribution of fluid in the extracellular space.
Haemolysis should be avoided
since it renders specimens unsuitable for plasma K+, magnesium and many protein and enzyme activity measurements.
Notes: Several changes occur in whole blood specimens following collection. The commoner and more important changes that occur prior to the separation of plasma or serum from the cells are:
1. Glucose is converted to lactate: this process is inhibited by fluoride;
2. Several substances pass through the erythrocyte membrane, or may be added in significant amounts to plasma as a result of red cell destruction insufficient to cause detectable haemolysis. Examples include K+ and lactate dehydrogenase;
3. Loss of CO2 occurs, since the Pco2, of blood is much higher than in air;
4. Plasma [phosphate] increases due to hydrolysis of organic ester phosphates in the red cells;
5. Labile plasma enzymes lose their activity.

## Slide 32
What we mean by accuracy & precision?
Why specificity & sensitivity are important?
What we mean by reference ranges?

## Slide 33: Precision and accuracy
Precision is the reproducibility of an analytical method.
Repeated measurement of an analyte will be close to each other if precise
Notes: If there is 2 methods performed for the same analyte repeated measurement of the same analyte will show more closed results to each others ( less scattering )

## Slide 34: Precision and accuracy
Accuracy: defines how close the measured value is to the actual value.
It is the objective in every biochemical method to provide good precision and accuracy.
Automation of analyses has improved precision in most cases.
Notes: Accuracy is therefore poor, as if the sights are off, so repeated measurement of an analyte is accurate if it is very close to actual value known before .

## Slide 37: Precision and Accuracy
Notes: Interpretation of Results
Accuracy important for diagnosis
Precision important for monitoring
Both are essential for high quality results

## Slide 38: Analytical sensitivity and specificity
Sensitivity
The analytical sensitivity of an assay is a measure of how little of the analyte the method can detect to improve the detection limit to help in discrimination normal results and those with suspected disease ( Positivity in disease) .
Specificity
Analytical specificity of an assay relates to how good the assay is at discriminating between the requested analyte and potentially interfering substances. So it measures the negativity in normal results .

## Slide 39: Summary :
Accurate : it gives a correct result
Precise : it give the same result if repeated
Sensitive : it measure law concentration of the analyte
Specific : is not subjected to interferance by other substance

## Slide 40: Interpretation of Results What is “Normal” ?
Reference ranges make no assumptions about normality.
An abnormal result, i.e. outside a reference interval, does not always indicate presence of pathological processes- Nor a ‘normal’ result its absence.
The more ‘abnormal’ a result, i.e. the greater the difference from the reference interval, the greater the probability that it is related to a pathological process.

## Slide 41: Reference Range
Reference Range (Normal Range) :
Usually established by testing a group of apparently ‘healthy’ individuals, to represent the wider population for which the service is provided.
The range of ‘normals’ is calculated from a Gaussian
distribution curve – 2 SD below and 2 SD above the mean, includes 95% of all values.

## Slide 42: The Normal Distribution

## Slide 43: Specimen rejection criteria
Specimen rejection criteria:
Specimen improperly labeled or unlabeled
Specimen improperly collected or preserved
Specimen submitted without properly completed request form
Hemolyzed sample