## Slide 1: lec 8 Pharmaceutical Technology aromatic waters
Stage: 3/ 1st course
Dr. Ameer S. Sahib

## Slide 2: Aromatic water
Aromatic waters are clear, aqueous solutions saturated with volatile oils or other aromatic or volatile substances.
They are saturated solutions usually of volatile oils or similar substances in distilled water.
Aromatic waters are not therapeutically potent because of the very small proportion of the active ingredient present in them.

## Slide 3: Examples of Aromatic Waters
Aromatic waters were prepared from a number of volatile substances, including:
orange oil
flower oil,
Peppermint oil,
anise oil,
wintergreen oil,
camphor,
chloroform.

## Slide 4: Peppermint waters

## Slide 5: Rose water

## Slide 6: Camphor water
Reduce itching, Rubefacient,
Soothing eye, soothing cough

## Slide 7: Hamamelis waters (WITCH HAZEL)
Hamamelis water 12.5% v/v and naphazoline 0.01% w/v Temporary relief of eye redness due to minor eye irritations

## Slide 8: Aromatic water uses
Aromatic Waters are used as Intermediate solutions for manufacturing of other preparations and also used as the liquid phase of emulsions and suspensions.
Aromatic water is used as a flavoring agent. Aromatic waters provide a pleasantly flavored medium for administration of water – soluble drugs when taste masking of undesirable taste is a problem. The odors and tastes of aromatic waters are of the volatile substances from which they are prepared.
Aromatic water prepared from essential oils like peppermint and anise waters have some carminative properties.

## Slide 9
Chloroform water: was used in expectorant preparations (dose 5-15ml).
Several aromatic waters are not used as vehicles for oral medication, but can be used topically. These include: Rose water, Hamamelis water and camphor water.
Rose water used as perfume,
Hamamelis water or witch Hazel, is employed commonly as a rub and also is used as an astringent and perfume in aftershave lotion and other cosmetic products.
Camphor water is frequently prescribed in eyedrops and eye washes for its slight refreshing effect.

## Slide 10: Preparation of aromatic water
Most of the aromatic substances in the preparation of aromatic waters have very low solubility in water, and even though the water may be saturated, its concentration of aromatic material is still rather small.
The official method of preparation of aromatic water are:
1. Distillation 2. Direct solution 3. Alternate solution
There are some modifications in the preparation methods:
Formulas for concentrates of the aromatic principles containing either alcohol or solubilizing agent like surfactant have been developed, and manufactured as concentrated waters.
To prepare an aromatic water the concentrates are diluted with water before use.

## Slide 11: 1- Distillation method
The distillation method consists of placing the odoriferous portion of the plant in a suitable still with sufficient purified water and then distilling most of the water, avoiding charring or scorching (burning) of the substance.
The excess oil is separated from the distillate .
The label of commercial witch hazel contain one or more symbol of (X) , each X represent one distillation. This process is called re-distillation. This is done to get a saturated solution if it is not obtained from the 1st distillation.

## Slide 12
Most of aromatic waters can be prepared by distillation. However, it is not practical or economically feasible to use this method in most cases, since other method is of low cost and with simple apparatus required.
Note: aromatic waters which are prepared directly from fresh plant material, e.g. stronger rose water, orange flower water, and Hamamelis water can not be prepared by any method other than distillation.

## Slide 13: 2- Direct solution method
It is done by shaking 2 grams or 2 ml (if liquid) of the volatile oil substance (suitably comminuted if a solid) with 1000 ml of purified water in a container of sufficient capacity.
The volatile substance is agitated with purified water for a period of 15 minutes.
The mixture is set aside for at least 12 hours to ensure saturation before it is filtered through wetted filter paper
The filter paper must be wet to prevent the passage of excess oil in to the filtrate and eliminate absorption of the dissolved aromatics by the filter.
Not necessary to make up to volume through the filter , since a saturated solution is sought or obtained.

## Slide 14: Direct solution method
It is easy method and performed with simple equipment.
In spite of repeated filtration it is difficult to obtain a brilliantly clear preparation owing to formation of extremely fine particles (clarification problem). This can be obviated by using boiling purified water.
It considered time consuming method.
Chloroform water is prepared by solution without clarification problem exists in this case, since a slight excess of chloroform must remain in the bottle, this is due to chloroform is heavier than water, so the excess will remain at the bottom of the container.

## Slide 16: 3- Alternate solution method
This method has been developed to overcome difficulties in the simple solution method; clarification and time consuming.
The volatile material 2ml is mixed with 15g purified talc or with sufficient quantity of purified siliceous earth (silica) or pulped filter paper. ( an adsorbent)
The mixture is agitated with a 1000ml of purified water for 10 minutes prior to filtration.
The talc or other inert material functions as both a filter aid and a distribution agent.
It serves to accelerate the rate of solution by adsorbing and facilitating the breaking up of the aromatic substance into fine particles, thus increasing the surface area exposed to solvent action, and it facilitates the clarification of the solution.
Disadvantage of this method is that the purified talc pass through the filter paper because it is subdivided too finely.

## Slide 17: Other methods which have been suggested for the preparation of aromatic waters are:
Dilution method
An alcoholic solution of the essential oil is mixed with water and talc. The mixture is agitated; after several hours it is filtered.
The concentrate (alcoholic solution of oil) contains 50-55% alcohol by volume.
One volume of concentrate is diluted with 39 volume of water, producing an aromatic water contains less than 1.5 percent of alcohol.
Disadvantage: aqueous preparation that contain small amounts of alcohol are prone to alterations in flavor and aroma, as a consequence of oxidative degradation of the alcohol.
Other than alcohol non ionic SAA may be used like Tween 80 (polysorbate 80) due to solubilization by micelles formation.

## Slide 18: Stability of aromatic waters
Aromatic waters are not very stable preparations.
Improper storage cause instability, many waters support mold growth
Excessive exposure to light and change in temperature cause aromatic waters to lose characteristics (loss of aroma).
Separation of volatile material when the temperature decrease causing cloudiness.
Salting out of volatile substance (leads to volatile oil separation) upon addition of water solution of strong electrolytes and may collect on surface of the liquid imparting a burning taste to the first dose.
Loss in flavor may be observed if aromatic waters are used in the external phase of dispersions, owing to adsorption of aromatic substances by suspended matter.
Oxidative degradation involving dissolved atmospheric oxygen with the aroma bearing solutes which may be catalyzed by light and trace metals like iron and copper

## Slide 19
↓ Temp
Oil separation (cloudiness)
↑ Temp
Loss of aroma
Oxygen + light
Oil oxidative degradation
Electrolytes
Salting out