## Slide 1
lec 2 Pharmaceutical Technology II semisolid dosage form
Stage: 3/ 1st course
Dr. Ameer S. Sahib

## Slide 2
Ointments, creams and gels
Ointments, creams, and gels are semisolid dosage forms intended for topical application. They may be applied to the skin, placed on the surface of the eye, or used nasally, vaginally, orally, or rectally.
Most of these preparations are used for the effects of the therapeutic agents they contain. The unmedicated ones are used for their physical effects as protectants (occlusive) or lubricants (emollient).

## Slide 3
Topical preparations are used for both local and systemic effects.
Systemic drug absorption should always be considered when using topical products if the patient is pregnant or nursing, because drugs can enter the fetal blood supply and breast milk and be transferred to the fetus or nursing infant.

## Slide 4
Ointments
Ointments are semisolid preparations intended for external application to the skin or mucous membranes. Ointments may be medicated or not. Unmedicated ointments are used for the physical effects they provide as protectants, emollients, or lubricants.
The differentiation between semisolid dosage forms is according to the type of the base used and the components (aqueous or oleaginous) ratios for each one.

## Slide 5
Ointment bases
Ointment bases, as described, may be used for their physical effects or as vehicles for medicated ointments
Ointment bases are generally classified by the USP (2) into four groups:
Oleaginous bases,
(b) Absorption bases,
(c) Water-removable bases,
(d) Water-soluble bases.

## Slide 6
Oleaginous Bases
Oleaginous bases are also termed hydrocarbon bases. On application to the skin, they have an emollient effect, protect against the escape of moisture, are effective as occlusive dressings, can remain on the skin for long periods without drying out, and because of their immiscibility with water, are difficult to wash off.
Water and aqueous preparations may be incorporated, but only in small amounts and with some difficulty. Petrolatum, white petrolatum, yellow ointment, and white ointment are examples of hydrocarbon ointment bases.

## Slide 7
When powdered substances are to be incorporated into hydrocarbon bases, liquid petrolatum (mineral oil) may be used as the levigating agent (Levigation is the process of decreasing the particle size of powders via triturating them with a mortar and pestle along with a small amount of liquid wherein the substance is insoluble to).

## Slide 8
Petrolatum
Petrolatum, USP, is a purified mixture of semisolid hydrocarbons obtained from petroleum. It is an unctuous (oily) mass, varying in color from yellowish to light amber. It melts at 38°C to 60°C and may be used alone or in combination with other agents as an ointment base.
Petrolatum is also known as yellow petrolatum and petroleum jelly. A commercial product is Vaseline.
White Petrolatum, USP, is a purified mixture of semisolid hydrocarbons from petroleum that has been wholly or nearly decolorized with same purposes of petrolatum (White Vaseline).

## Slide 9
Yellow Ointment, USP.
This ointment prepared by using yellow wax 5%w/w with petrolatum. Yellow wax is the purified wax obtained from the honeycomb of the bee Apis mellifera. (yellow wax+petrolatum)
It is also called simple ointment, it has a slightly greater viscosity than plain petrolatum.
White Ointment, USP. This ointment differs from yellow ointment by substitution of white wax (bleached and purified yellow wax) and white petrolatum in the formula.
(white wax+white petrolatum)

## Slide 10
Absorption Bases
Absorption bases are of two types:
Those that permit the incorporation of aqueous solutions resulting in the formation of water in oil (W/O) emulsions (e.g., hydrophilic petrolatum)
(b) Those that are W/O emulsions (syn: emulsion bases) that permit the incorporation of additional quantities of aqueous solutions (e.g., lanolin).
These bases may be used as emollients, although they do not provide the degree of occlusion afforded by the oleaginous bases.
Absorption bases are not easily removed from the skin with water washing, because the external phase of the emulsion is oleaginous.
Absorption bases are useful as pharmaceutical adjuncts to incorporate small volumes of aqueous solutions into hydrocarbon bases. This is accomplished by incorporating the aqueous solution into the absorption base and then incorporating this mixture into the hydrocarbon base.

## Slide 11
Hydrophilic Petrolatum, USP,
has the following formula for the preparation of 1,000 g:
Cholesterol: 30 g
Stearyl alcohol: 30 g
White wax: 80 g
White petrolatum: 860 g
Commercial products, Aquaphor and Aquabase, variations of hydrophilic petrolatum, have the capacity to absorb up to three times their weight in water and are useful to help incorporate a water-soluble drug, for example, tobramycin sulfate, into an oleaginous ointment base. This concept is used in the preparation of ophthalmic ointments. Eucerin is a 50% W/O emulsion.

## Slide 12
Lanolin, USP, (anhydrous lanolin) obtained from the wool of sheep (Ovis aries), is a purified waxlike substance that has been cleaned, deodorized, and decolorized. It contains not more than 0.25% water. Additional water may be incorporated into lanolin by mixing.
Modified Lanolin, USP, is lanolin processed to reduce the contents of free lanolin alcohols and any detergent and pesticide residues.

## Slide 13
Water-Removable Bases
Water-removable bases are oil-in-water emulsions commonly called creams. Because the external phase of the emulsion is aqueous, they are easily washed from skin and are often called water-washable bases. They may be diluted with water or aqueous solutions. They can absorb serous discharges.
Hydrophilic Ointment, USP, has the following formula for 1,000 g:
Methylparaben: 0.25g
Propylparaben: 0.15g
Sodium lauryl sulfate: 10g
Propylene glycol: 120g
Stearyl alcohol: 250g
White petrolatum: 250g
Purified water: 370g
Sodium lauryl sulfate is the emulsifying agent, with the stearyl alcohol and white petrolatum constituting the oleaginous phase of the emulsion and the other ingredients the aqueous phase. Methylparaben and propylparaben are antimicrobial preservatives.

## Slide 14
Water-Soluble Bases
Water-soluble bases do not contain oleaginous components. They are completely water washable and often referred to as greaseless. Because they soften greatly with the addition of water, large amounts of aqueous solutions are not effectively incorporated into these bases. They mostly are used for incorporation of solid substances.

## Slide 15
Polyethylene Glycol (PEG) Ointment
Polyethylene glycol, NF, PEG is a polymer of ethylene oxide and water represented by the formula H(OCH2CH2)nOH, in which n represents the average number of oxyethylene groups. The numeric designations associated with PEGs refer to the average molecular weight of the polymer(ex PEG200, PEG4000 etc). PEGs having average molecular weight below 600 are clear, colorless liquids; those with molecular weight above 1,000 are waxlike white materials; and those with molecular weight in between are semisolids. The greater the molecular weight, the greater the viscosity. The NF lists the viscosity of PEGs ranging from average molecular weight of 200 to 8000. Combining PEG 3350, a solid, with PEG 400, a liquid, results in a very pliable semisolid ointment. If a firmer ointment is desired PEG3350 added more, and vice versa.

## Slide 16
Selection of the Appropriate Base
Selection of the base to use in the formulation of an ointment depends on careful assessment of a number of factors, including the following:
• Desired release rate of the drug substance from the ointment base
• Desirability of topical or percutaneous drug absorption
• Desirability of occlusion of moisture from the skin
• Stability of the drug in the ointment base
• Effect, if any, of the drug on the consistency or other features of the ointment base
• Desire for a base easily removed by washing with water
• Characteristics of the surface to which it is applied

## Slide 17
Preparation of Ointments
Ointments are prepared by two general methods,
Incorporation
(b) fusion,
depending primarily on the nature of the ingredients.

## Slide 18
Incorporation
The components are mixed until a uniform preparation is attained (ointment is prepared by thoroughly rubbing and working the components together on the hard surface until the product is smooth and uniform).
On a small scale using mortar and pestle or slab and spatula. Others will use an ointment mill, an electronic mortar and pestle, or a device called an “Unguator,”, can be controlled manually or via computer software.
Through incorporation of solids, a small portion of the powder is mixed with a portion of the base until uniform. Geometric dilution is continued until all portions of the powder and base are combined and thoroughly and uniformly blended.

## Slide 19
It often is desirable to reduce the particle size of a powder or crystalline material before incorporation into the ointment base so the final product will not be gritty. This may be done by levigating, or mixing the solid material in a vehicle in which it is insoluble to make a smooth dispersion.
The levigating agent (e.g., mineral oil for bases in which oils are the external phase or glycerin for bases in which water is the external phase) should be physically and chemically compatible with the drug and base. The levigating agent should be about equal in volume to the solid material.
For incorporating a gummy material, such as camphor, pulverization by intervention can be used. The material is dissolved in a solvent and spread out on the pill tile. The solvent is allowed to evaporate, leaving a thin film of the material onto which the other ingredient or ingredients are spread.

## Slide 20
Incorporation of Liquids. Liquid substances or solutions of drugs, are added to an ointment according to the base’s capacity to accept the volume required.
For example, only very small amounts of an aqueous solution may be incorporated into an oleaginous ointment, whereas hydrophilic ointment bases readily accept aqueous solutions.
When it is necessary to add an aqueous preparation to a hydrophobic base, the solution first may be incorporated into a minimum amount of a hydrophilic base and then that mixture added to the hydrophobic base.
However, all bases, even if hydrophilic, have their limits to retain liquids, beyond which they become too soft or semiliquid.

## Slide 21
Fusion
By the fusion method, all or some of the components of an ointment are combined by being melted together and cooled with constant stirring until congealed.

## Slide 22
Components not melted are added to the congealing mixture as it is being cooled and stirred.
Naturally, heat-labile substances and any volatile components are added last, when the temperature of the mixture is low enough not to cause decomposition or volatilization of the components.
Substances may be added to the congealing mixture as solutions or as insoluble powders levigated with a portion of the base.
On a small scale, fusion may be conducted in a porcelain dish or glass beaker.
On a large scale, it is carried out in large steam jacketed kettles.

## Slide 23
Medicated ointments and ointment bases containing components such as beeswax, paraffin, stearyl alcohol, and high molecular weight PEGs, which do not lend themselves well to mixture by incorporation, are prepared by fusion.
By this general process, the materials with the highest melting points are heated to the lowest required temperature to produce a melt.
The additional materials are added with constant stirring during cooling of the melt until the mixture is congealed.

## Slide 24
In preparation of ointments having an emulsion base, the method of manufacture often involves both melting and emulsification.
The water-immiscible components such as the oil and waxes are melted together in a steam bath to about 70°C to 75°C. Meantime, an aqueous solution of the heat-stable, water soluble components is prepared and heated to the same temperature as the oleaginous components (If the aqueous solution is not at the same temperature as the oleaginous melt, some of the waxes will solidify on addition of the colder aqueous solution to the melted mixture). Then the aqueous solution is slowly added, with mechanical stirring, to the melted oleaginous mixture.
The temperature is maintained for 5 to 10 minutes, and the mixture is slowly cooled and stirred until congealed.

## Slide 25
Creams
Pharmaceutical creams are semisolid preparations containing one or more medicinal agents dissolved or dispersed in either a water-in-oil (W/O) emulsion or an oil-in-water (O/W) emulsion or in another type of water-washable base.
The so-called vanishing creams are oil-in-water emulsions containing large percentages of water and stearic acid or other oleaginous components. After application of the cream, the water evaporates, leaving behind a thin residue film of the stearic acid or other oleaginous component.

## Slide 26
Creams find primary application in topical skin products and in products used on mucous membranes, such as rectally and vaginally.
Many patients and physicians prefer creams to ointments because they are easier to spread and remove.
Creams have a relatively soft, spreadable consistency; an example of a W/O cream is cold cream and an example of an O/W cream is hydrophilic ointment.
Creams are generally described as either washable or non-washable, reflecting that an emulsion with an aqueous external continuous phase (O/W) is more easily removed than one with a nonaqueous external phase (W/O emulsion).

## Slide 27
Preparation of Creams
Creams may be formulated from a variety of oils, both mineral and vegetable, and from fatty alcohols, fatty acids, and fatty esters. The solid excipients are melted at the time of preparation. Emulsifying agents include nonionic surfactants, detergents, and soaps.
  Preparation usually involves separating the formula components into two portions:
lipid and aqueous. The lipid portion contains all water-insoluble components and the aqueous portion the water-soluble components. Both phases are heated to a temperature above the melting point of the highest melting component. The phases then are mixed, and the mixture is stirred until reaching ambient temperature or the mixture has congealed. Mixing generally is continued during the cooling process to promote uniformity. Traditionally, the aqueous phase is added to the lipid phase, but comparable results have been obtained with the reverse procedure.

## Slide 28
High-shear homogenization may be employed to reduce particle or droplet size and improve the physical stability of the resultant dosage form.

## Slide 29
Gels
Gels (sometimes called jellies) are semisolid systems consisting of dispersions of small or large molecules in an aqueous liquid vehicle rendered jellylike by the addition of a gelling agent.

## Slide 30
Among the gelling agents used are synthetic macromolecules, such as carbomer 934; cellulose derivatives, such as carboxymethylcellulose CMC or hydroxypropyl methylcellulose HPMC; and natural gums, such as tragacanth.
Carbomers are high molecular weight water-soluble polymers of acrylic acid cross-linked with allyl ethers of sucrose and/or pentaerythritol. Their viscosity depends on their polymeric composition.
Single-phase gels are gels in which the macromolecules are uniformly distributed throughout a liquid with no apparent boundaries between the dispersed macromolecules and the liquid.
A gel mass consisting of floccules of small distinct particles is termed a two-phase system, often referred to as a magma.
Gels may thicken on standing, forming a thixotrope, and must be shaken before use to liquefy the gel and enable pouring.

## Slide 31
Medicated gels may be prepared for administration by various routes, including the skin, the eye, the nose, the vagina, and the rectum. Gels can be administered by the topical oromucosal routes.
Gels formed with large organic molecules may be formed by dispersing the molecule in the continuous phase (e.g., by heating starch), by cross-linking the dispersed molecules by changing the pH (as for carbomers), or by reducing the continuous phase (as for jellies formed with sucrose).
Care should be taken to ensure uniformity of the APIs by dispersing them by vigorous mixing or milling or by shaking if the preparation is less viscous.
Gels should be stored in tight containers to prevent water loss. Avoid freezing gels.