## Slide 1
lec 5 Pharmaceutical Technology II
aerosols and foams
Stage: 3/ 1st course
Dr. Ameer S. Sahib

## Slide 2
Aerosols are the pressurized systems, (containing one or more active ingredients) which act by releasing either continuous or metered dose of fine mist spray (a fine dispersion of liquid and/or solid materials in a gaseous medium) after a proper activation of its valve system (upon valve actuation).
The term pressurized package is commonly
used when referring to the aerosol container or completed product
Aerosols

## Slide 3
Pressure is applied to the aerosol system through the use of one or more liquefied or gaseous propellants. Upon activation of the valve assembly of the aerosol, the pressure exerted by the propellant forces the contents of the package out through the opening of the valve.
The physical form in which the contents are emitted depends on the formulation of the product and the type of valve. Aerosol products may be designed to expel their contents as a fine mist; a coarse, wet, or dry spray; a steady stream; or a stable or a fast-breaking foam.
An aerosol for inhalation therapy, as in the treatment of asthma or emphysema, must present particles in the form of a fine liquid mist or as finely divided solid particles. Particles <6 μm will reach the respiratory bronchioles, and those <2 μm will reach the alveolar ducts and alveoli

## Slide 5
Types of Aerosols
Inhalation aerosols, commonly known as metered-dose inhalers (MDIs), are intended to produce fine particles or droplets for inhalation through the mouth and deposition in the pulmonary tree.
Each actuation of the valve releases measured mass and appropriate quality of the active substance.

## Slide 6
Types of aerosols including:
Inhalation aerosol (pulmonary tree)
Nasal aerosols (nasal vestibule)
Lingual aerosols (surface of the tongue)
Topical aerosols (skin).
Topical aerosol drug products may be designed, as needed, to deliver a metered amount of formulation upon actuation of the designed valve or continuous release of formulation during depressed status of the valve.

## Slide 7
Advantages of the Aerosol Dosage Form
1. A portion of medication may be easily withdrawn from the package without contamination or exposure to the remaining material.
2. By virtue of its hermetic character, the aerosol container protects medicinal agents from atmospheric oxygen, light, and moisture.
3. Topical medication may be applied in a uniform thin layer to the skin without anything else touching the affected area (fingertip application sometimes causes irritation). The rapid volatilization of the propellant also provides a cooling, refreshing effect.

## Slide 8
4. By proper formulation and valve control, the physical form and the particle size of the emitted product may be controlled, which may contribute to the efficacy of a drug, as with the fine controlled mist of an inhalant aerosol.
5. Aerosol application is a clean process, requiring little or no washup by the user.
6. Aerosols used for large surfaces.

## Slide 9
The Aerosol Principle
An aerosol formulation consists of two component parts: the product concentrate and the propellant.
The product concentrate is the active ingredient of the aerosol combined with the required adjuncts, such as antioxidants, surface-active agents, and solvents, to prepare a stable and efficacious product.
The concentrate can be a solution, suspension, emulsion, semisolid, or powder.

## Slide 10
The propellant provides the force that expels the product concentrate from the container and additionally is responsible for the delivery of the formulation in the proper form. It must be inflammable, nontoxic.
In certain aerosol systems, compressed gases—carbon dioxide, nitrogen, and nitrous oxide—are employed as the propellant.

## Slide 11
Propellant types
Type I - Propellent A: Liquified gas
a- Oral and Inhalation (fluorinated HC) Cl₃ F C, Cl₂ F₂C
b- Topical Pharmaceutical Aerosol ( HC ) propane, butane (why?)
When the propellant is a liquefied gas or a mixture of liquefied gases, it can also serve as the solvent or vehicle for the product concentrate.
They are immiscible with water and have a density less than 1. (?)
When the propellant is in the external phase, foams are not created but sprays or wet streams result.
Fluorinated hydrocarbon gases may be liquefied by cooling below their boiling point or by compressing the gas at room temperature
Type II Propellent B: Compressed gas N₂ , CO₂

## Slide 12
Chlorofluorocarbons (CFCs)
CFCs propellants are being phased out and will be prohibited for nonessential use under federal regulations following recognition that they reduce the amount of ozone in the stratosphere, which results in an increase in the amount of ultraviolet radiation reaching the earth, an increase in the incidence of skin cancer, and other adverse environmental effects.
Under the law, the FDA has the authority to exempt from the prohibition specific products under the agency’s jurisdiction when there is sufficient evidence showing that (a) there are no technically feasible alternatives to the use of a CFC propellant in the product, (b) the product provides a substantial health or other public benefit unobtainable without the use of the CFC, and (c) the use does not involve a significant release of CFCs into the atmosphere.

## Slide 13
Liquified gas propellant
This propellant is established an equilibrium quickly between the portion of propellant that remains liquefied and that which vaporizes and occupies the upper portion of the aerosol container.
The vapor phase exerts pressure in all directions, which upon actuation of the aerosol valve, forces the liquid phase up the dip tube and out of the orifice of the valve into the atmosphere.
As the propellant meets the air, it expands and evaporates because of the drop in pressure, leaving the product concentrate as airborne liquid droplets or dry particles, depending upon the formulation.

## Slide 14
As the liquid phase is removed from the container, equilibrium between the propellant remaining liquefied and that in the vapor state is reestablished.
However, when the liquid reservoir is depleted, the pressure may not be maintained, and the gas may be expelled from the container with diminishing pressure until it is exhausted.

## Slide 15
Compressed gas propellant
Compressed gas propellants occupy the head space above the liquid in the can.
When the aerosol valve is opened the gas pushes the liquid out of the can.
The amount of the gas in the headspace remains the same but it has more space and as a result the pressure will drop during the life of the can.
Spray performance is maintained however by careful choice of the aerosol valve and actuator.

## Slide 16
Actuator and Valve Assembly

## Slide 17
Actuator: The actuator permits easy opening and closing of the valve The design of the inner chamber and size of the emission orifice of the actuator contribute to the physical form (mist, coarse spray, solid stream, or foam) in which the product is discharged. The type and quantity of propellant used and the actuator design and dimensions control the particle size of the emitted product. Larger orifices (and less propellant) are used for products to be emitted as foams and solid streams than for those intended to be sprays or mists.
Stem: supports the actuator and delivers the formulation in the proper form to the chamber of the actuator.
Gasket: placed with the stem and prevents leakage of the formulation when the valve is closed.

## Slide 18
Spring: holds the gasket in place and is the mechanism by which the actuator retracts when pressure is released, returning the valve to the closed position.
Mounting cup: attached to the aerosol can or container and holds the valve in place.
Housing: Directly below the mounting cup, the housing links the dip tube and the stem and actuator.
Dip tube: extends from the housing down into the product; brings the formulation from the container to the valve

## Slide 19
Spray types
Metered dose inhaler (MDI) for potent medications (pulmonary route)
Continuous (Used for topical application)

## Slide 20
Filling Operations
Cold Filling
In the cold method, both the product concentrate and the propellant must be cooled to −34.5°C to −40°C (−30°F to 40°F). This temperature is necessary to liquefy the propellant gas. The cooling system may be a mixture of dry ice and acetone or a more elaborate refrigeration system.
Because of the low temperatures required, aqueous systems cannot be filled by this process, because the water turns to ice.

## Slide 21
Pressure Filling
By the pressure method, the product concentrate is quantitatively placed in the aerosol container, the valve assembly is inserted and crimped into place, and the liquefied gas, under pressure, is metered into the valve stem from a pressure burette.
Pressure filling is used for most pharmaceutical aerosols. It has two advantages over cold filling: There is less danger of moisture contamination of the product, and less propellant is lost in the process.

## Slide 22
Class | Examples | 
Anti-infective agents | Povidone iodine Tolnaftate Terbinafine | Lamisil®
Adrenocortical steroids | Betamethasone dipropionate and valerate, Dexamethasone, and Triamcinolone acetonide | 
Local anesthetic | Dibucaine hydrochloride. | 
Hair growth | Minoxidil | Rogaine®
Topical aerosols

## Slide 23
Pharmaceutical Foams

## Slide 24
Pharmaceutical Foams
A foam is an emulsion dosage form containing dispersed gas bubbles, it is a gas in liquid dispersion. When dispensed, it has a fluffy, semisolid consistency.
Medicated foams are emulsions containing a dispersed phase of gas bubbles in a liquid continuous phase containing the active pharmaceutical ingredient.

## Slide 25
Medicated foams are packaged in pressurized containers or special dispensing devices and are intended for application to the skin or mucous membranes.
The medicated foam is formed at the time of application. Surfactants are used to ensure the dispersion of the gas and the two phases. Medicated foams have a fluffy, semisolid consistency and can be formulated to break to a liquid quickly or to remain as foam to ensure prolonged contact.
Medicated foams intended to treat severely injured skin or open wounds must be sterile.
Medicated foams

## Slide 26
Preparation of Foams
A foam may contain one or more active pharmaceutical ingredients, surfactants, aqueous or nonaqueous liquids, and propellants.
If the propellant is in the internal, or discontinuous, phase, a stable foam is discharged (O/W type).
If the propellant is in the external, or continuous, phase, a spray or a quick-breaking foam is discharged (W/O type).
Quick-breaking foams formulated with alcohol create a cooling sensation when applied to the skin and may have disinfectant properties.

## Slide 27
Quick breaking foams are thermally unstable and collapse upon exposure to skin temperature.

## Slide 28
Advantage of foams
It is easy to be used the patient.
It is easy to be applied and spread topically than other semisolid dosage forms.
Used for vaginal, rectal route, and for burn dressing.
Foams may be formulated in various ways to provide emollient or drying functions to the skin, depending on the formulation constituents.

## Slide 29
Surfactants used
Anionic surfactants: Fatty acids saponified with triethanolamine,
Nonionic surfactants: such as the polyoxyethylene fatty esters, polyoxyethylene sorbitan esters, alkyl phenoxy ethanols, and alkanolamides.
The nonionic surfactants are present fewer compatibility problems because they charge no electronic charge

## Slide 30
Foam types 1 -Breaking Foam
A quick breaking foam creates a foam when emitted from the container but the foam collapses in a relatively short time.
This type of foam is used to apply the product concentrate to a large area without having to manually rub or spread the product. Also, the active drug is more rapidly available because the foam quickly collapses.

## Slide 31
Foam type 2 -Stable foams
Depending on the components, the emitted product can be a stable foam (shaving cream type)
Stable foams are produced when surfactants are used that have limited solubility in both the organic and aqueous phases.
Surfactants concentrate at the interface between the propellant and the aqueous phase forming a thin film referred to as the "lamella." It is the specific composition of this lamella that dictates the structural strength and general characteristics of the foam.
Thick and tightly layered lamellae produce very structured foams which are capable of supporting their own weight