## Slide 1
Lecture 1&2
Method of imaging the Head

## Slide 2: Method of imaging the brain
Human brain imaging methods noninvasive, though they may include exposure to ionizing radiation or contrast agents. These methods can be equally used to noninvasively study brain structure and function.
New technologies allow non-invasive spatial mapping, (morphology), and observations of processes within the brain during set tasks. There are a range of scanning techniques, their purpose are described below

## Slide 3: 1. X-ray
the x-ray, early structural imaging developed in 1895. X-rays measure the density of tissues. X-rays use photons, a quantum of visible light that possesses energy; the photons are passed through the body and deflected and absorbed to different degrees by the person’s tissues. The photons were initially recorded onto a silver halide film as they passed out of the body. Dense structures such as bone, which block most of the photons, appear white; structures containing air appear black; and muscle, fat, and fluids appear in various shades of gray.

## Slide 4: 2. CT
A computerized tomography (CT) scan is a series of X-ray images converted into cross-sectional images of your brain. These X-rays are combined to form cross-sectional slices or even a 3-D model of your brain. The results of a CT scan can also provide more detail than a standard X-ray.
CT scans can:
find certain types of brain injuries (hemorrhagic strokes)
identify cancer
locate brain swelling or bleeding
reveal structural brain changes from schizophrenia

## Slide 5: 3.Magnetic Resonance Imaging Magnetic
This imaging method is a painless, non-invasive imaging technology that produces 3D detailed anatomical images of our brain.
Resonance Imaging (MRI) is based on the principle of nuclear magnetic resonance (NMR) and uses radiofrequency waves the scanner uses magnetic fields that emit radio waves to manipulate the magnetic position of the hydrogen protons of the body.
The rotation and energy release of the protons are detected by a powerful antenna which sends the information to a computer. The computer analyzes the information, and through complex mathematical calculations, creates a clear, cross-sectional black-and-white image of the body. These images can be converted into
three-dimensional pictures of the scanned area, with the results looking something like the images below.

## Slide 6
Clinically, MRI has become the most important diagnostic imaging modality in neuroscience. One of the many benefits of MRI in
The central nervous system is that the radiofrequency signals readily penetrate the skull and spinal column, allowing the tissue within it to be imaged with no interference.
Radiofrequency energy is also non-ionizing, so MRI is
safer than CT scanning.
MRI provides the best visualization of parenchymal (tissue) abnormalities in the brain and spinal cord including tumors, demyelinating lesions, infections, vascular lesions (such as stroke), developmental abnormalities, and traumatic injuries.

## Slide 7: 4. fMRI
Functional magnetic resonance imaging (fMRI) can detect changes in blood flow and oxygen levels that result from your brain’s activity. It uses the magnetic field of the scanner to affect the magnetic nuclei of hydrogen atoms, so they can be measured and converted into images.
MRIs display anatomic structure and fMRIs measure metabolic function.
fMRIs have many uses, such as:
assessing brain activity finding brain abnormalities
creating pre-surgical brain maps

## Slide 8: 4. fMRI

## Slide 9: 5.PET
A positron emission tomography (PET) scan uses a radioactive tracer that attaches to the glucose in your bloodstream. Since your brain uses glucose as its primary fuel source, the tracer accumulates in areas of higher brain activity.
A PET scan is able to see these tracers and observe how they move and accumulate in your brain. This allows doctors to see trouble spots where glucose isn’t moving correctly.
PET scans can evaluate:
seizures Alzheimer’s tumors

## Slide 10: 6.EEG
An electroencephalography (EEG) test measures your brain waves. Before the scan, clinicians will attach small electrodes to your scalp that are attached to wires. These electrodes detect electrical activity in your brain and send it to a computer where it creates a graph-like image. Each type of frequency appears on its own line and gives your doctor information about your brain activity.
EEG can detect issues such as:
anxiety
head injuries epilepsy
sleep disruption

## Slide 11: 6.EEG

## Slide 12: 7.MEG
Magnetoencephalography (MEG) measures the magnetic field from neuron electrical activity. This type of scan can locate and identify malfunctioning neurons in your brain. Doctors use MEG to evaluate both spontaneous brain activity, as well as neuronal responses triggered by stimuli. MEG allows doctors to assess areas such as:
epilepsy sources motor areas sensory areas
language and vision

## Slide 13: 7.MEG

## Slide 14: 8. NIRS
Near-infrared spectroscopy (NIRS) monitors your brain’s oxygen saturation. It uses infrared light to detect variations in hemoglobin oxygen levels in your blood. Since oxygen is critical for your brain to function properly, NIRS can assist doctors in any clinical setting where brain oxygen levels may fluctuate.
NIRS is used to monitor:
brain oxygen levels during cardiac surgery
brain function and oxygenation levels in preterm infants in a neonatal intensive care unit (NICU) setting

## Slide 15: 8. NIRS

## Slide 16: MRI of the brain

## Slide 17: Indications for MRI brain
•
•
•
•
•
•
•
•
•
•
•
•
•
•
Transient ischaemic atta(TIA), cerebrovascular attack (CVA) Infection, inflammation, meningitisck, encephalitis, HIV, AIDS, TB Cognitive decline, neurodegenerative disorders, dementia Demyelinating disease, multiple sclerosis
Loss of consciousness, seizures, epilepsy
Brain tumour, metastases, abscess
Cerebellar lesion, brainstem lesion Congenital abnormalities
Post-operative follow-up
Vascular pathologies Headaches Haemorrhage Trauma
Ataxia

## Slide 18
Contraindications
•
•
•
•
•
•
Any electrically, magnetically or mechanically activated implant (e.g. cardiac pacemaker, insulin pump biostimulator, neurostimulator, cochlear implant, and
hearing aids)
Intracranial aneurysm clips (unless made of titanium)
Pregnancy (risk vs benefit ratio to be assessed) Ferromagnetic surgical clips or staples Metallic foreign body in the eye
Metal shrapnel or bullet

## Slide 19: Patient preparation for MRI brain
Ask the patient to remove all metal objects including keys, coins, wallet, cards with magnetic strips, jewellery, hearing aid and hairpins
patients (e.g. relative or staff)
If possible provide a chaperone for claustrophobic
The exam must be explained to the patient before the scan
Before injecting Gadolinium make sure that the patient has normal kidney function tests (Blood urea and serum
creatinine levels) (normal GFR)

## Slide 20: Positioning for MRI brain
•
•
•
•
Head first supine
Position the head in the head coil and immobilise with cushions Give cushions under the legs for extra comfort
Centre the laser beam localiser over the glabella

## Slide 21: Suggested protocols, parameters and planning
Localiser
A three plane localizer must be taken in the beginning to localise and plan the sequences. Localizers are usually less than 25sec.
T1 weighted low resolution scans.

## Slide 22: T1 SE coronal
Plan the coronal slices on the sagittal plane; angle the position block perpendicular to the corpus callosum. Check the positioning block in the other two planes. An appropriate angle must be given in the axial plane on a tilted head (perpendicular to mid line of the brain). Slices must be sufficient to cover the whole brain from the frontal sinus to
the line of the occipital protuberance.

## Slide 23: T2 axial
Plan the axial slices on the sagittal plane; angle the position block parallel to the genu and splenium of the corpus callosum. Slices must be sufficient to cover the whole brain from the vertex to the line of the foramen magnum.
Check the positioning block in the other two planes. An appropriate angle must
be given in coronal plane on a tilted head (perpendicular to the line of 3rd
ventricle and brain stem).

## Slide 24: T2 sagittal Plan the sagittal slices on the axial plane; angle the position block parallel to midline of the brain. Check the positioning block in the other two planes. An appropriate angle must be given in the coronal plane on a tilted head (parallel to the line along 3rd ventricle and brain stem). Slices must be sufficient to cover the
brain from temporal lobe to temporal lobe.

## Slide 25: T2 FLAIR axial
Plan the axial slices on the sagittal plane; angle the position block parallel to the genu and splenium of the corpus callosum. Slices must be sufficient to cover the whole brain from the vertex to the line of the foramen magnum. Check the positioning block in the other two planes.
An appropriate angle must be given in coronal plane on a tilted head
(perpendicular to the line of 3rd ventricle and brain stem).

## Slide 26: DWI axial
Plan the DWI axial slices on the sagittal plane; angle the position block parallel to the line from the glabella to the foramen magnum. This angle will reduce air-bone interface artefacts from the Para nasal sinuses. Slices must be sufficient to cover the whole brain from the vertex to the foramen magnum. Check the positioning block in the other two planes. An appropriate angle must be given in the coronal plane on a tilted head (perpendicular to the line of 3rd
ventricle and brain stem).

## Slide 27: Indications for contrast enhancement brain scans
Tumour, Metastases, Cranial nerve lesion, Indeterminate intracranial lesion, IAC mass
Meningitis, Encephalitis, Leptomeningeal spread
•
•
Multiple Sclerosis, AVM, HIV, Infection Abscess Leukodystrophies, Delayed development
•
Syringomyelia(Syrinx)
Use T1 SE axial and coronal after the administration of IV gadolinium DTPA injection(copy the planning outlined above). The recommended dose of gadolinium DTPA injection is 0.1 mmol/kg,
i.e. 0.2 mL/kg in adults, children and infants.

## Slide 29: TR & TE
TE ( echo time) : Time interval in which signals are measured after RF excitation.
TR (repetition time) : The time between two excitations is called repetition time.
By varying the TR and TE one can obtain T1WI and T2WI.
In general a short TR (<1000ms) and short TE (<45ms) scan is T1WI.
Long TR (>2000ms) and long TE (>45ms) scan is T2WI.

## Slide 30: T1 W Images
Short TE
Short TR
Better anatomical details
Fluids are dark
Gray matter is gray
White matter is white
Most Pathologies dark on T1
Bright On T1
Fat
Hemorrhage
Melanin
Early Calcification
Protein contents (Colloid cyst/ Rathke cyst)
Posterior pituitary appears Bright on T1
Gadolinium .

## Slide 31: T1 W Images

## Slide 32: T2 W Images
Long TE
Long TR
Better pathological details
Fluids are bright
Gray matter is relatively bright
White matter is dark

## Slide 33: T1 & T2 W Images

## Slide 34: T2 Flair – Fluid Attenuated Inversion Recovery Sequences
Long TE
Long TR
Similar to T2 Except free water suppression ( Inversion Recovery)
Most pathology is Bright
Especially good for lesions near ventricles or sulci (eg. Multiple sclerosis)

## Slide 35
 | T1W | T2W | Flair(T2)
TR | Short | Long | Long
TR | Short | Long | Long
CSF | Low | High | Low
Fat | High | Low | Medium
Brain | Low | High | High
Edema | Low | High | High