## Slide 1: INVERSE LAPLACE TRANSFORM

## Slide 2: Definition
Transforms -- a mathematical conversion from one way of thinking to another to make a problem easier to solve
transform
solution
in transform
way of
thinking
inverse
transform
solution in original way of thinking
problem in original way of thinking
2. Transforms

## Slide 3: Laplace transformation
linear
differential
equation
time
domain
solution
Laplace
transformed
equation
Laplace
solution
time domain
Laplace domain or
complex frequency domain
algebra
Laplace transform
inverse Laplace
transform
4. Laplace transforms

## Slide 4: Basic Tool For Continuous Time: Laplace Transform
Convert time-domain functions and operations into frequency-domain
  f(t) ® F(s) (tR, sC)
  Linear differential equations (LDE) ® algebraic expression in Complex plane
Graphical solution for key LDE characteristics
Discrete systems use the analogous z-transform
Notes: Jlh: First red bullet needs to be fixed?

## Slide 5: The Complex Plane (review)
Imaginary axis (j)
Real axis
(complex) conjugate

## Slide 6: Laplace Transforms of Common Functions
Name
f(t)
F(s)
Impulse
Step
Ramp
Exponential
Sine
1
Notes: Jlh: function for impulse needs to be fixed

## Slide 7: Laplace Transform Properties

## Slide 8: Transforms (5 of 11)
Most mathematical handbooks have tables of Laplace transforms
4. Laplace transforms

## Slide 9: LAPLACE TRANSFORMS
PARTIAL FRACTION EXPANSION

## Slide 10: Definition
Definition -- Partial fractions are several fractions whose sum equals a given fraction
Purpose -- Working with transforms requires breaking complex fractions into simpler fractions to allow use of tables of transforms

## Slide 11: Partial Fraction Expansions
Expand into a term for each factor in the denominator.
Recombine RHS
Equate terms in s and constant terms. Solve.
Each term is in a form so that inverse Laplace transforms can be applied.

## Slide 12: Example of Solution of an ODE
ODE w/initial conditions
Apply Laplace transform to each term
Solve for Y(s)
Apply partial fraction expansion
Apply inverse Laplace transform to each term

## Slide 13: Different terms of 1st degree
To separate a fraction into partial fractions when its denominator can be divided into different terms of first degree, assume an unknown numerator for each fraction
Example --
  (11x-1)/(X2 - 1) = A/(x+1) + B/(x-1)
  = [A(x-1) +B(x+1)]/[(x+1)(x-1))]
  A+B=11
  -A+B=-1
  A=6, B=5

## Slide 14: Repeated terms of 1st degree (1 of 2)
When the factors of the denominator are of the first degree but some are repeated, assume unknown numerators for each factor
  If a term is present twice, make the fractions the corresponding term and its second power
  If a term is present three times, make the fractions the term and its second and third powers
3. Partial fractions

## Slide 15: Repeated terms of 1st degree (2 of 2)
Example --
  (x2+3x+4)/(x+1)3= A/(x+1) + B/(x+1)2 + C/(x+1)3
  x2+3x+4 = A(x+1)2 + B(x+1) + C
  = Ax2 + (2A+B)x + (A+B+C)
  A=1
  2A+B = 3
  A+B+C = 4
  A=1, B=1, C=2
3. Partial fractions

## Slide 16: Different quadratic terms
When there is a quadratic term, assume a numerator of the form Ax + B
Example --
  1/[(x+1) (x2 + x + 2)] = A/(x+1) + (Bx +C)/ (x2 + x + 2)
  1 = A (x2 + x + 2) + Bx(x+1) + C(x+1)
  1 = (A+B) x2 + (A+B+C)x +(2A+C)
  A+B=0
  A+B+C=0
  2A+C=1
  A=0.5, B=-0.5, C=0
3. Partial fractions

## Slide 17: Repeated quadratic terms
Example --
  1/[(x+1) (x2 + x + 2)2] = A/(x+1) + (Bx +C)/ (x2 + x + 2) + (Dx +E)/ (x2 + x + 2)2
  1 = A(x2 + x + 2)2 + Bx(x+1) (x2 + x + 2) + C(x+1) (x2 + x + 2) + Dx(x+1) + E(x+1)
  A+B=0
  2A+2B+C=0
  5A+3B+2C+D=0
  4A+2B+3C+D+E=0
  4A+2C+E=1
  A=0.25, B=-0.25, C=0, D=-0.5, E=0
3. Partial fractions

## Slide 18: Apply Initial- and Final-Value Theorems to this Example
Laplace transform of the function.
Apply final-value theorem
Apply initial-value theorem

## Slide 19: LAPLACE TRANSFORMS
SOLUTION PROCESS

## Slide 20: Solution process (1 of 8)
Any nonhomogeneous linear differential equation with constant coefficients can be solved with the following procedure, which reduces the solution to algebra
4. Laplace transforms

## Slide 21: Solution process (2 of 8)
Step 1: Put differential equation into standard form
  D2 y + 2D y + 2y = cos t
  y(0) = 1
  D y(0) = 0

## Slide 22: Solution process (3 of 8)
Step 2: Take the Laplace transform of both sides
  L{D2 y} + L{2D y} + L{2y} = L{cos t}

## Slide 23: Solution process (4 of 8)
Step 3: Use table of transforms to express equation in s-domain
  L{D2 y} + L{2D y} + L{2y} = L{cos  t}
  L{D2 y} = s2 Y(s) - sy(0) - D y(0)
  L{2D y} = 2[ s Y(s) - y(0)]
  L{2y} = 2 Y(s)
  L{cos t} = s/(s2 + 1)
  s2 Y(s) - s + 2s Y(s) - 2 + 2 Y(s) = s /(s2 + 1)

## Slide 24: Solution process (5 of 8)
Step 4: Solve for Y(s)
  s2 Y(s) - s + 2s Y(s) - 2 + 2 Y(s) = s/(s2 + 1)
  (s2 + 2s + 2) Y(s) = s/(s2 + 1) + s + 2
  Y(s) = [s/(s2 + 1) + s + 2]/ (s2 + 2s + 2)
  = (s3 + 2 s2 + 2s + 2)/[(s2 + 1) (s2 + 2s + 2)]

## Slide 25: Solution process (6 of 8)
Step 5: Expand equation into format covered by table
  Y(s) = (s3 + 2 s2 + 2s + 2)/[(s2 + 1) (s2 + 2s + 2)]
  = (As + B)/ (s2 + 1) + (Cs + E)/ (s2 + 2s + 2)
  (A+C)s3 + (2A + B + E) s2 + (2A + 2B + C)s + (2B +E)
  1 = A + C
  2 = 2A + B + E
  2 = 2A + 2B + C
  2 = 2B + E
  A = 0.2, B = 0.4, C = 0.8, E = 1.2

## Slide 26: Solution process (7 of 8)
  (0.2s + 0.4)/ (s2 + 1)
  = 0.2 s/ (s2 + 1) + 0.4 / (s2 + 1)
  (0.8s + 1.2)/ (s2 + 2s + 2)
  = 0.8 (s+1)/[(s+1)2 + 1] + 0.4/ [(s+1)2 + 1]

## Slide 27: Solution process (8 of 8)
Step 6: Use table to convert s-domain to time domain
  0.2 s/ (s2 + 1) becomes 0.2 cos t
  0.4 / (s2 + 1) becomes 0.4 sin t
  0.8 (s+1)/[(s+1)2 + 1] becomes 0.8 e-t cos t
  0.4/ [(s+1)2 + 1] becomes 0.4 e-t sin t
  y(t) = 0.2 cos t + 0.4 sin t + 0.8 e-t cos t + 0.4 e-t sin t

## Slide 28: LAPLACE TRANSFORMS
TRANSFER FUNCTIONS

## Slide 29: Introduction
Definition -- a transfer function is an expression that relates the output to the input in the s-domain
differential
equation
r(t)
y(t)
transfer
function
r(s)
y(s)
5. Transfer functions

## Slide 30: Transfer Function
Definition
  H(s) = Y(s) / X(s)
Relates the output of a linear system (or component) to its input
Describes how a linear system responds to an impulse
All linear operations allowed
  Scaling, addition, multiplication
H(s)
X(s)
Y(s)

## Slide 31: Block Diagrams
Pictorially expresses flows and relationships between elements in system
Blocks may recursively be systems
Rules
  Cascaded (non-loading) elements: convolution
  Summation and difference elements
Can simplify

## Slide 32: Typical block diagram
control
Gc(s)
plant
Gp(s)
feedback
H(s)
pre-filter
G1(s)
post-filter
G2(s)
reference input, R(s)
error, E(s)
plant inputs, U(s)
output, Y(s)
feedback, H(s)Y(s)
5. Transfer functions

## Slide 33: Example
v(t)
R
C
L
v(t) = R I(t) + 1/C I(t) dt + L di(t)/dt
V(s) = [R I(s) + 1/(C s) I(s) + s L I(s)]
Note: Ignore initial conditions
5. Transfer functions

## Slide 34: Block diagram and transfer function
V(s)
  = (R + 1/(C s) + s L ) I(s)
  = (C L s2 + C R s + 1 )/(C s) I(s)
I(s)/V(s) = C s / (C L s2 + C R s + 1 )
C s / (C L s2 + C R s + 1 )
V(s)
I(s)
5. Transfer functions

## Slide 35: Block diagram reduction rules
G1
G2
G1 G2
U
Y
U
Y
G1
G2
U
Y
+
+
G1 + G2
U
Y
G1
G2
U
Y
+
-
G1 /(1+G1 G2)
U
Y
Series
Parallel
Feedback
5. Transfer functions

## Slide 36: Rational Laplace Transforms
Notes: Jlh: Need to give insights into why poles and zeroes are important. Otherwise, the audience will be overwhelmed.

## Slide 37: First Order System
Reference
S
1
Notes: Examples of transducers in computer systems are mainly surrogate variables. For example, we may not be able to measure end-user response times. However, we can measure internal system queueing. So we use the latter as a surrogate for the former and sometimes use simple equations (e.g., Little’s result) to convert between the two.
Use the approximation to simplify the following analysis
Another aspect of the transducer are the delays it introduces. Typically, measurements are sampled. The sample rate cannot be too fast if the performance of the plant (e.g., database server) is

## Slide 38: First Order System
Impulse response |  | Exponential
Step response |  | Step, exponential
Ramp response |  | Ramp, step, exponential
No oscillations (as seen by poles)
Notes: Jlh: Haven’t explained the relationship between poles and oscillations

## Slide 39: Second Order System
Notes: Get oscillatory response if have poles that have non-zero Im values.

## Slide 40: Second Order System: Parameters
Notes: Get oscillatory response if have poles that have non-zero Im values.

## Slide 41: Transient Response Characteristics

## Slide 42: Transient Response
Estimates the shape of the curve based on the foregoing points on the x and y axis
Typically applied to the following inputs
  Impulse
  Step
  Ramp
  Quadratic (Parabola)

## Slide 43: Effect of pole locations
Faster Decay
Faster Blowup
Oscillations
(higher-freq)
Im(s)
Re(s)
(e-at)
(eat)

## Slide 44: Basic Control Actions: u(t)
Notes: Jlh: Can we give more intuition on control actions. This seems real brief considering its importance.

## Slide 45: Effect of Control Actions
Proportional Action
  Adjustable gain (amplifier)
Integral Action
  Eliminates bias (steady-state error)
  Can cause oscillations
Derivative Action (“rate control”)
  Effective in transient periods
  Provides faster response (higher sensitivity)
  Never used alone

## Slide 46: Basic Controllers
Proportional control is often used by itself
Integral and differential control are typically used in combination with at least proportional control
  eg, Proportional Integral (PI) controller:

## Slide 47: Summary of Basic Control
Proportional control
  Multiply e(t) by a constant
PI control
  Multiply e(t) and its integral by separate constants
  Avoids bias for step
PD control
  Multiply e(t) and its derivative by separate constants
  Adjust more rapidly to changes
PID control
  Multiply e(t), its derivative and its integral by separate constants
  Reduce bias and react quickly

## Slide 48: Root-locus Analysis
Based on characteristic eqn of closed-loop transfer function
Plot location of roots of this eqn
  Same as poles of closed-loop transfer function
  Parameter (gain) varied from 0 to 
Multiple parameters are ok
  Vary one-by-one
  Plot a root “contour” (usually for 2-3 params)
Quickly get approximate results
  Range of parameters that gives desired response

## Slide 49: LAPLACE TRANSFORMS
LAPLACE APPLICATIONS

## Slide 50: Initial value
In the initial value of f(t) as t approaches 0 is given by
f(0 ) = Lim s F(s)
s

f(t) = e -t
F(s) = 1/(s+1)
f(0 ) = Lim s /(s+1) = 1
s

Example
6. Laplace applications

## Slide 51: Final value
In the final value of f(t) as t approaches  is given by
f(0 ) = Lim s F(s)
s
0
f(t) = e -t
F(s) = 1/(s+1)
f(0 ) = Lim s /(s+1) = 0
s
0
Example
6. Laplace applications

## Slide 52: Apply Initial- and Final-Value Theorems to this Example
Laplace transform of the function.
Apply final-value theorem
Apply initial-value theorem

## Slide 53: Poles
The poles of a Laplace function are the values of s that make the Laplace function evaluate to infinity. They are therefore the roots of the denominator polynomial
10 (s + 2)/[(s + 1)(s + 3)] has a pole at s = -1 and a pole at s = -3
Complex poles always appear in complex-conjugate pairs
The transient response of system is determined by the location of poles
6. Laplace applications

## Slide 54: Zeros
The zeros of a Laplace function are the values of s that make the Laplace function evaluate to zero. They are therefore the zeros of the numerator polynomial
10 (s + 2)/[(s + 1)(s + 3)] has a zero at s = -2
Complex zeros always appear in complex-conjugate pairs
6. Laplace applications

## Slide 55: Stability
A system is stable if bounded inputs produce bounded outputs
The complex s-plane is divided into two regions: the stable region, which is the left half of the plane, and the unstable region, which is the right half of the s-plane
s-plane
stable
unstable
x
x
x
x
x
x
x
j


## Slide 56: LAPLACE TRANSFORMS
FREQUENCY RESPONSE

## Slide 57: Introduction
Many problems can be thought of in the time domain, and solutions can be developed accordingly.
Other problems are more easily thought of in the frequency domain.
A technique for thinking in the frequency domain is to express the system in terms of a frequency response
7. Frequency response

## Slide 58: Definition
The response of the system to a sinusoidal signal. The output of the system at each frequency is the result of driving the system with a sinusoid of unit amplitude at that frequency.
The frequency response has both amplitude and phase
7. Frequency response

## Slide 59: Process
The frequency response is computed by replacing s with j  in the transfer function
f(t) = e -t
F(s) = 1/(s+1)
Example
F(j ) = 1/(j  +1)
Magnitude = 1/SQRT(1 + 2)
Magnitude in dB = 20 log10 (magnitude)
Phase = argument = ATAN2(- , 1)
magnitude in dB

7. Frequency response

## Slide 60: Graphical methods
Frequency response is a graphical method
Polar plot -- difficult to construct
Corner plot -- easy to construct
7. Frequency response

## Slide 61: Constant K
+180o
+90o
0o
-270o
-180o
-90o
60 dB
40 dB
20 dB
0 dB
-20 dB
-40 dB
-60 dB
magnitude
phase
0.1 1 10 100
, radians/sec
20 log10 K
arg K
7. Frequency response

## Slide 62: Simple pole or zero at origin, 1/ (j)n
+180o
+90o
0o
-270o
-180o
-90o
60 dB
40 dB
20 dB
0 dB
-20 dB
-40 dB
-60 dB
magnitude
phase
0.1 1 10 100
, radians/sec
1/ 
1/ 2
1/ 3
1/ 
1/ 2
1/ 3
G(s) = n2/(s2 + 2 ns +  n2)

## Slide 63: Simple pole or zero, 1/(1+j)
+180o
+90o
0o
-270o
-180o
-90o
60 dB
40 dB
20 dB
0 dB
-20 dB
-40 dB
-60 dB
magnitude
phase
0.1 1 10 100
T
7. Frequency response

## Slide 64: Error in asymptotic approximation
T
0.01
0.1
0.5
0.76
1.0
1.31
1.73
2.0
5.0
10.0
dB
0
0.043
1
2
3
4.3
6.0
7.0
14.2
20.3
arg (deg)
0.5
5.7
26.6
37.4
45.0
52.7
60.0
63.4
78.7
84.3
7. Frequency response

## Slide 65: Quadratic pole or zero
+180o
+90o
0o
-270o
-180o
-90o
60 dB
40 dB
20 dB
0 dB
-20 dB
-40 dB
-60 dB
magnitude
phase
0.1 1 10 100
T
7. Frequency response

## Slide 66: Transfer Functions
Defined as G(s) = Y(s)/U(s)
Represents a normalized model of a process, i.e., can be used with any input.
Y(s) and U(s) are both written in deviation variable form.
The form of the transfer function indicates the dynamic behavior of the process.

## Slide 67: Derivation of a Transfer Function
Dynamic model of CST thermal mixer
Apply deviation variables
Equation in terms of deviation variables.

## Slide 68: Derivation of a Transfer Function
Apply Laplace transform to each term considering that only inlet and outlet temperatures change.
Determine the transfer function for the effect of inlet temperature changes on the outlet temperature.
Note that the response is first order.

## Slide 69: Poles of the Transfer Function Indicate the Dynamic Response
For a, b, c, and d positive constants, transfer function indicates exponential decay, oscillatory response, and exponential growth, respectively.

## Slide 70: Poles on a Complex Plane

## Slide 71: Exponential Decay

## Slide 72: Damped Sinusoidal

## Slide 73: Exponentially Growing Sinusoidal Behavior (Unstable)

## Slide 74: What Kind of Dynamic Behavior?

## Slide 75: Unstable Behavior
If the output of a process grows without bound for a bounded input, the process is referred to a unstable.
If the real portion of any pole of a transfer function is positive, the process corresponding to the transfer function is unstable.
If any pole is located in the right half plane, the process is unstable.