## Slide 1
Dimensioning

## Slide 2: TOPICS
Introduction
Dimensioning components
Dimensioning object’ s features
Placement of dimensions.

## Slide 3: Introduction

## Slide 4
Shape
Multiview
Drawing
Dimensioning
Design
a part
1. Size, Location
ENGINEERING DESIGN
2. Non-graphic information
TRANSFERRED
INFORMATION
Create
drawings
Manufacture
RESULT
Sketches
of ideas
PROCESS

## Slide 5: DEFINITION
Dimensioning is the process of specifying part’ s
information by using of figures, symbols and notes.
This information are such as:
1. Sizes and locations of features
2. Material’s type
3. Number required
4. Kind of surface finish
5. Manufacturing process
6. Size and geometric tolerances
This course

## Slide 6: DIMENSIONING SYSTEM
1. Metric system : ISO and JIS standards
2. Decimal-inch system
3. Fractional-inch system
,
0.25 (not .25), 5.375 etc.
Examples
Examples
32, 32.5, 32.55, 0.5 (not .5) etc.
Examples
etc.
This
course

## Slide 7
Dimensioning Components

## Slide 8
DIMENSIONING COMPONENTS
Extension lines
Dimension lines (with arrowheads)
Leader lines
Dimension figures
Notes : - local note
- general note
Drawn with
4H pencil
Lettered with
2H pencil.

## Slide 9
indicate the location on the object’s features that are dimensioned.
EXTENSION LINES

## Slide 10
DIMENSION LINES
indicate the direction and extent of a dimension, and inscribe dimension figures.
10
27
43
13
123o

## Slide 11
indicate details of the feature with a local note.
LEADER LINES
10
27
43
13
123o
10 Drill, 2 Holes
R16

## Slide 12
Recommended Practices

## Slide 13
EXTENSION LINES
Leave a visible gap (≈ 1 mm) from a view and start drawing an extension line.
Extend the lines beyond the (last) dimension line 1-2 mm.
Visible gap
COMMON MISTAKE

## Slide 14
Do not break the lines as they cross object lines.
COMMON MISTAKE
Continuous
EXTENSION LINES

## Slide 15
Dimension lines should not be spaced too close to each other and to the view.
11
34
Leave a space at least
2 times of a letter height.
16
35
DIMENSION LINES
Leave a space at least
1 time of a letter height.

## Slide 16
DIMENSION FIGURES
The height of figures is suggested to be 2.5~3 mm.
Place the numbers at about 1 mm above dimension line and between extension lines.
COMMON MISTAKE
11
11
34
34

## Slide 17
16.25
16.25
or
DIMENSION FIGURES
When there is not enough space for figure or
arrows, put it outside either of the extension lines.
1
Not enough space
for figures
Not enough space
for arrows
1
1

## Slide 18
The JIS and ISO standards adopt the unit of
Angular dimension in degree with a symbol “o”
place behind the figures (and if necessary
minutes and seconds may be used together).
DIMENSION FIGURES : UNITS
Length dimension in millimeters without
specifying a unit symbol “mm”.

## Slide 19
1. Aligned method
2. Unidirectional method
The dimension figures are placed so that they are readable from the bottom and right side of the drawing.
The dimension figures are placed so that they can be read from the bottom of the drawing.
Do not use both system on the same drawing or on the same series of drawing (JIS Z8317)
DIMENSION FIGURES : ORIENTATION

## Slide 20
30
30
30
30
30
30
30
30
EXAMPLE : Dimension of length using aligned method.

## Slide 21
30
30
30
30
30
30
30
30
EXAMPLE : Dimension of length using unidirectional method.

## Slide 22
45o
45o
45o
45o
45o
45o
45o
45o
EXAMPLE : Dimension of angle using aligned method.

## Slide 23
45o
45o
45o
45o
45o
45o
45o
45o
EXAMPLE : Dimension of angle using unidirectional method.

## Slide 24
LOCAL NOTES
Place the notes near to the feature which they
apply, and should be placed outside the view.
Always read horizontally.
10 Drill
COMMON MISTAKE
10 Drill
≈ 10mm
10 Drill
Too far

## Slide 25
Dimensioning Practices

## Slide 26
THE BASIC CONCEPT
Dimensioning is accomplished by adding size and location information necessary to manufacture
the object.
Clear
Complete
Facilitate the
- manufacturing method
measurement method
This information have to be

## Slide 27
L
L
S
S
S
Designed
part
EXAMPLE
To manufacture this part
we need to know…
1. Width, depth and
thickness of the part.
2. Diameter and depth
of the hole.
3. Location of the holes.
“S” denotes size dimension.
“L” denotes location dimension.
S
L
L

## Slide 28: ANGLE
To dimension an angle use circular dimension
line having the center at the vertex of the angle.
COMMON MISTAKE

## Slide 29
ARC
Arcs are dimensioned by giving the radius, in the
views in which their true shapes appear.
R 200
The letter “R” is always lettered before the figures
to emphasize that this dimension is radius of an
arc.
R 200
or

## Slide 30
ARC
The dimension figure and the arrowhead should
be inside the arc, where there is sufficient space.
R 200
R 62.5
Move figure outside
R 6.5
Move both figure
and arrow outside
Sufficient space
for both.
Sufficient space
for arrowhead only.
R 58.5
Insufficient space
for both.

## Slide 31
ARC
Leader line must be radial and inclined with
an angle between 30 ~ 60 degs to the horizontal.
COMMON MISTAKE
R62.5
R62.5
R62.5
R62.5
R62.5
30o
60o
R62.5

## Slide 32
ARC
Use the foreshortened radial dimension line,
when arc’ s center locates outside the sheet or
interfere with other views.
Drawing sheet
Method 1
Method 2

## Slide 33
FILLETS AND ROUNDS
Give the radius of a typical fillet only by using a
local note.
R6.5
If all fillets and rounds are uniform in size,
dimension may be omitted, but it is necessary to
add the note “ All fillets and round are Rxx. ”
NOTE:
All fillets and round are R6.5
Drawing sheet
R12
unless otherwise specified.
NOTE:
All fillets and round are R6.5

## Slide 34
The curve constructed from two or more arcs,
requires the dimensions of radii and center’s
location.
CURVE
COMMON MISTAKE
Tangent point

## Slide 35
CYLINDER
Size dimensions are diameter and length.
Measurement
method
Location dimension must be located from its
center lines and should be given in circular view.

## Slide 36
 100
 70
CYLINDER
Diameter should be given in a longitudinal view with the symbol “ ” placed before the figures.

## Slide 37
HOLES
Size dimensions are diameter and depth.
Location dimension must be located from its
center lines and should be given in circular view.
Measurement
method

## Slide 38
f xx
Use leader line and local note to specify diameter and hole’s depth in the circular view.
HOLES : SMALL SIZE
xx Drill, Thru.
1) Through thickness hole
f xx Thru.
or
xx Drill.
or
or

## Slide 39
f xx, yy Deep
HOLES : SMALL SIZE
or
xx Drill, yy Deep
Hole’s
depth
Use leader line and local note to specify diameter and hole’s depth in the circular view.
2) Blind hole

## Slide 40
f xx
Use extension and dimension lines
Use diametral dimension line
Use leader line and note
HOLES : LARGE SIZE

## Slide 41
COMMON MISTAKE
f xx
f xx
f xx
Rxx
f xx
HOLES
f xx

## Slide 42
CHAMFER
Use leader line and note to indicate linear
distance and angle of the chamfer.
S
q
S q
For a 45o chamfer
S S
CS
or

## Slide 43
ROUNDED-END SHAPES
R12
f 12
21
5
Dimensioned according to the manufacturing
method used.
Center to Center Distance

## Slide 44
ROUNDED-END SHAPES
R12
21
5
12
Dimensioned according to the manufacturing
method used.
Center to Center Distance

## Slide 45
ROUNDED-END SHAPES
Dimensioned according to the manufacturing
method used.
R12
21
12
16

## Slide 46
ROUNDED-END SHAPES
R12
27
12
Dimensioned according to the manufacturing
method used.
Tool cutting distance

## Slide 47
ROUNDED-END SHAPES
Dimensioned according to the standard sizes of
another part to be assembled or manufacturing
method used.
25
Key
(standard part)

## Slide 48
ROUNDED-END SHAPES
Dimensioned according to the standard sizes of
another part to be assembled or manufacturing
method used.
20

## Slide 49
Placement of Dimensions

## Slide 50
Extension lines, leader lines should not cross dimension lines.
POOR
GOOD
RECOMMENDED PRACTICE

## Slide 51
2. Extension lines should be drawn from the nearest points to be dimensioned.
POOR
GOOD
RECOMMENDED PRACTICE

## Slide 52
3. Extension lines of internal feature can cross visible lines without leaving a gap at the intersection point.
WRONG
CORRECT
RECOMMENDED PRACTICE

## Slide 53
4. Do not use object line, center line, and dimension line as an extension lines.
POOR
GOOD
RECOMMENDED PRACTICE

## Slide 54
POOR
GOOD
5. Avoid dimensioning hidden lines.
RECOMMENDED PRACTICE

## Slide 55
POOR
GOOD
6. Place dimensions outside the view, unless placing them inside improve the clarity.
RECOMMENDED PRACTICE

## Slide 56
JUST OK !!!
BETTER
RECOMMENDED PRACTICE
6. Place dimensions outside the view, unless placing them inside improve the clarity.

## Slide 57
7. Apply the dimension to the view that clearly show the shape or features of an object.
POOR
GOOD
RECOMMENDED PRACTICE

## Slide 58
8. Dimension lines should be lined up and grouped together as much as possible.
POOR
GOOD
RECOMMENDED PRACTICE

## Slide 59
9. Do not repeat a dimension.
POOR
GOOD
RECOMMENDED PRACTICE