## Slide 1: الرسـم الهندسـي Engineering Drawing

## Slide 2: مـقـدمـة Introduction
الرسم الهندسي هو احد انواع الرسم التقني، يستخدم لتعريف الاجزاء الهندسية بشكل كامل وواضح، وعادة ينفذ وفق مواصفات متفق عليها بالنسبة للمخططات، التسميات، التفسير، الحجم الظاهر،.....الخ.
هدفه هو اظهار الخاصية الهندسية للمنتج او الاجزاء بشكل واضح ودقيق.
الهدف الاخير للرسم الهندسي هو نقل كل المعلومات المطلوبة التي تسمح للمصنع من تقديم هذه الاجزاء.

## Slide 3: الهدف من الرسم الهندسي Purpose of an Engineering Drawing
الرسم الهندسي هو ليس تصوير.
هو اعطاء مواصفات الحجم والشكل للجزء او الاجزاء المجمعة.
المعلومات المهمة في الرسم هي الابعاد والسماحات لجميع خواص الرسم.

## Slide 4
عناصـر الرســـم الهندســــي
Elements of Engineering Drawing
الرسم الهندسي يتكون من لغة الرسم ولغة الكتابة
لغة
الرسم
توصف الشكل
لغة
الكتابة
توصف الحجم، الموقع وخواص الجسم

## Slide 5
المفاهيم الاسـاسـية للرســـم
Basic Knowledge for Drafting
لغــة
الرســم
لغــة
الكتابــة
انواع
الخطوط
البنية
الانشائية
الكتابة
طرق
الاسقاط

## Slide 6: Traditional Drawing Tools

## Slide 7: Instruments
Drawing board/table.
Drawing sheet/paper.
Drafting tape.
Pencils.
Eraser.
Sharpener.
T-square.
Set-squares/triangles.
Scales.
Compass and divider.

## Slide 8: Drawing board

## Slide 9: Drawing table

## Slide 10: Drawing sheet/paper
216 X 280 mm
280 X 382 mm
382 X 560 mm
585 X 726 mm

## Slide 11: Drafting tape

## Slide 12: Pencils
Wood pencils: H, 2H, 3H, 4H, 5H, 6H, 7H, 8H, 9H, B, HB, 2B, 3B, 4B, 5B, 6B.
Semiautomatic Pencils (lead holder) are more convenient then ordinary wood pencils.

## Slide 13: Eraser

## Slide 14: Erasing Shield

## Slide 15: Sharpener

## Slide 16: T-square

## Slide 20: Set-squares/triangles

## Slide 22: Circle Template

## Slide 23: Scales

## Slide 24: Compass and divider

## Slide 25: Sandpaper

## Slide 26: Tissue paper

## Slide 27: Clean paper

## Slide 28: Drawing Standard

## Slide 29: Introduction
Standards are set of rules that govern how technical drawings are represented.
Drawing standards are used so that drawings convey
the same meaning to everyone who reads them.

## Slide 30
ISO
International Standards Organization
Standard Code
ANSI
American National Standard Institute
USA
JIS
Japanese Industrial Standard
Japan
BS
British Standard
UK
AS
Australian Standard
Australia
Deutsches Institut für Normung
DIN
Germany
Country
Code
Full name
มอก.
สำนักงานมาตรฐานผลิตภัณฑ์อุตสาหกรรม
Thailand

## Slide 31
Partial List of Drawing Standards
JIS Z 8311 Sizes and Format of Drawings
JIS Z 8312 Line Conventions
JIS Z 8313 Lettering
JIS Z 8314 Scales
JIS Z 8315 Projection methods
JIS Z 8316 Presentation of Views and Sections
JIS Z 8317 Dimensioning
Code number
Contents

## Slide 32: Drawing Sheet
Trimmed paper of
a size A0 ~ A4.
Standard sheet size (JIS)
A4 210 x 297
A3 297 x 420
A2 420 x 594
A1 594 x 841
A0 841 x 1189
A4
A3
A2
A1
A0
(Dimensions in millimeters)

## Slide 33
Drawing space
Drawing
space
Title block
d
d
c
c
c
Border
lines
1. Type X (A0~A4)
2. Type Y (A4 only)
Orientation of drawing sheet
Title block
Sheet size c (min) d (min)
A4 10 25
A3 10 25
A2 10 25
A1 20 25
A0 20 25

## Slide 34
216 X 280 mm
280 X 382 mm
382 X 560 mm
585 X 726 mm

## Slide 35
الاسم: الجامعة: رقم اللوحة:
المرحلة : الكلية: مقياس الرسم:
المجموعة : االقسم : التاريخ:
Title Block of drawing sheet

## Slide 36
Drawing Scales
Scale is the ratio of the linear dimension of an element
of an object shown in the drawing to the real linear
dimension of the same element of the object.
Size in drawing
Actual size
Length, size
:

## Slide 37
Drawing Scales
Designation of a scale consists of the word “SCALE”
followed by the indication of its ratio, as follow
SCALE 1:1 for full size
SCALE X:1 for enlargement scales (X > 1)
SCALE 1:X for reduction scales (X > 1)
Dimension numbers shown in the drawing are correspond
to “true size” of the object and they are independent of
the scale used in creating that drawing.

## Slide 38
Basic Line Types
Types of Lines
Appearance
Name according
to application
Continuous thick line HB
Visible line
Continuous thin line 2H
Dimension line
Extension line
Leader line
Dash thick line HB
Hidden line
Chain thin line 2H
Center line
NOTE : We will learn other types of line in later chapters.

## Slide 39
Visible lines represent features that can be seen in the
current view
Meaning of Lines
Hidden lines represent features that can not be seen in the current view
Center line represents symmetry, path of motion, centers of circles, axis of axisymmetrical parts
Dimension and Extension lines indicate the sizes and location of features on a drawing

## Slide 40: Types of Line

## Slide 41: Line Conventions
Visible Lines – solid thick lines that represent visible edges or contours
Hidden Lines – short evenly spaced dashes that depict hidden features
Section Lines – solid thin lines that indicate cut surfaces
Center Lines – alternating long and short dashes
Dimensioning
  Dimension Lines - solid thin lines showing dimension extent/direction
  Extension Lines - solid thin lines showing point or line to which dimension applies
  Leaders – direct notes, dimensions, symbols, part numbers, etc. to features on drawing
Cutting-Plane and Viewing-Plane Lines – indicate location of cutting planes for sectional views and the viewing position for removed partial views
Break Lines – indicate only portion of object is drawn. May be random “squiggled” line or thin dashes joined by zigzags.
Phantom Lines – long thin dashes separated by pairs of short dashes indicate alternate positions of moving parts, adjacent position of related parts and repeated detail
Chain Line – Lines or surfaces with special requirements

## Slide 42
1
2
3
4
5
6
7
8
9
10
14
13
12
11
Viewing-plane line
Extension line
Dimension Line
Center Line
Hidden Line
Break Line
Cutting-plane Line
Visible Line
Center Line (of motion)
Leader
VIEW B-B
SECTION A-A
Section Line
Phantom Line

## Slide 43
ABCDEFGHIJKLMNOPQRSTUVWXYZABCDEFGHIJKLMNOPQRSTUVWXYZABCD
ABCDEFGHIJKLMNOPQRSTUVWXYZABCDEFGHIJKLMNOPQRSTUVWXYZABCDEF
Lettering

## Slide 44: Text on Drawings
Text on engineering drawing is used :
To communicate nongraphic information.
As a substitute for graphic information, in those instance where text can communicate the needed information more clearly and quickly.
Uniformity
- size - line thickness
Legibility
- shape
- space between letters and words
Thus, it must be written with

## Slide 45: Lettering Standard
ANSI Standard
This course
Use a Gothic text style,
either inclined or vertical.
Use all capital letters.
Use 3 mm for most
text height.
Space between lines
of text is at least 1/3
of text height.
Use only a vertical Gothic
text style.
Use both capital and
lower-case letters.
Same. For letters in title block it is recommend to use 5~8 mm text height
N/A. Follows ANSI rule.

## Slide 46: Basic Strokes
Straight
Slanted
Curved
Horizontal
1
1
2
3
Examples : Application of basic stroke
“I” letter
“A” letter
1
2
3
4
5
6
“B” letter

## Slide 47
Suggested Strokes Sequence
Straight line
letters
Curved line
letters
Curved line
letters &
Numerals
Upper-case letters & Numerals

## Slide 48
The text’ s body height is about 2/3 the height of a capital letter.
Suggested Strokes Sequence
Lower-case letters

## Slide 49: Stroke Sequence
I
L
T
F
E
H

## Slide 50: Stroke Sequence
V
X
W

## Slide 51: Stroke Sequence
N
M
K
Z
Y
A
4

## Slide 52: Stroke Sequence
O
Q
C
G

## Slide 53: Stroke Sequence
D
U
P
B
R
J
1
2

## Slide 54: Stroke Sequence
5
7

## Slide 55: Stroke Sequence
6
8
9
0
S
3

## Slide 56
Stroke Sequence
l
i

## Slide 57
Stroke Sequence
v
w
x
k
z

## Slide 58
Stroke Sequence
j
y
f
r
t

## Slide 59
Stroke Sequence
c
o
a
b
d
p
q
e

## Slide 60
Stroke Sequence
g
n
m
h
u
s

## Slide 61
Word Composition
Look at the same word having different spacing between letters.
JIRAPONG
J
I
G
O
R
N
P
A
Which one is easier to read ?
A) Non-uniform spacing
B) Uniform spacing

## Slide 62
GOOD
Not uniform in style.
Not uniform in height.
Not uniformly vertical or inclined.
Not uniform in thickness of stroke.
Area between letters not uniform.
Area between words not uniform.
Example : Good and Poor Lettering

## Slide 63
Leave the space between words equal to the space requires for writing a letter “O”.
Example
Sentence Composition
ALL
DIMENSIONS
ARE
IN
MILLIMETERS
O
O
O
O
UNLESS
OTHERWISE
SPECIFIED.
O