## Slide 1
Non-invasive ventilation(NIV)
ICU L4
Dr.Zainab Al_youseif
M.B.Ch.B /FICMS.A&IC

## Slide 2: NIV
Non-invasive ventilation (NIV) refers to the administration of ventilatory support without using an invasive artificial airway (endotracheal tube or tracheostomy tube).
Non-invasive ventilation (NIV) augments spontaneous ventilation using the tight-fitting nasal or oronasal mask without endotracheal intubation. This can be used in a large number of conditions if there is no contraindication. The application of NIV should not delay clinically indicated endotracheal intubation.

## Slide 3: Advantages and disadvantages
the advantages of being readily taken on and off to facilitate weaning, maintaining some ability to communicate, and avoids the complications of sedation and ventilator-associated pneumonia.
The main disadvantages of NIV are no direct protection of the airway, no deep suctioning below the vocal cords, limited ability to apply high pressures and development of intolerance to the mask over time.

## Slide 4: NIV

## Slide 5: Interfaces
There are 6 types of interfaces that can be used during NIV therapy in the acute setting. Choosing the appropriate interface for patients with ARF involves consideration of patient preferences and tolerance, and determining the correct size and fit is essential to successful ventilation.
Although interfaces are constructed from a variety of materials, the most commonly used material is silicone, although gel masks are available from some manufacturers as well.

## Slide 6: Types of interfaces
Nasal mask: this mask covers the nose only and rests on the upper lip, the sides of the nose, and the nasal bridge (fig. A).
Oro-nasal mask (also referred to as a face mask): this mask covers the nose and mouth and rests on the chin, the sides of the nose and mouth, and the nasal bridge (fig. B).
Nasal pillow mask: this mask fits on the rim of the nostrils. This type of mask is usually recommended for individuals who find nasal or oro-nasal masks uncomfortable or experience skin breakdown on the nasal bridge. Nasal pillows are used mainly in stable patients with sleep-disordered breathing (fig. C).

## Slide 7: Types of interfaces
Oral mask: this mask fits inside the mouth between the teeth and lips and has a tongue guide to prevent the tongue from obstructing the airway passage. This type is not common in practice (fig. D).
Total face mask: this mask covers the whole face and is used mainly in patients with AHF (fig. E).
Helmet: the helmet is a transparent hood that covers the entire head and face of the patient and has a rubber collar neck seal. It is used as an alternative to the oro-nasal mask in patients with acute hypoxemic respiratory failure or acute cardiogenic pulmonary edema in certain countries. it was developed to improve tolerability and reduce complications in patients with ARF on NIV. it is not commonly used in patients with acute hypercapnic respiratory failure (fig. F).

## Slide 11: Nasal masks (general advantages)
Best suited for more cooperative patients
Better in patients with a lower severity of illness
Not claustrophobic
Allows speaking, drinking, coughing, and secretion clearance
Less aspiration risk with emesis
Generally better tolerated
Notes: Claustrophobia is a situational phobia triggered by an irrational and intense fear of tight or crowded spaces

## Slide 12: Nasal masks (cautions, disadvantages)
More leaks possible (eg, mouth breathing or lacking teeth patients)
Effectiveness limited in patients with nasal deformities or blocked nasal passages
Notes: Edentulous simply refers to a lack of teeth

## Slide 14: Oronasal masks (general advantages)
Best suited for less cooperative patients
Better in patients with a higher severity of illness
Better for patients with mouth-breathing
Better in edentulous patients
Generally more effective ventilation

## Slide 15: Oronasal masks (cautions, disadvantages)
Claustrophobic
Hinder speaking and coughing
Risk of aspiration with emesis

## Slide 17: Clinical criteria for using NIPPV
Moderate to severe respiratory distress
Tachypnea (respiratory rate > 25/min)
Accessory muscle use or abdominal paradox
Blood gas derangement pH < 7.35, PaCO2 > 45 mmHg
PaO2/FiO2 < 300 or SpO2 < 92% with FiO2 0.5

## Slide 18: Contraindications
Non-availability of trained medical personnel
Inability to protect the airways—comatose patients, patients with cerebrovascular accident or bulbar involvement, confused and agitated patients, upper airway obstruction
Hemodynamic instability—uncontrolled arrhythmia, patients on very high doses of inotropes, recent myocardial infarction
Inability to fix the interface—facial abnormalities, facial burns, facial trauma, facial anomaly
Severe gastrointestinal symptoms—vomiting, obstructed bowel; recent gastrointestinal surgery, upper gastrointestinal bleeding
Life-threatening hypoxemia
Copious secretions
Conditions in which NIV has not been found to be effective

## Slide 19: Monitoring
The patient must be monitored very closely clinically (Table 1). All this must be documented every 15 min for the first hour in the clinical notes.

## Slide 20
Table 1

## Slide 21: Complications of NIV and corrective action

## Slide 22: Discontinuation of NIV
It is very important to know when to discontinue NIV and intubate and ventilate the patient.
NIV failure.
Worsening mental status
Deterioration of pH and PaCO2 after 1–3 h of therapy
Refractory hypoxemia—when even a brief discontinuation of NIV leads to significant fall in oxygen saturation
Intolerance to NIV.
Hemodynamic instability.
Inability to clear secretions

## Slide 23: Modes of NIV
NIV is divided into two main types, negative-pressure ventilation (NPV) and noninvasive positive-pressure ventilation (NIPPV); the latter is further subdivided into several subtypes, including continuous positive airway pressure (CPAP), bilevel positive airway pressure (BiPAP), and volume-assured pressure support (VAPS).
Choosing the initial mode of ventilation is based in part on past experience, in part on the capability of ventilators available to provide support, and in part on the condition being treated.

## Slide 24: NIV-CPAP
Improve oxygenation by increasing FRC and recruiting collapsed alveoli
It provides certain positive airway pressure throughout all phases of spontaneous ventilation
It is similar to breathing with your head stuck out of a moving car
CPAP » PEEP

## Slide 25
CPAP reduces preload and afterload. Hence it is a very effective for treatment of pulmonary oedema with low work of breathing.
Pressures are usually limited to 5-12 cm of H2O, since higher pressure tends to result in gastric distension requiring continual aspiration through a nasogastric tube.

## Slide 28: NIV- BiPAP
IPAP + EPAP( CPAP)
The higher pressure augments alveolar ventilation and CO2 clearance
The lower pressure maintains alveolar recruitment
IPAP: assists in improving tidal volume, thus decreasing CO2
EPAP : improve FRC, helps recruit more alveoli, thus increasing O2. may reduce work of breathing associated with autopeep

## Slide 30
Differential in pressure between inspiration and expiration allows for better patient-ventilator synchrony and thus more comfort
EPAP » PEEP
IPAP –EPAP » PS
Augments TV
Reduces Atelectasis
Reduces WOB

## Slide 31: NIPPV for acute exacerbation of COPD
The largest amount of supportive evidence for the use of NIPPV (particularly bilevel) is in the management of COPD exacerbation. Complications arising from dynamic hyperinflation in this population lead to excessive elastic and resistive forces that increase respiratory muscle workload and ultimately lead to respiratory failure. Intubation and invasive mechanical ventilation become difficult because of the complicated lung mechanics associated withCOPD.
The use of NIPPV in these patients results in lower failure rates compared to standard medical therapy, lower requirement for intubation, lower mortality and decreased length of stay in hospital.
The level of applied EPAP helps to splint open airways at risk of collapsing, and the delivered pressure (IPAP) assists with the increased respiratory muscle workload.

## Slide 32: NIPPV for acute cardiogenic pulmonary edema
The use of NIPPV for acute cardiogenic pulmonary edema (ACPE) is aimed at treating the respiratory complications related to the presence of pulmonary edema.
The use of CPAP alone may increase the functional residual capacity, reduce atelectasis, improve respiratory system compliance, reduce right-to-left intrapulmonary shunting and improve cardiac output.
However, because there is often an associated increased respiratory workload with ACPE, the use of bilevel NIPPV may be more appropriate for the patient to reduce the amount of respiratory distress.
The patient presentation and response to therapy should therefore influence the choice of mode and pressures used.

## Slide 33: NIPPV for ARDS
Acute respiratory distress syndrome (ARDS) is not a good candidate disease for NIPPV, since it is slow to resolve and patients have very severe pulmonary dysfunction, and the literature has been discouraging.
While CPAP and NIPPV have been shown to improve gas exchange, they do not reduce the eventual need for intubation or mortality.
Patients with ARDS are also prone to the effects of stress placed on the lungs by positive pressure ventilation and a controlled ventilatory approach targeting small lung volumes is more appropriate.

## Slide 34: Fraction of inspired oxygen (FIO2)
For all supplemental oxygen delivery devices, the patient is not just breathing the direct oxygen, but rather is breathing a combination of room air plus the oxygen from the supplemental device.
The concentration of oxygen in the air that we breathe is called the FiO2 (Fraction of inspired oxygen). If a patient is not receiving any additional oxygen, we often say that the patient is on an FiO2 of .21 (21%) or "Room Air"
Notes: the FIO2 should always be set at 100% until adequate arterial oxygenation is documented. A short period with an FIO2 of 100% is not dangerous to the patient receiving mechanical ventilation and offers the clinician several advantages
Except COPD PT

## Slide 35
The I:E ratio is the ratio of the duration of inspiratory and expiratory phases
A normal I:E ratio at rest is about 1:2, and so the default duration of the expiratory phase in mechanical ventilation is approximately twice the duration of the inspiratory phase.
The inspiratory rise time determines the rate at which the ventilator achieves a target pressure (in pressure control and pressure support modes) or flow rate (in volume control modes).

## Slide 37
Ramp Rise time
ms
Inspiratory time
Tinsp (Inspiratory Time) seconds or ms
Rise time
Inspiratory time