## Slide 1
Unit # 06
Pin Out of 8086 Microprocessor
By
Dr. Feryal Althefery
Pin Out of 8086 Microprocessor
Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq

## Slide 2
1
Outlines of the lecture
1. Pin Out Description.
2. Logic Devices for Interfacing.
Unit # 06
Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq

## Slide 3
2
Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
q
Pin Out Description
X1 & X2
Pin 1 and Pin 2 (Input)
These are also called Crystal Input Pins.
A 8085 microprocessor need oscillator to
generate clock signal.
The frequency of oscillator is twice of
microprocessor frequency.
H/W / solve the question 18 of reference book in
p.p. 1-51 (frequency only)
Unit # 06

## Slide 4
3
Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
It is used to reset the microprocessor.
It is active low signal.
When the signal on this pin is low for at least
3 clock cycles, it forces the microprocessor
to reset itself which means:
RESET IN and RESET OUT
Pin 36 (Input) and Pin 3 (Output)
RESET IN:
Clearing the PC and IR.
Disabling all interrupts (except TRAP).
Disabling the SOD pin.
All the buses (data, address, control) are
tristated( what is meaning that?).
Gives HIGH output to RESET OUT pin.
Unit # 06

## Slide 5
4
Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
It is used to reset the peripheral devices and
other ICs on the circuit.
It is an output signal.
It is an active high signal.
RESET IN and RESET OUT
Pin 36 (Input) and Pin 3 (Output)
RESET OUT:
The output on this pin goes high whenever
RESET IN is given low signal.
Unit # 06

## Slide 6
5
Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
It takes 1 bit input from serial port of 8086.
Stores the bit at the 8th position (MSB) of the
Accumulator.
RIM (Read Interrupt Mask) instruction is
used to transfer the bit.
SID (Serial Input Data):
SID and SOD
Pin 4 (Input) and Pin 5 (Output)
Unit # 06

## Slide 7
6
Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
It takes 1 bit from Accumulator to serial
port of 8085.
Takes the bit from the 8th position (MSB) of
the Accumulator.
SIM (Set Interrupt Mask) instruction is used
to transfer the bit.
SOD (Serial Output Data):
SID and SOD
Pin 4 (Input) and Pin 5 (Output)
Unit # 06

## Slide 8
7
Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
It has the highest priority.
It cannot be disabled.
It is both edge and level triggered.
It is an non-mask able interrupt.
TRAP
Pin 6 (Input)
It means TRAP signal must go from low to high.
And must remain high for a certain period of
time.
TRAP is usually used for power failure and
emergency shutoff.
Unit # 06

## Slide 9
8
Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
It has the second highest priority.
It is positive edge triggered only.
It is a mask able interrupt.
RST 7.5
Pin 7 (Input)
The internal flip-flop is triggered by the rising
edge.
The flip-flop remains high until it is cleared
by RESET IN.
Unit # 06

## Slide 10
9
Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
It has the third highest priority.
It is triggered edge only.
It is a mask able interrupt.
RST 6.5
Pin 8 (Input)
The pin has to be held high for a specific period
of time.
RST 6.5 can be enabled by EI instruction.
It can be disabled by DI instruction.
Unit # 06

## Slide 11
10
Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
It has the fourth highest priority.
It is also triggered edge only.
It is a mask able interrupt.
RST 5.5
Pin 9 (Input)
The pin has to be held high for a specific period
of time.
This interrupt is very similar to RST 6.5.
Unit # 06

## Slide 12
11
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
It is an out going signal.
It is an active low signal.
It stands for interrupt acknowledge.
INTA
Pin 11 (Input)
Low output on this pin indicates that
microprocessor has acknowledged the INTR
request.
Unit # 06

## Slide 13
12
Dr. Feryal Althefery
Feryal. Ibrahim @uomus.edu.iq
Pin Out Description
Address and Data Pins
Address Bus:
• The address bus is used to send
address to memory or IO devices.
• It selects one of the many locations in
memory or one of I/O devices.
• Its length 16-bit.
Data Bus:
• It is used to transfer data between
microprocessor and memory or IO devices.
• Its length 8-bit.
Unit # 06

## Slide 14
13
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
During 1st clock cycle, these pins operate as lower
half of address.
The separation of lower order address
and data is done using address latch circuit.
These pins serve the dual purpose of
transmitting lower order address and data byte.
In remaining clock cycles, these pins operate as
data bus.
AD0 – AD7
Pin 19-12 (Bidirectional)
H/W / solve the question 23 of reference book in p.p. 1-51
Unit # 06

## Slide 15
14
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
During 1st clock cycle, ALE is activated.
This latch circuit used to latch the status
of lower order address bus
AD0 – AD7
Pin 19-12 (Bidirectional)
Unit # 06

## Slide 16
15
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
The address is sent from microprocessor to
memory or I/O devices.
These pins carry the higher order of address
bus.
These 8 pins are switched to high impedance
state during HOLD and RESET mode.
A8 – A15
Pin 21-28 (Unidirectional)
Unit # 06

## Slide 17
16
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
It indicates whether bus functions as
address bus or data bus.
If ALE = 1 then
Bus functions as address bus.
It is used to enable Address Latch.
ALE
Pin 30 (Output)
If ALE = 0 then
◦ Bus functions as data bus.
Unit # 06

## Slide 18
17
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
They tell the current operation which is in
progress in 8085.
S0 and S1 are called Status Pins.
S0 and S1
Pin 29 (Output) and Pin 33 (Output)
Unit # 06

## Slide 19
18
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
This pin tells whether I/O or memory operation
is being performed.
IO/M
Pin 34 (Output)
If IO/M = 1 then
◦ I/O operation is being performed.
If IO/M = 0 then
◦ Memory operation is being performed.
Unit # 06

## Slide 20
19
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
It is an active low signal.
It is a control signal used for Read operation
either from memory or from Input device.
RD stands for Read.
A low signal indicates that data on the data
bus must be placed either from selected
memory location or from input device.
RD
Pin 32 (Output)
Unit # 06

## Slide 21
20
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
It is also active low signal.
It is a control signal used for Write operation
either into memory or into output device.
WR stands for Write.
A low signal indicates that data on the data
bus must be written into selected memory
location or into output device.
WR
Pin 31 (Output)
Unit # 06

## Slide 22
21
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
A low value causes the microprocessor to enter
into wait state.
The microprocessor remains in wait state
until the input at this pin goes high.
This pin is used to synchronize slower
peripheral devices with fast microprocessor.
READY
Pin 35 (Input)
Unit # 06

## Slide 23
22
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
A high signal on this pin is a request to
microprocessor to relinquish the hold on buses.
This request is sent by DMA controller.
HOLD pin is used to request the microprocessor
for DMA (Direct Memory Accesses) transfer.
HOLD
Pin 38 (Input)
Intel 8257 and Intel 8237 are two DMA
controllers.
Unit # 06

## Slide 24
23
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
The microprocessor uses this pin to
acknowledge the receipt of HOLD signal.
When HLDA signal goes high, address bus, data
bus, RD, WR, IO/M pins are tri-stated. This
means they are cut-off from external
environment.
HLDA stands for Hold Acknowledge.
HLDA
Pin 39 (Output)
The control of these buses goes to DMA controller.
Control remains at DMA Controller until
HOLD is held high.
When HOLD goes low, HLDA also goes low and
the microprocessor takes control of the buses.
Unit # 06

## Slide 25
24
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Pin Out Description
Ground signal is connected to VSS.
+5V power supply is connected to VCC.
VSS and VCC
Pin 20 (Input) and Pin 40 (Input)
H/W / solve the question 21 of
reference book in p.p. 1-51
Unit # 06

## Slide 26
25
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Logic Devices for Interfacing:
It is explained previously.
1. Multiplexing AD7 - AD0
Unit # 06

## Slide 27
26
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Logic Devices for Interfacing:
2. Generation of control signals:
Table below shows the logic state to execute these three control signals.
The important control signals are RD, WR and IO/M signals which organize the data
follow between microprocessor and memory location or IO devices.
IO/M | RD | WR | MEMR RD + IO/M | MEMW WR + IO/M | IOR RD + IO/M | IOW WR+ IO/M
0 | 0 | 0 | Condition never exists, because RD and WR signals doesn’t go low simultaneously |  |  | 
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | Condition never exists, because RD and WR signals doesn’t go low simultaneously |  |  | 
1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
Unit # 06

## Slide 28
27
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Logic Devices for Interfacing:
2. Generation of control signals:
Figure below shows the circuit which generates the truth table shown in previous slide
IO/M | RD | WR | MEMR RD + IO/M | MEMW WR + IO/M | IOR RD + IO/M | IOW WR+ IO/M
0 | 0 | 0 | Condition never exists, because RD and WR signals doesn’t go low simultaneously |  |  | 
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | Condition never exists, because RD and WR signals doesn’t go low simultaneously |  |  | 
1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
Unit # 06

## Slide 29
28
Dr. Feryal Althefery
Feryal.Ibrahim@uomus.edu.iq
Logic Devices for Interfacing:
3. Bus Drivers :
Typically, the 8085 buses can source 400 A and sink 2 mA of current, i.e. it can drive
only one TTL load.
One of solutions of this problem is using buffer which increase capacity of buses for
more than one TTL as in figures below.
Unit # 06