## Slide 1
ventilation
Mechanical ventilation(MV)
Invasive ventilation
Non-invasive ventilation(NIV)
L-6
Dr.Zainab AL_Youseif
M.B.Ch.B /FICMS.A&IC

## Slide 2: I:E Ratio
The I:E ratio is the ratio of the duration of inspiratory and expiratory phases
A normal I:E ratio at rest is about 1:2, and so the default duration of the expiratory phase in mechanical ventilation is approximately twice the duration of the inspiratory phase.
The inspiratory rise time determines the rate at which the ventilator achieves a target pressure (in pressure control and pressure support modes) or flow rate (in volume control modes).

## Slide 4
Total cycle time (TCT) equals inspiratory time (TI) plus expiratory time:
Respiratory rate (f) equals 1 min (60 seconds) divided by TCT.
a Calculate TCT from f.

## Slide 5
I:time (Inspiratory Time)
E:time (Expiratory Time)
I:E Ratio= 1:2 most common
Respiratory Rate 15
60 ÷ 15 = 4 (total cycle time)
I= 1 second, E= 3 seconds, I:E Ratio 1:3
Respiratory Rate 12
60 ÷ 12 = 5 (total cycle time)
I= 1 second, E= 4 seconds, I:E Ratio 1:4

## Slide 6: Notes
Infant ReVel default I:Time= 0.3 seconds
Pediatric ReVel default I:Time= 0.7 seconds
Measured I:E ratios will have decimal points – They are actual real time measurements that change dependent on patients measured respiratory rate.
Examples= 1:3.2, 1:4.1, 1:2.7, 0.7:2.3

## Slide 7
Ti=Vt(L)/flow(L/s)

## Slide 8
A time cycled ventilator is set with the following parameter: Vt=500 f=12 I:E =1:4. If a constant flow waveform is used, what is the inspiratory gas flow?
Flow= 0.5L/1sec x 60sec/min=
30L/min

## Slide 9
You are asked to ventilate a 63yr old female pt in severe CHF. Her ABG on a non-rebreather: ph 7.18, PaCO2 83, PaO2 98 HCO3 31. She is orally intubated with a 7.5 ETT with VT=400ML, RR=15, I:E = 1:4
Determine the following:
Ti
Ei
TCT
flow

## Slide 10
You are asked to ventilate a 33yr old male pt in severe ARF. His ABG on a non-rebreather: ph 7.18, PaCO2 73, PaO2 90 HCO3 31. he is orally intubated with a 8 ETT with constant gas flow 40 L/min, RR=14, I:E = 2:3
Determine the following:
Ti(I time)
Te(E time)
TCT
VT

## Slide 11
  Adjusting I:E Ratio
    I :  I  TI  smaller I:E ratio
    I :  I  TI  larger I:E ratio
    VT: VT  TI  larger I:E ratio
    VT: VT  TI  smaller I:E ratio
    f : RR  TE  larger I:E ratio
    f : RR  TE  smaller I:E ratio