## Slide 1: TRANSPOSITION

## Slide 2
Transposition is the term applied to the method of converting a prescription of lens power to another possible optically equivalent lens power. Thus, by transposition a prescription of convex cylindrical lens can be converted to optically equivalent concave cylindrical power, or vice versa.
RULES OF TRANSPOSITION
Power of the spherical lens–Add the spherical and cylindrical power algebraically, taking into account their signs.
Power of the cylindrical lens–Only change the sign of the cylinder from plus (+) to minus ( – ), or vice versa. The numerical strength of the cylinder remains the same.
Axis of the cylinder–Change the axis by 90º. If the original axis is at or less than 90°, add 90° to it. If the original axis is over 90°, subtract 90° from it.

## Slide 3
EXAMPLES
1. If the original prescription is –3.00DSPH with +1.00DCYL 90°↓
Rule i. –3.00 + (+) 1.00 = –2.00 DSPH
Rule ii. +1.00DCYL becomes –1.00DCYL
Rule iii. 90°↓ axis becomes 180° axis
Hence, the transposed power is –2.00DSPH with –1.00DCYL 180°
2. If the original prescription is –3.00DSPH with -1.00DCYL 45°
Rule i. –3.00 + (–) 1.00 = –4.00 DSPH
Rule ii. –1.00DCYL becomes +1.00DCYL
Rule iii. 45° axis becomes 45° + 90° = 135° axis Hence, the transposed power is
–4.00DSPH with +100DCYL 135° axis.
3. If the original prescription is –2.00DSPH with +2.00DCYL 105°
Rule i. –2.00 + (+) 2.00 = 0, i.e. Plano
Rule ii. +2.00DCYL becomes –2.00DCYL
Rule iii. 105° axis becomes 105º – 90º = 15° axis
Hence, the transposed power is –2.00DCYL 15° axis

## Slide 4
NEUTRALISATION (DETERMINATION OF POWER OF A LENS)
Neutralisation is the technique for determining the power of an ophthalmic lens. Neutralisation is done by following methods.
MANUAL METHOD
It is basically a very simple but quick and accurate way of checking the power of glasses. It is done by trial and error with the help of the lenses present in the trial box. In this method, lenses of known power are placed in contact with the lens under verification until the power of the combination becomes zero, i.e. there is no movement of the distant object. A lens under verification will be neutralised by another lens of equivalent power of opposite sign. So, a –3.00DSPH lens will be neutralised by a +3.00D SPH lens
{–3.00DSPH + (+3.00DSPH) = 0}.
Neutralisation is based on the identification properties of convex and concave spherical lenses discussed earlier in this chapter. Convex spherical lens exhibit against movement and concave spherical lens exhibit with movement of the object, if they are moved in front of the eye.

## Slide 5
RULES OF NEUTRALISATION
•Object/Target should be placed at a convenient furthest distance.
•Ideally a cross with two limbs at 90° should be the target. In the absence of cross, a window frame or other vertical and horizontal intersection may be employed as the target. Conveniently, Snellen’s distant vision chart may also be used.
Neutralizing lens should be placed in close contact with the front surface of the spectacle lens.
Attention must be paid to the central portion of the cross during neutralization.
The lenses should be held in front of the eyes.

## Slide 6
PROCEDURE OF NEUTRALISATION
Manual
a. Spherical lenses (Table 21.1)
b. Astigmatic lenses–Here the same principle is applied but it requires further steps. It can be done in two ways— 1st procedure–Here both spherical and planocylindrical neutralising lenses are employed.

## Slide 7
Table 12-1:
Manual neutralisation of spherical lens

## Slide 8
i. Align the principle meridians of the lens under test with the cross by rotating until no scissors effect is seen. So, the principle meridians are now vertical and horizontal.
ii. Neutralise the vertical meridian with a spherical lens as described earlier.
iii. Now, the transverse movement in horizontal meridian still exists contributed by the cylindrical power of the lens under test.

## Slide 10
Example: If vertical meridian is neutralized by a +2.50D lens and the horizontal meridian is neutralised by a –3.00D lens what will be the power of the lens ?
Ans. Hence, the power of the vertical meridian will be –2.50D and power of the horizontal meridian will be +3.00D. So, the power of the lens under test will be either –2.50DSPH with +5.50DCYL 90° or +3.00DSPH with –5.50DCYL 180°.
Mechanical
It can be done by the following instruments (discussed in chapter 16).
Geneva lens measure
Focimeter/Lensometer
Automated Lensometer.

## Slide 11
: Spherical Equivalent
. The Spherical Equivalent of an Astigmatic Prescription An astigmatic eye requires a prescription with spherical power, cylinder power and cylinder axis; this combination results in a focal point positioned on the retina. The cylinder axis and power are correcting the astigmatic part of the refractive error. If an astigmatic eye were to be corrected with a spherical lens alone, the result would be a blur circle — circle of least confusion — on the retina. The spherical lens power that places the circle of least confusion on the retina is called the spherical equivalent. Rule for finding the spherical equivalent: Add one-half of the cylinder power to the sphere algebraically (that is, keeping in mind the plus and minus signs). Example 1: What is the spherical equivalent for: -6.00 +2.00 × 90? Applying the rule: One-half of the cylinder power is +1.00; +1.00 added algebraically to -6.00 = -5.00 Answer: -5.00

## Slide 12
Note When writing a glasses prescription, the spherical equivalent calculation is used if one decides to give less cylinder power than was measured. If it was decided to reduce the cylinder power in this example by half a diopter, the resulting prescription would be: -5.75 +1.50 × 90. This calculation can and should be checked by making sure the original and the modified prescriptions have the same spherical equivalent. Example 2: What is the spherical equivalent for +3.50 +0.50 × 180? Applying the rule: +0.25 added algebraically to +3.50 = +3.75 Answer: +3.75