## Slide 1: Digital Electronic
Asst.lec Israa Hussein
2nd semester

## Slide 2: Chapter one
Lecture 1

## Slide 3: 1.1 Introduction
The Boolean algebra was created by the English
mathematician George Boole (1815-1864).
The Boolean algebra codifies rules of relationship between mathematical quantities to one of two possible values: true or false, 1 or 0.
All arithmetic operations performed with Boolean quantities have but one of two possible outcomes: either 1 or 0.

## Slide 4
There are three basic Boolean arithmetic operations:
Boolean addition which is equivalent to the OR logic function, as well as parallel switch contacts.
Boolean multiplication, which is equivalent to the AND function as well as series switch contacts.
Boolean complementation which is equivalent to the NOT logic function.

## Slide 5: 2.1 Digital versus Analogue representation:
O There are two basic ways to represent quantities:
Analogue representation and digital representation.
O With analogue representation, the quantity is
symbolized in a way that is infinitely divisible.
O With digital representation, the quantity is symbolized in a way that is discreetly packaged.

## Slide 6: Example 1.1:
O The height of the red column which indicates the temperature measured by a thermometer is an analogue representation.
O An electronic watch whose digits changes second after second, minute after minute, shows a digital representation.

## Slide 7
The comparison between digital and analogue representations can be given as in the following chart:
Analogue representation | Digital representation
Infinitely divisible | Discrete (Step by step)
Prone to errors of precision | Absolute precision

## Slide 8: 1.3 Systems of numeration:
To represent quantities in the different systems of numeration, specific symbols are used, which are also called ciphers.
O
    Decimal numeration system:
      Decimal system is the most common numeration system for daily uses. It is constituted by 10 symbols or ciphers: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9.
      Each cipher represents an integer quantity and each place from right to left in a decimal notation represents a weight for each integer quantity.

## Slide 9: Example 1.2:
Hundreds place, thousands place, and so on…
Let’s consider the decimal notation 1253. This number can be broken into its constituent weight-products as such:
1253= 1000 + 200 + 50 + 3
1253= 1×1000 + 2×100 + 5×10 + 3×1
1253= 1×103 + 2×102 + 5×101 + 3×100
It is easily to notice that the cipher 1 is more weighted than the cipher 2 which in his turn is more weighted than the cipher 5. The cipher 3 is the less weighted.
In the decimal numeration system, each cipher is called a digit.
Each weight or place value is ten that of the one to the immediate
right.
The less weighted cipher carries the One place, the cipher at the immediate left carries the Tens place, the follower carries the

## Slide 10: 1.3.2 Binary numeration system:
The binary numeration system uses only two ciphers instead of ten as the decimal numeration system. Those two ciphers are “0” and “1”.
In binary system of numeration, ciphers are called bit
(Binary Digit).
Cipher are arranged right to left in doubling values of weight (instead of multiplying the weight by 10 as in the case of decimal system).
10

## Slide 11: 1.3.2 Binary numeration system:
Let’s consider the following binary number
,
Each weight is 2 that of the one in the immediate right.
The less weighted cipher carries the Ones place
the cipher at the immediate left carries the twos place
the following cipher carries the fourth place …
11

## Slide 12: Exercise 1.1:
O Convert the following binary numbers to decimal numbers:
A = 110101
B = 100110101
C = 11110111101
D = 101100001111
12