## Slide 1: Digital Electronic
Assistance lecture : Israa Hussein
2nd semester

## Slide 2: Chapter One Lecture 3

## Slide 3: 1.3.5 Hexadecimal numeration system:
The hexadecimal numeration system is a place weighted system with a base of sixteen.
Valid ciphers include the normal decimal symbols “0”,”1”,”2”,”3”,”4”,”5”,”6”,”7”;”8”;9” Plus six alphabetical characters A, B, C, D, E, and F.
To convert from binary to hexadecimal numeration,
we group bits in fours.
Each group of four bit is replaced by its hexadecimal equivalent.
The following table summarizes the equivalence between decimal, binary, octal and hexadecimal systems.

## Slide 4
Decimal | Binary | Octal | Hexadecimal
0 | 0000 | 0 | 0
1 | 0001 | 1 | 1
2 | 0010 | 2 | 2
3 | 0011 | 3 | 3
4 | 0100 | 4 | 4
5 | 0101 | 5 | 5
6 | 0110 | 6 | 6
7 | 0111 | 7 | 7
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 5
Example 1.6:
Convert the following binary numbers in hexadecimal?
A = 1101011101
B = 11101011101.11
Solution :
As explained above,
We just have to group the binary number in groups of four bits each:

## Slide 6
As explained above, we just have to group the binary number in groups of four bits each:
The binary number has been grouped is groups of four bits each, from the right to the left two implied zeros have been added at the extreme left. In the same way the number B can also be converted.

## Slide 7
  Changing of base:
We have already seen in the previous section how to change from binary to decimal, octal or hexadecimal systems of numeration. The present section is intended to show how to move from a given system of numeration to any other system.
From octal and hexadecimal to binary and decimal:
The octal and hexadecimal systems are actually used by computer engineers just to obtain a “shorthand” representation of binary numbers (because octal and hexadecimal representations take a few numbers of ciphers or symbols as compared to the binary system).
Only binary system is implemented in the electronic circuits of digital systems (through two levels of voltages or currents: high (1) and low (0)), the other systems being used by engineers just for simplification issues.
However, we sometimes have the need to convert either of those systems to binary or decimal forms.

## Slide 8
      Octal and hexadecimal to binary:
It is obvious that to convert from octal to binary,
We must convert each octal cipher to its binary equivalent in 3 bits.
In the same way, to convert from hexadecimal to binary, we should convert each hexadecimal symbol into its binary equivalent in 4 bits.

## Slide 9: Example 1.7:
Convert the following octal number to digital 5238.
Convert the following hexadecimal number to binary 4DC216.

## Slide 10: 1.4.1.2 Octal to Decimal
Because octal is a base of eight numeration system, each place weight value differs from either adjacent place by factor of eight.
Example 1.8:
Let us convert the following octal number to decimal: A = 264.748

## Slide 11: Exercise 1.3:
Convert the following octal number to decimal:
A = 4562.368
B = 523411.2328
C= 264.3658
D = 4516328
Is the number 12586 an octal number?

## Slide 12
      Hexadecimal to Decimal
The technique for converting hexadecimal notation to decimal is the same as the one used above, except that each successive place weight changes by a factor of sixteen.
Example 1.9:
Let us convert the following hexadecimal number to decimal:

## Slide 13: Exercise 1.4:
Convert from hexadecimal to decimal.
X = A23C.DF16
Y = 7D3E16
Z= D96EC.FA16