## Slide 2: Analysis Methods and Y-D (Star-Delta)
8.2 CURRENT SOURCES
A current source determines the direction and magnitude of the current in the branch where it is located.
The magnitude and the polarity of the voltage across a current source are each a function of the network to which the voltage is applied.
EXAMPLE 8.1 Find the source voltage, the voltage V1, and current I1 for the circuit in Fig.
1

## Slide 3: EXAMPLE 8.2 Find the voltage Vs and currents I1 and I2 for the network in Fig.
for the current source, Vs must be determined, and for the voltage source, Is must be determined.
Since the current source and voltage source are in parallel,

## Slide 4
8.3 SOURCE CONVERSIONS
For the voltage source, if Rs=0 , or if it is so small compared to any series resistors that it can be ignored, then we have an “ideal” voltage source for all practical purposes.
For the current source, since the resistor Rp is in parallel, if RP = ∞ , or if it is large enough compared to any parallel resistive elements that it can be ignored, then we have an “ideal” current source.
Note that:
Ideal sources cannot be converted from one type to another.
The equivalence between a current source and a voltage source exists only at their external terminals.

## Slide 5
EXAMPLE 8.4 For the circuit in Fig.
Determine the current IL.
Convert the voltage source to a current source.
Using the resulting current source of part (b), calculate the current through the load resistor, and compare your answer to the result of part (a).

## Slide 6
8.4 CURRENT SOURCES IN PARALLEL
Current sources of different values cannot be placed in series due to a violation of Kirchhoff’s current law.
However, current sources can be placed in parallel just as voltage sources can be placed in series. In general,
Two or more current sources in parallel can be replaced by a single current source having a magnitude determined by the difference of the sum of the currents in one direction and the sum in the opposite direction. The new parallel internal resistance is the total resistance of the resulting parallel resistive elements.
Current sources of different current ratings cannot be connected in series.
EXAMPLE 8.6 Reduce the parallel current sources in Fig. to a single current source.

## Slide 7: EXAMPLE 8.8 Reduce the network in Fig. to a single current source, and calculate the current through RL .
Applying the current divider rule to the resulting network in Fig.

## Slide 8
8.6 BRANCH-CURRENT ANALYSIS
Assign a distinct current of arbitrary direction to each branch of the network.
Indicate the polarities for each resistor as determined by the assumed current direction.
Apply Kirchhoff’s voltage law around each closed, independent loop of the network.
Apply Kirchhoff’s current law at the minimum number of nodes that will include all the branch currents of the network.
Solve the resulting simultaneous linear equations for assumed branch currents.

## Slide 9
EXAMPLE 8.9 Apply the branch-current method to the network in Fig.
Step 1: Since there are three distinct branches (cda, cba, ca), three currents of arbitrary directions (I1, I2, I3) are chosen, as shown.
The current directions for I1 and I2 were chosen to match the “pressure” applied by sources E1 and E2, respectively.
Since both I1 and I2 enter node a, I3 is leaving.
Step 2: resistor with
Polarities are drawn assumed
for each to agree current
directions, as shown.

## Slide 10: Step 3: Kirchhoff’s voltage law is applied around each closed loop (1 and 2) in the clockwise direction:
Step 4: Applying Kirchhoff’s current law at node a (in a two-node network, the law is applied at only one node),

## Slide 11: Step 5: There are three equations and three unknowns (units removed for clarity):
Using third-order determinants (Appendix D), we have

## Slide 12
Solution 2: Instead of using third-order determinants as in Solution 1, we can reduce the three equations to two by substituting the third equation in the first and second equations:

## Slide 13
Mesh Analysis Procedure
Assign a distinct current in the clockwise direction to each independent, closed loop of the network. It is not absolutely necessary to choose the clockwise direction for each loop current. However, by choosing the clockwise direction as a standard, we can develop a shorthand method (Section 8.8) for writing the required equations that will save time and possibly prevent some common errors.
Indicate the polarities within each loop for each resistor as determined by the assumed direction of loop current for that loop. Note the requirement that the polarities be placed within each loop. This requires, as shown in Fig., that the 4 Ω resistor have two sets of polarities across it.
Apply Kirchhoff’s voltage law around each closed loop in the clockwise direction. Again, the clockwise direction was chosen to establish uniformity and prepare us for the method to be introduced in the next section.
  If a resistor has two or more assumed currents through it, the total current through the resistor is the assumed current of the loop in which Kirchhoff’s voltage law is being applied, plus the assumed currents of the other loops passing through in the same direction, minus the assumed currents through in the opposite direction.
  The polarity of a voltage source is unaffected by the direction of the assigned loop
currents.
Solve the resulting simultaneous linear equations for the assumed loop currents.

## Slide 14
EXAMPLE 8.11 Consider the same basic network as in Example 8.9, now appearing as shown

## Slide 15
The actual current through the 2 V source and 2 Ω resistor is therefore 1 A in the other direction, and the current through the 6 V source and 1 Ω resistor is 2 A in the opposite direction indicated on the circuit.
The current through the 4 Ω resistor is determined by the following equation from the original network:

## Slide 16
8.9 NODAL ANALYSIS (GENERAL APPROACH)
The number of nodes for which the voltage must be determined using
nodal analysis is 1 less than the total number of nodes.
Nodal Analysis Procedure
Determine the number of nodes within the network.
Pick a reference node, and label each remaining node with a subscripted value of voltage: V1, V2, and so on.
Apply Kirchhoff’s current law at each node except the reference. Assume that all unknown currents leave the node for each application of Kirchhoff’s current law. In other words, for each node, don’t be influenced by the direction that an unknown current for another node may have had. Each node is to be treated as a separate entity, independent of the application of Kirchhoff’s current law to the other nodes.
Solve the resulting equations for the nodal voltages.

## Slide 17: EXAMPLE 8.21 Determine the nodal voltages for the network shown.
For the node V1. Applying Kirchhoff’s current
law:
For node V2, the currents are defined as

## Slide 20: 8.12 (Star-Delta) Y- Δ (T- π) AND Δ -Y (π -T) CONVERSIONS
19
It is our purpose to find some expression for R1, R2, and R3 in terms of RA, RB, and RC , and vice versa, that will ensure that the resistance between any two terminals of the Y configuration will be the same with the Δ configuration inserted in place of the Y configuration (and vice versa).

## Slide 22: Note that each resistor of the Y is equal to the product of the resistors in the two closest branches of the Δ divided by the sum of the resistors in the Δ.
Note that the value of each resistor of the Δ is equal to the sum of the possible product combinations of the resistances of the Y divided by the resistance of the Y farthest from the resistor to be determined.
Let us consider what would occur if all the values of a Δ or Y were the same. If RA RB RC, (using
RA only) the following:

## Slide 23
The Y and the Δ often appear as shown below. They are then referred to as a tee (T) and a pi (π) network, respectively. The equations used to convert from one form to the other are exactly the same as those developed for the Y and Δ transformation.

## Slide 24
EXAMPLE 8.29 Find the total resistance of the network shown, where RA = 3Ω , RB = 3 Ω , and RC
= 6 Ω .

## Slide 25
EXAMPLE 8.30 Find the total resistance of the network shown.
a. Converting the Δ to a Y:

## Slide 26
b. Converting the Y to a Δ :

## Slide 27: PROBLEMS
SECTION 8.2 Current Sources: 1, 2, 4, 6
SECTION 8.3 Source Conversions: 7, 8, 9, 10
SECTION 8.4 Current Sources in Parallel: 11, 12, 14
SECTION 8.6 Branch-Current Analysis: 15, 16, 18, 24
SECTION 8.9 Nodal Analysis: 35, 36, 38, 40
SECTION 8.12 Y – Δ (T-π) and Δ - Y (π-T) Conversions: 51, 52, 54, 56

## Slide 28
SECTION 8.2 Current Sources
1. For the network in Fig. 8.102:
a. Determine currents I2 and I3.
b. Find voltage V1.
c. Find the voltage across the source Vs.
2. For the network in Fig. 8.103:
a. Find current I2. Comment on the impact of Rp > > R1 or R2.
b. Calculate voltage V2.
c. Find the source voltage Vs.

## Slide 29
For the network in Fig. 8.105:
a. Find voltage Vs.
b. Calculate current I2.
c. Find the source current Is.
6. For the network in Fig. 8.107:
a. Find the currents I1 and Is.
b. Find the voltages Vs and V3.

## Slide 30: Thank you very much