## Slide 1: Analogue Electronic
1st semester

## Slide 2: Chapter 4 Transistor Lecture 9

## Slide 3
Transistor Currents
The conventional current flows toward the arrow on the emitter terminal. The emitter current (IE) is the sum of the collector current (IC) and the small base current (IB).
That is, IE = IC + IB
IB is very small compared to IE or IC. The capital-letter subscripts indicate DC values.
The voltage drop between the base and emitter is VBE, whereas the voltage drop between the collector and base is called VCB.
Figure:
Transistor currents.

## Slide 4
BJT Characteristics and Parameters
Two important parameters, βDC (DC current gain) and αDC are used to analyze a BJT circuit.
When a transistor is connected to DC bias voltages, as shown in Figure below for both npn and pnp types,
VBB forward-biases the base-emitter
junction, and VCC reverse-biases
the base-collector junction.
Figures of transistor DC bias circuits.
The collector current is directly proportional to the base current.
IC ∝ IB
The βDC of a transistor is the ratio of the DC collector current (IC) to the DC base current (IB).
This equation explains the amplification of current.
The ratio of the DC collector current (IC) to the DC emitter current (IE) is the (αDC).
is always less than 1

## Slide 5
Example
Determine the dc current gain βDC and the emitter current IE for a transistor where IB=50μA and IC= 3.65 mA.
Solution

## Slide 6
BJT Circuit Analysis
Consider the basic transistor bias circuit configuration in the Figure below. Three transistor DC currents and three DC voltages can be identified.
IB: DC base current
IE: DC emitter current
IC: DC collector current
VBE: DC voltage across the base-emitter junction
VCE: DC voltage across collector-emitter junction
VCB: DC voltage across collector-base junction
Figure 4: Transistor currents and voltages.

## Slide 7
When the base-emitter junction is forward-biased,
It is like a forward-biased diode and has a forward voltage drop of VBE≅0.7 V
The voltage at the collector concerning the grounded emitter is
VCE=VCC – ICRC (ICRC=VRC )
The current across IB is
The voltage across the reverse-biased collector-base junction is
VCB=VCE – VBE

## Slide 8
Example: Determine IB, IC, IE, VBE, VCE, and VCB in the circuit of the following Figure. The transistor has a βDC = 150.
Solution:
VBE≅ 0.7 V, Calculate the base, collector, and emitter currents as follows:
Since the collector is at a higher voltage than the base, the CB junction is reverse-biased.

## Slide 9
Collector Characteristic Curves
The collector characteristic curves show three modes of operation of the transistor. The collector current IC variation varies with the VCE for a specified value of base current IB.
Assume that VBB is set to produce a certain value of IB, VCC is zero, and VCE is zero. As VCE is increased, IC increases until IB becomes constant.
When both BE, and BC junctions are forward biased, and the transistor is in the saturation region.
Figure : Collector
characteristic curves.

## Slide 10
In saturation, an increase in base current does not affect the collector current, and the relation IC=βDCIB is no longer valid.
The transistor current is maximum, and the voltage across the collector is minimum for a given load.
Figure : Base-emitter and base-collector junctions are forward-biased.

## Slide 11
When VCE is increased further and exceeds 0.7 V, the base-collector junction becomes reverse-biased, and the transistor goes into its operation's active, or linear, region.
IC levels off and remains essentially constant for a given value of IB as VCE continues to increase. The value of IC is determined only by the relationship expressed as IC=βDCIB.
A family of collector characteristic curves is produced when IC versus VCE is plotted for several values of IB, as illustrated in Figure below. It can be read from the curves. The value of βDC is nearly the same wherever it is read in the active region. In a BJT, the cutoff is the condition of no base current (IB=0), which results in only an extremely small leakage current (ICEO) in the collector circuit.
The subscript CEO represents collector to emitter with the base open. For practical work, this current is assumed to be zero. In cutoff, neither the BE junction nor the BC junction is forward-biased.
Figure: Cutoff: Base-emitter and
base-collector junctions are reverse-biased.

## Slide 12
Example:
Determine whether or not the transistor in the following figure is in saturation. Assume VCE(sat)= 0.2V.
Solution:
This shows that with the specified βDC, this base current can produce an IC greater than IC(sat). Therefore, the transistor is saturated.

## Slide 13
The BJT as a Switch
A BJT can be used as a switching device in logic circuits to turn on or off the current to a load. As a switch, the transistor is normally in either cutoff (load is OFF) or saturation (load is ON).
Figure: Switching action of an ideal transistor.