## Slide 1: Analogue Electronic

## Slide 2: Chapter 5 Amplifiers Lec. 10

## Slide 3
Amplifier Operation
DC Quantities use upper case Roman subscripts. Example: VCE (The second letter in the subscript indicates the reference point).
AC Quantities and time-varying signals use lowercase subscripts. Example: Vce. Instantaneous quantities are represented by lowercase letters and subscripts such as Ic, Ie, Ib, and Vce.
Internal transistor resistances are indicated as lowercase quantities with a prime and an appropriate subscript. An example is the internal ac emitter resistance (ŕe) .
External resistances are indicated as capital R with either a capital or lowercase subscript, depending on if it is a DC or AC resistance. Examples: RC and Rc.

## Slide 4
The Figure 1 shows an example of a specific waveform for the collector emitter voltage.

## Slide 5
Linear Amplifier
A linear amplifier amplifies a signal without distortion, so the output signal is an exact amplified replica of the input signal.
A voltage-divider-biased transistor with a sinusoidal AC source capacitive coupled to the base through C1 and a load capacitive coupled to the collector through C2 is shown in Figure 2.
For the amplifier shown, notice that the voltage waveform is inverted between the input and output but has the same shape.
Figure 2

## Slide 6
Transistor AC Models
To assume the operation of a transistor in an amplifier circuit, representing the device by a model circuit is often useful.
A transistor model circuit uses various internal transistor parameters to represent its operation. Transistor models are described in this section based on resistance or r parameters.
Another system of parameters is called h parameters. The five r parameters commonly used for BJTs are given in the following.
Table 1. The lowercase letter r with a prime denotes resistances internal to the transistor.

## Slide 7
To explain this model circuit in terms of a transistor’s AC operation as follows:
A resistance (ŕe) appears between the emitter and base terminals. This is the resistance “seen” looking into the emitter of a forward-biased transistor. The collector effectively acts as a dependent current source of αacIe or, equivalently, βacIb, represented by the diamond-shaped symbol; these factors are shown in Figure 3.
Figure 3: Relation of transistor symbol to r-parameter model.
It is also temperature-dependent and is based on an ambient temperature of 20°C.

## Slide 8: H.W
H.W 1: Determine the (ŕe) of a transistor that is operating with a DC emitter current of 2 mA.
H.W 2: What is IE if (ŕe) = 8Ω?