## Slide 1: Computer Network Protocols Network Layer (Part 2) Lesson 1
By
Dr. Layth Abdulkareem Hassnawi
جامعة المستقبل
كلية الهندسة والتقنيات الهندسية
قسم هندسة تقنيات الحاسوب
المرحلة الرابعة

## Slide 2: Network Layer Additional Protocols
The are number of additional protocols in network layer which perform additional task such as:
Addressing
Securing packets
Error reporting

## Slide 3: Addressing Protocol
Internet Protocol (IP): this protocol is responsible about gives an address to the client this address is called IP address.
IP Addresses Features
IP: (a logical address) Provides connectionless, best-effort (unreliable) delivery of datagrams through the network.
IP addresses are network layer addresses.
IP addresses are 32-bit numbers.
The host can get IP address by using one of these two ways
hard-coded by system administrator in a file (Static addressing)
Dynamic Host Configuration Protocol (DHCP): dynamically get address from as server (plug-and-play)

## Slide 4: Addressing Protocol
DHCP Working Steps (pool operation)
Step 1: When the client is connected to a network, a DHCPDISCOVER message is broadcasted from the client to the servers (client asks for IP address).
Step 2: When the DHCP server receives the DHCPDISCOVER request message then it replies with a DHCPOFFER message. This message contains all the network configuration settings required by the client.
Step 3: The client forms a DHCPREQUEST message in reply to DHCPOFFER message and sends it to the server indicating it wants to accept the network configuration sent in the DHCPOFFER message.
Step 4: Once the server receives DHCPREQUEST from the client, it sends the DHCPACK message indicating that now the client is allowed to use the IP address assigned to it.

## Slide 5: Addressing Protocol
DHCP can return more information than just allocated IP address on subnet:
Address of first-hop router for client.
Name and IP address of DNS sever.
Network mask. (Indicating network versus host portion of address).

## Slide 6: Addressing Protocol
The main benefits of IPv6 include the following:
Larger address space: IPv6 addresses are 128 bits, compared to IPv4’s 32 bits.
Globally unique IP addresses: Every node can have a unique global IPv6 address.
Site multihoming: IPv6 allows hosts to have multiple IPv6 addresses.
Header format efficiency: A simplified header with a fixed header size makes processing more efficient.
Improved privacy and security: IPsec is standard for IP network security, available for both IPv4 and IPv6.
Flow labeling capability: A new capability enables the labeling of packets belonging to particular traffic flows.
Increased mobility and multicast capabilities: Mobile IPv6 allows an IPv6 node to change its location on an IPv6 network and still maintain its existing connections.

## Slide 7: IP Security (IPSec) Protocols
IP Security (IPSec) is a collection of protocols designed by the Internet Engineering Task Force (IETF) to provide security for a packet at the network level.
IPSec helps to create authenticated and confidential packets for the IP layer.
IPSec operates in one of two different modes: the transport mode or the tunnel mode.
Transport Mode | Tunnel Mode
IPSec in the transport mode does not protect the IP header; it only protects the information coming from the transport layer. | IPSec in the tunnel mode protects the original IP header.

## Slide 8: Internet Control Message Protocol (ICMP)
ICMP is an error reporting protocol and is used by routers, hosts and network devices to generate error messages when there are problems delivering IP packets. It has the following features:
Used by hosts & routers to communicate network-level information
ICMP reports errors (unreachable host, router, port, or a requested service is not available) and sends control message(echo request/reply (used by ping)
ICMP does not attempt to make IP a reliable protocol. It simply attempts to report errors and provide feedback on specific condition.
ICMP messages are divided into error-reporting messages and query messages.
ICMP Applications
There are two simple and widely used applications which are based on ICMP:
Ping: The ping checks whether a host is alive & reachable or not. This is done by sending an ICMP Echo Request packet to the host, and waiting for an ICMP Echo Reply from the host.
Trace route: Trace route is a utility that records the route through the Internet between your computer and a specified destination computer. It also calculates and displays the amount of time each hop took.

## Slide 9
End Of Lesson 1
Thanks For Listening