## Slide 1: Computer Network Protocols Network Layer (Part 1) Lesson 5
By
Dr. Layth Abdulkareem Hassnawi
جامعة المستقبل
كلية الهندسة والتقنيات الهندسية
قسم هندسة تقنيات الحاسوب
المرحلة الرابعة

## Slide 2: Routing Protocols
A routing protocol is a combination of rules and a procedure that lets routers in the internet inform each other of changes.
Routing metric: a method by which routing algorithms determines that one route is better than another route, Metric may be (hop count, bandwidth, delay, and load).

## Slide 3: Interior versus Exterior Routing Protocols
An Autonomous System (AS), also known as a domain, is a collection of routers that are under a common administration, such as a company’s internal network or an Internet service provider’s (ISP’s) network. Because the Internet is based on the AS concept, two types of routing protocols are required:
Interior Gateway Protocols (IGPs): handle routing within an Autonomous System. IGP's figure out how to get from place to place between the routers you own.
Exterior Gateway Protocols (EGP): handle routing outside an Autonomous System and get you from your network, through your Internet provider's network and onto any other network.

## Slide 4: Interior versus Exterior Routing Protocols
IGP uses less-complicated metrics to ease configuration and speed up the decisions about best routing paths for faster convergence.
Slower to converge and more complex to configure.

## Slide 5: Routing Information Protocol (RIP)
RIP is a routing protocol for exchanging routing table information between routers.
It is a very simple protocol based on distance vector routing.
Simple intra-domain protocol.
Uses hop count as a path selection metric. (RIP prevents routing loops by implementing a limit on the number of hops allowed in a path from the source to a destination. The maximum number of hops allowed for RIP is 15. This hop limit, however, also limits the size of networks that RIP can support, a hop count of 16 are considered an infinite distance, in other words the route is considered unreachable).

## Slide 6: Routing Information Protocol (RIP)
There are three types of timers in RIP routing protocol, these are:
Routing-update timer (periodic timer): The periodic timer controls the advertising of regular update messages. Routers send updates every 30 seconds.
Route timeout (Expiration Timer): Expiration Timer if there is a problem on an internet and no update is received within the allotted 180 s, the route is considered expired and the hop count of the route is set to 16, which means the destination is unreachable.( Because 15 hop max).
Route-flush timer (Garbage Collection Timer): After the route timeout expires, the route-flush timer eventually expires, deleting the route from the table after 120s.
Drawbacks of RIP:
RIP has slow convergence and count to infinity problems
The hop count cannot exceed 15, or routes will be dropped.

## Slide 7: EIGRP
EIGRP is a protocol for routing IPv4 and IPv6.
EIGRP, however, is a hybrid routing protocol—it is a distance vector protocol with additional link-state protocol features.
Uses triggered updates (EIGRP has no periodic updates).
Provide fast convergence to minimize network traffic.
Uses the minimum bandwidth on the path of the destination network, and calculate a route from the total delay metrics.

## Slide 8
End Of Lesson 5
Thanks For Listening