## Slide 1
Thermodynamics 1 (Spring 2025)
Undergraduate 1st class
First Law of Thermodynamics
Mohammed Obeid
Department of Mechanical Power Techniques Engineering
Al-Mustqbal University
Week 2

## Slide 2
Main Contents
• First Law of Thermodynamics
• Steady Flow Energy Equation
• Non Flow Energy Equation
• Ideal Gas & Equation of State

## Slide 3
The First Law of Thermodynamics
(conservation of energy principle)
The First Law of Thermodynamics is a special case of the law of Conservation of Energy, where energy can neither be created nor destroyed but it can change forms.
This law stated that:
work
Heat
work
Heat
U = q – w U = q + w

## Slide 4
The First Law of Thermodynamics
(conservation of energy principle)
When a system under goes a thermodynamics cycle then the net heat supplied to the system from its surroundings is equal to the net work done by the system on its surroundings.
 means the sum of the heat (q) and work (w) done on/by the system during the complete cyclic change.
dq  dw
Notes: Meaning of thermodynamic cycle ماذا نعني بالدورة الثرموديناميكية,Fluid States in the Cycle:
Boiler: Water is heated to become high-pressure, high-temperature steam.
Turbine: Steam expands, producing work (power output).
Condenser: Steam is cooled and condenses back into water.
Pump: The pump increases the pressure of the condensed water before sending it back to the boiler.

## Slide 5
Solution
Application of first law of thermodynamics
Example 1:
In a certain steam plant, the turbine develops 1000 kW. The net heat supplied to the steam in the boiler is 2800 kJ/kg. The heat rejected to the cooling water in the condenser is 2100 kJ/kg, and the feed pump work required to pump the condense back to the boiler is 5 kW. Calculate the steam flow rate round the cycle.
Notes: في نظام بخاري معين, جزء التوربين سلط شغلا بمقدار 1000 كيلو واط, فان الحرارة المزوده الى هذا النظام البخاري في جزء البويلر تساوي 2800 كيلوجول/كيلوغرام, أيضا الحرارة المفقودة او المصروفة الى جزء المكثف او الكوندنسر تساوي 2100 كيلوجول/كيلو غرام لغرض تبريد الماء,,, الحرارة المنبعثة إلى مياه التبريد في المكثف هي 2100 كيلوجول/كجم، الشغل المطلوب لمضخة التغذية لضخ المكثف مرة أخرى إلى جزء البويلر هو 5 كيلواط. جد معدل تدفق البخار خلال هذه الدورة
q = q supplied – q rejected ……………. w = w turbine – w pump ……. m= Q/q ,, m steam flow rate & Q power output

## Slide 6
Main Contents
• First law of thermodynamics
• Steady Flow Energy Equation
• Non Flow Energy equation
• Ideal Gas & Equation of State

## Slide 7
The Steady Flow Energy Equation (open system)
This equation is a mathematical statement of the principle of the conservation of
energy as applied to the flow of fluid through a thermodynamic system.
The various forms of energy which fluid can have, as follows:
(a) Potential Energy Ep
If the fluid is at some height Z above a given datum level, then, as a result of its mass, it possesses potential energy
with respect to that datum.
Potential energy Ep= gZ (z is the height)
(b) Kinetic Energy: Ek
If the fluid is in motion, then it possesses kinetic energy. For a unit mass of fluid,
Kinetic energy Ek = ½ c2
(c) Internal Energy: u
It is the energy stored within a fluid which results from the internal motion of its atoms and molecules.
(d) Flow or Displacement Energy: DE
Any volume of fluid entering or leaving a system must displace an equal volume ahead of itself in order to enter or
leave the system.
Displacement energy = Pv
(e) Heat Received (rejected) (f) Work done
Notes: مائع…. Datum level متوى الافقي لبروجت معين
معادلة تدفق الطاقة بشكل منتظم

## Slide 8
The Steady Flow Energy Equation (open system)
The change in the total energy of a system during a process is the sum of the changes in its internal, kinetic, and potential energies and can be expressed as:
Esystem
Enthalpy change h = + (Pv)

## Slide 9
The Steady Flow Energy Equation (open system)
Total energy entering the system = Total energy leaving the system
Energy entering
the system
Heat entering
the system
Energy leaving
the system
Work transferred from the system
+
+
=
u1 + p1v1 + ½ C12 + gZ1 + (q) = u2 + p2v2 + ½ C22 + gZ2 + (w)
u - internal energy
p – pressure
v – specific volume
C – fluid velocity
g- gravitational force
Z – height
w - work
q- heat
h - enthalpy
[1]
h1 انثالبي
h2
Heat (q)
Work (w)

## Slide 10
The Steady Flow Energy Equation (Example-1)
In a turbine of gas turbine unit, the gases flow rate through the turbine at 17 kg/s and the power developed by the turbine is 14000 kW. The enthalpies of the gases at inlet and outlet are 1200 and 360 kJ/kg respectively and the velocities of the gas at inlet and outlet are 60 and 150 m/s respectively. Find the rate at which heat is rejected from the turbine.
m/s
kJ/kg
kJ/kg
Notes: m gas or mass flow rate = 17,
في وحدة توربين غازي، يبلغ معدل تدفق الغازات عبر التوربين 17 كجم/ثانية، وتبلغ الطاقة المُولّدة 14000 كيلوواط. تبلغ الانثالبي للغازات عند المدخل والمخرج 1200 و360 كيلوجول/كجم على التوالي، وسرعتا الغاز عند المدخل والمخرج 60 و150 مترًا/ثانية على التوالي. أوجد معدل طرد الحرارة من التوربين.

## Slide 11
The Steady Flow Energy Equation (Assignment)
Q/Air flows at a rate of 0.4 kg/s through an air compressor entering at 6 m/s, 1bar and 0.85 m3 /kg and leaving at 4.5 m/s, 6.9 bar and 0.16 m3 /kg. The internal energy of the energy leaving is greater than that of entering air by 88 kJ/kg, cooling water in the jacket surrounding the cylinder absorbs heat from the air at a rate of 59 kJ/s. find the power required to drive the compressor.
m = 0.4 kg/s
C1= 6 m/s
p1 = 1 bar
v1 = 0.85
C2= 4.5 m/s
p2 = 6.9 bar
v2 = 0.16
u2 = 88 kJ/kg
Q = m.q ….. m = mass flow rate = 0.4 kg/s, q = heat ? , Q = rate of heat absorbed = 59
Z1 ≈ Z2
Power = m . w? ….. w = work

## Slide 12
Main Contents
• First law of thermodynamics
• Steady Flow Energy Equation
• Non Flow Energy equation
• Ideal Gas & Equation of State

## Slide 13
The Non Flow Energy Equation (Closed system)
In the previous slide, it has been shown that the steady flow energy equation connecting the energies before and after the flow of unit mass of substance through a system according to equation [1],
However, in the case of a closed system, however, in which the fluid mass remains constant, no substance passing through the system boundary, the flow terms in equation [1] will not apply. Thus, the terms Pv, Z and C are neglected. The system is then to be nonflow. Thus, from equation [1], the energy equation for the non-flow case becomes:
u1  q  u2  w
from which
q  (u2  u1)  w The non-flow energy equation or simple energy equation
this is often written
q  w u

## Slide 14
Main Contents
• First law of thermodynamics
• Steady Flow Energy Equation
• Non Flow Energy equation
• Ideal Gas & Equation of State

## Slide 15
Ideal gas & Equation of State
It is a simple model to understand how gases behave by neglecting many complicated interactions at the atomic scale.
- The Equation of Ideal Gas is:
PV= mRT ……….. قانون الغاز المثالي

## Slide 16
The equation of state between two conditions at constant volume can be rewritten as:
Ideal gas & Equation of State

## Slide 17
Ideal gas & Equation of State

## Slide 18
Example:
Ideal gas & Equation of State (example)

## Slide 19
Next Week Lecture
Specific heat & Processes Using Ideal Gas