## Slide 1
AL- Mustaqbal University
Pharmacy college
Pharmacognosy 1
Second stage
Lab. 7 Column Chromatography
Dr. Abdulla Al-Khakani
Dr. Haider Redha

## Slide 2: Column Chromatography
This includes chromatographic methods in which:
The stationary phase is either solid or liquid packed into a column.
The mobile phase is a moving liquid or gas.
According to the mechanism of separation of solutes, five major types of CC are distinguished.
Usually, one mechanism predominates but does not exclude the others.

## Slide 3
Mechanism | Mobile phase | Stationary phase | Mode or type
Solutes move at different rates according to the forces of attraction to the stationary phase. | Liquid or gas | Solid that attracts the solutes | Adsorption Chromatography
Solutes equilibrate between the 2 phases according to their partition coefficients | Liquid or gas | Thin film of liquid formed on the surface of a solid inert support | Partition Chromatography
Solute ions of charge opposite to the fixed ions are attracted to the resin by electrostatic forces & replace the mobile counterions. | Liquid containing electrolytes | Solid resin that carries fixed ions & mobile counterions of opposite charge attached by covalent bonds | Ion Exchange Chromatography

## Slide 4
Mechanism | Mobile phase | Stationary phase | Mode or type
Molecules separate according to their size: Smaller molecules enter the pores of the gel, And need a larger volume of eluent. Larger molecules pass through the column at a faster rate. | Liquid | Porous gel with no attractive action on solute molecules | Molecular Exclusion Chromatography
Special kind of solute molecules interact with those immobilized on the stationary phase | Liquid or gas | Solid on which specific molecules are immobilized | Affinity Chromatography

## Slide 5: Column chromatography
Stationary phase is held in a narrow tube through which the mobile phase is forced under pressure or under the effect of gravity.

## Slide 6
Packing & operating the column:
1- Packing
The selection of the method of packing depends mainly on the density of the solid.
Techniques used are the wet, dry & slurry methods.
In all cases avoid inclusion of air bubbles.
2- Sample Application
Apply evenly & in a concentrated solution to the top of the column which is protected from disturbance (e.g. add glass wool or filter paper).

## Slide 7
3-Elution techniques:
Procedure | Technique
Addition of solvent mixture of fixed composition during the whole process. | Isocratic elution
Continuous or linear elution: in which there is continuous change in the composition of the mobile phase over a period (e.g. polarity, pH or ionic strength). Step wise or fractional elution: in which the change is not continuous i.e. a sudden change in the composition of the mobile phase is followed by a period where the mobile phase is held constant | Gradient elution

## Slide 8
4- Detection:
On column detection for colored or fluorescent compounds directly after
developing the chromatogram.
Monitoring of eluted fractions (PC or TLC).
Using special detectors connected to the column such as refractive index, UV detector.