## Slide 1
Biochemical Techniques
7th Lecture
Sterilization Techniqes,continued
Second Year Students / 2nd semester / 2024-2025
By
Prof. Dr. Naser Abdulhasan Naser
Al-Mustaqbal University
College of Science

## Slide 2
B-moist heat:-
1.pasteurization: uses heat 63ºС at 30 minutes. The organisms such as Brucella or Salmonella and tubercle bacilli which contribute to milk born-disease are readily killed by this process. The alternative method raises the temperature of milk to 72 ºС (161 º F) for 15-20 seconds and is referred to as the flash process. N.T: bacterial spores are not killed by this method.
2.Boiling water: A temperature at 100ºС will kill all non-sporing or vegetative organisms within 10 minutes. Most spores will be killed in 30 minutes at this temperature, but some spores will resist boiling for several hours. The addition of 2% sodium carbonate increases the disinfecting power of the water, and spores resistant to boiling water for 10 hours have been killed in 30 minutes by this addition. This method is suitable for infected instruments or small pieces of infected glassware and also for instruments (such as animal autopsy).
3.Steam at 100ºС:the process of sterilization by intermittent steaming (or boiling) is called Tyndallization.
4.Steam under pressure (high pressure steam): The autoclave or pressure cooker is the instruments used for high pressure steam sterilization. Then steam is placed under pressure in an autoclave. Bacteriological media, surgical instruments are sterilized in the autoclave at 121ºС (15 Ibs) for 15 minutes.

## Slide 3: MOIST HEAT
Sterilization
By
Moist heat
Moist heat at
Below 100˚C
e.g.. pasteurization
Moist heat
At 100˚C
Boiling
Tyndallization
Moist heat
At above 100˚C
Autoclave

## Slide 4
2.Filtration: The principle of this method is to pass the material to be sterilized through special bacterial filters which hold back any bacteria present; the filtrate is thus obtained bacteria free.
This method is used for the sterilization of fluids that do not withstand heating, e.g. sera, Plasma, Vitamins and antibiotic solutions.
Several kinds of bacterial filters are available. The kinds which are most used are the chamborlain and Daulton filters which are made of unglazed porcelain, the Mandler Fillters ,Seitz filters, etc. .
Either positive pressure on the liquid to be filtered should be exerted or negative pressure by sucking from the filtrate container on the filtration in order to enhance the process.
3.Radiation: It is employed commercially for the sterilization of large amount of pre-packed disposable items such as plastic syringes and Catheters that are unable to withstand heat. It is done by applying ultra-violet rays, this process induces thymine dimmer of DNA and this interferes with replication of Micro-organism.

## Slide 5: Autoclaving (At a temperature above 100Co)
Steam under increased pressure, this is called (autoclaving) Under autoclave conditions, pressurize steam KILLS bacterial spore, vegetative cells and other microbial forms.

## Slide 8
What is Autoclave (Sterilization by Steam)?
Sterilization is the destruction of all forms of microbial life, as verified by demonstrating the killing of highly resistant bacterial spores, destroying all microorganisms, both pathogenic and non-pathogenic, including spores and viruses.
Sterilization by steam or autoclaving is one of the most common and widely used methods for sterilization in dental practices. The process refers to a process of instrument sterilization that uses time, temperature and pressure to kill all forms of microbial life, including spores. An autoclave is a pressure chamber, kind of a vessel that uses high-pressure steam to sterilize equipment and supplies.
Autoclaving requires a minimum of 121 degrees celsius (250 degree Fahrenheit) with steam pressure of 15 pounds per square inch (psi), for 15 minutes to ensure sterilization.