## Slide 1
Biochemical Techniques
6th Lecture
Sterilization Techniques
Second Year Students / 2nd semester / 2024-2025
By
Prof. Dr. Naser Abdulhasan Naser
Al-Mustaqbal University
College of Science

## Slide 2
Sterilization: is the killing or removal of all microorganisms(bacteria, viruses, parasites, fungus, protozoan, Helminth including bacterial spores, which are highly resistant).
Surgical instruments that can be damaged by moist heat are usually sterilized by exposure to ethyl oxide gas and most intravenous solution are sterilized by filtration.
Disinfection: is the killing of most, but not all microorganisms, mainly the pathogenic ones. For adequate disinfection, pathogens must be killed but some organisms and bacterial spores may survive.
Disinfectants vary in their tissue-damaging from the corrosive phenol-containing compounds, which should be used only on inanimate objects, to less toxic materials such as ethanol and iodine which can be used on skin surface.
Chemicals used to kill microorganisms on the surface of skin and mucous membrane are called antiseptics.

## Slide 4
Classification of sterilizing agents:
1-physical agents:
heat
Filtration
Radiation.
2- Chemical agents.
Of all the physical agents that exert antimicrobial effects, heat is the most effective. It is an excellent sterilizing agent when applied in appropriate intensity for an adequate period of time, for it effectively stops cellular activates.
Depending on whether it is moist or dry, heat can coagulate cellular proteins (think of a boiled egg) or oxidize cell components (think of a burned finger or a flaming piece of paper).

## Slide 5: STERILIZATION METHODS
VARIOUS METHODS EMPLOYED
CLASSIFICATION
CHEMICAL AGENTS
PHYSICAL AGENTS

## Slide 6
physical mean of sterilization.
1-Heat: Glassware and medium are routinely sterilized by heat. The method depends on the effective oxidation of the microorganisms by carbonization or the coagulation of the protoplasm.
A. Dry Heat:
1. Direct flame: whenever rapid and repeated sterilization is required, the simplest method is direct flaming. This Type of sterilization is used for metal instruments such as platinum wire loop, forceps and scissors etc.
Bunsen burner is commonly used for sterilization by dry heat (direct flame).
2. Hot air: All dry glassware and metal instrument are usually sterilized by this method. Generally, the instruments are left in a Hot Air Oven on a temperature of 160-180ºС for one hour.
3. Incineration: The use of electrically heated or gas-fired incineration filled with forced air blower units provide an excellent means of rapidly destroying articles such as solid dressings, pathological material, animal caresses and bedding.

## Slide 7
FLAMING
A simple & effective method.
Loops or wires, needle , glass slides, cover slips
Instruments held on a Bunsen flame till red-hot.

## Slide 8: flaming

## Slide 9: boiling

## Slide 10: incinerator

## Slide 11
B-moist heat:-
1.pasteurization: uses heat 63ºС at 30 minutes. The organisms such as Brucella or Salmonella and tubercle bacilli which contribute to milk born-disease are readily killed by this process. The alternative method raises the temperature of milk to 72 ºС (161 º F) for 15-20 seconds and is referred to as the flash process. N.T: bacterial spores are not killed by this method.
2.Boiling water: A temperature at 100ºС will kill all non-sporing or vegetative organisms within 10 minutes. Most spores will be killed in 30 minutes at this temperature, but some spores will resist boiling for several hours. The addition of 2% sodium carbonate increases the disinfecting power of the water, and spores resistant to boiling water for 10 hours have been killed in 30 minutes by this addition. This method is suitable for infected instruments or small pieces of infected glassware and also for instruments (such as animal autopsy).
3.Steam at 100ºС:the process of sterilization by intermittent steaming (or boiling) is called Tyndallization.
4.Steam under pressure (high pressure steam): The autoclave or pressure cooker is the instruments used for high pressure steam sterilization. Then steam is placed under pressure in an autoclave. Bacteriological media, surgical instruments are sterilized in the autoclave at 121ºС (15 Ibs) for 15 minutes.

## Slide 12: MOIST HEAT
Sterilization
By
Moist heat
Moist heat at
Below 100˚C
e.g.. pasteurization
Moist heat
At 100˚C
Boiling
Tyndallization
Moist heat
At above 100˚C
Autoclave

## Slide 13
2.Filtration: The principle of this method is to pass the material to be sterilized through special bacterial filters which hold back any bacteria present; the filtrate is thus obtained bacteria free.
This method is used for the sterilization of fluids that do not withstand heating, e.g. sera, Plasma, Vitamins and antibiotic solutions.
Several kinds of bacterial filters are available. The kinds which are most used are the chamborlain and Daulton filters which are made of unglazed porcelain, the Mandler Fillters ,Seitz filters, etc. .
Either positive pressure on the liquid to be filtered should be exerted or negative pressure by sucking from the filtrate container on the filtration in order to enhance the process.
3.Radiation: It is employed commercially for the sterilization of large amount of pre-packed disposable items such as plastic syringes and Catheters that are unable to withstand heat. It is done by applying ultra-violet rays, this process induces thymine dimmer of DNA and this interferes with replication of Micro-organism.

## Slide 14: Autoclaving (At a temperature above 100Co)
Steam under increased pressure, this is called (autoclaving) Under autoclave conditions, pressurize steam KILLS bacterial spore, vegetative cells and other microbial forms.

## Slide 17
What is Autoclave (Sterilization by Steam)?
Sterilization is the destruction of all forms of microbial life, as verified by demonstrating the killing of highly resistant bacterial spores, destroying all microorganisms, both pathogenic and non-pathogenic, including spores and viruses.
Sterilization by steam or autoclaving is one of the most common and widely used methods for sterilization in dental practices. The process refers to a process of instrument sterilization that uses time, temperature and pressure to kill all forms of microbial life, including spores. An autoclave is a pressure chamber, kind of a vessel that uses high-pressure steam to sterilize equipment and supplies.
Autoclaving requires a minimum of 121 degrees celsius (250 degree Fahrenheit) with steam pressure of 15 pounds per square inch (psi), for 15 minutes to ensure sterilization.

## Slide 21
- It depends upon the physical removal of microorganisms by adsorption on the filter medium or by sieving mechanisms.
- It is used for sterilization of heat-sensitive solutions.
Medicinal preparations sterilized by this method are required to undergo severe validation and monitoring since the effectiveness of the filtered product can be greatly influenced by the microbial load in the solution being filtered.
It removes, but does not destroy
M.O.
Commercially available filters are produced with a variety of pore-size specifications (e.g. Millipore filters).
Filtration

## Slide 22
Most filters consist of:
1- diatomaceous earth
2- cellulose acetate or
3- nitrocellulose
  0.45 µm filters removes most
  bacteria
  0.20 µm more inclusive,
  viruses need 0.01 µm
  Useful for sterilizing liquids
  (enzymes, vaccines) that are
  destroyed by heat
Filtration …cont.

## Slide 23
Factors affecting removal of M.O.:
1- Pore size of filter
2- Electrical charge of the filter
and that of the M.O.
3- pH of the solution
4- T, P, and Vacuum applied
  Advantages:
1- Speed
2- Good for thermolabile
materials
3- Inexpensive
4- The complete removal of living
and dead M.O. as well as
other particulate matter from
the solution
Filtration …cont.

## Slide 24
Disadvantages:
1- The membrane is fragile and because of that, it is essential to determine that the assembly was properly made and the membrane was not ruptured
2- Filtration of large volumes of liquids would require more time (particularly if the liquids were viscous)
3- Useful when heat cannot be used and small volumes of liquids.
Filtration …cont.