## Slide 1
Department of Anesthesia Techniques
Electrocardiogram
Dr. Mohammed Sami
Mohammed.sami.hasan@uomus.edu.iq

## Slide 3: Electrical Conduction System of the heart

## Slide 6: ECG
1- Electrocardiography is the process of producing an electrocardiogram (ECG or EKG , a recording of the heart's electrical activity through repeated cardiac cycles.
2- It is an electrogram of the heart which is a graph of voltage versus time of the electrical activity of the heart using electrodes placed on the skin.
3- These electrodes detect the small electrical changes that are a consequence of cardiac muscle depolarization followed by repolarization during each cardiac cycle (heartbeat).

## Slide 7: Limb Lead

## Slide 8: Standard Limb Lead

## Slide 9: Augmented Limb Leads

## Slide 10: Limb Lead
1 - Leads I, II, and III are bipolar leads, which consist of two electrodes of opposite polarity (positive and negative). The third (ground) electrode minimizes electrical activity from other sources.
2 - Leads aVR, aVL, and aVF are unipolar leads and consist of a single positive electrode and a reference point (with zero electrical potential) that lies in the center of the heart’s electrical field.

## Slide 11: Chest Leads

## Slide 13: Components of an ECG Tracing

## Slide 14: Recording of the ECG

## Slide 15: Standerd ECG
ECGs are normally printed on a grid. The horizontal axis represents time and the vertical axis represents voltage. The standard values on this grid are shown in the adjacent image at 25mm/sec:[58]
A small box is 1 mm × 1 mm and represents 0.1 mV × 0.04 seconds. A large box is 5 mm × 5 mm and represents 0.5 mV × 0.20 seconds.

## Slide 17: ECG Fundamentals
Next, report on the fundamental features of the ECG recording itself, namely:
1- Rate 2- Rhythm
  • Supraventricular
  • Ventricular
  • Conduction problems
3- Axis

## Slide 18: ECG Details
Next, review the individual features of the ECG using a step-by-step approach. Describe:
  • P wave
  • PR interval
  • Q wave
  • QRS complex
  • ST segment
  • T wave
  • QT interval
  • U wave

## Slide 19: Heart Rate
Methods for Calculating Heart Rate:
Method 1: Count Large Boxes Regular rhythms can be quickly determined by counting the number of large graph
boxes between two R waves.
* That number is divided into 300 to calculate bpm.
* The rates for the first one to six large boxes can be easily memorized.
* Remember:60sec/mindividedby0.20sec/largebox300largeboxes/min.

## Slide 20: Method 2: Count Small Boxes
Sometimes it is necessary to count the number of small boxes between two R waves for fast heart
rates.
* That number is divided into 1500 to calculate bpm.
* Remember: 60 sec/min divided by 0.04 sec/small box 1500 small boxes/min.
* Examples: If there are six small boxes between two R waves: 1500/6 250 bpm.
* If there are ten small boxes between two R waves: 1500/10 150 bpm

## Slide 21: Methods 1 and 2 for Calculating Heart Rate

## Slide 22: Method 3: Six-Second ECG Rhythm Strip
The best method for measuring irregular rates with varying R-R intervals is to count the number of R waves in a 6-sec strip and multiply by 10
This gives the average number of bpm

## Slide 23: 9- What does an electrocardiogram (ECG or EKG) primarily represent?
  A- Blood pressure changes
  B- Electrical activity of the heart
  C- Cardiac muscle contraction
  D- Oxygen saturation levels
  -E Hormonal fluctuations

## Slide 24: Q 10- All the following are one the properties of the cardiac cells except one
A - Automaticity
B- Excitability
C- Conductivity
D- Temperature regulation
E- Contractility

## Slide 25: Which aspect of the heart is represented by ECG lead III?
A- Inferior
B- Lateral
C- Anterior
D- Posterior
E- septal

## Slide 26: - Regarding Sinus tachyeardia which is true
A- P wave morphology is abnormal
B- The heart rate is less than 100/min
C- Every P wave is not followed by a QRS complex
D- Caused by hypothyroidism
E- Could be caused by ischemia

## Slide 27
Which condition is characterized by a heart rate that increases during inspiration and decreases during expiration?
  A - Sinus arrhythmia
  B- Atrial fibrillation
  C- Atrioventricular nodal
  D- Re-entry tachycardia
  E- Sinus bradycardia
Q What is the main purpose of using 15-ECG leads?
  A- To assess left ventricular function
  B- To evaluate atrial arrhythmias
  C- To monitor ST segment changes in the inferior leads
  D-To assess right ventricle and posterior wall of left ventricle
  E- To diagnose atrial fibrillation