## Slide 1
Al-Mustaqbal University College of Engineering & Technology Computer Engineering Department
Computer Fundamentals
Lecture 2
Basic components of computer system

## Slide 2: Textbooks and Reference Books:
Computer Fundamentals by Pradeep K. Sinha, 6th Edition.
Introduction to Computer by Peter Norton.
Fundamentals of Computers by V. Rajaraman and N. Adabala, 6th Edition.

## Slide 3: What is Computer ?
A computer is a programmable electronic device that accepts raw data as input and processes it with a set of instructions (a program) to produce result as output.
It can process numerical as well as non numerical calculations.
The term “COMPUTER” is derived from the Latin word “COMPUTARE” which means to calculate .

## Slide 4
The activity of processing data using a computer is called data processing
Data processing consists of three sub-activities:
1- Capturing the input data
2- Manipulating the data
3- Managing the output data
In data processing, information is data arranged in an order and form, which is useful to the people who receive it.
Data is raw material used as input and information is processed data obtained as output of data processing

## Slide 5: Characteristics of Computers
1) Automatic: Given a job, computer can work on it automatically without human interventions
2) Speed: Computer can perform data processing jobs very fast, usually measured in microseconds (10-6), nanoseconds (10-9), and picoseconds (10-12)
3) Accuracy: Accuracy of a computer is consistently high, and the degree of its accuracy depends upon its design. Computer errors caused due to incorrect input data or unreliable programs are often referred to as Garbage In-Garbage-Out (GIGO)

## Slide 6
4) Diligence: Computer is free from monotony, tiredness, and lack of concentration. It can continuously work for hours without creating any error and without grumbling
5) Versatility: Computer is capable of performing almost any task, if the task can be reduced to a finite series of logical steps
6) Power of Remembering: Computer can store and recall any amount of information because of its secondary storage capability. It forgets or looses certain information only when it is asked to do so.
7) No I.Q.: A computer does only what it is programmed to do. It cannot take its own decision in this regard
8) No Feelings: Computers are devoid of emotions. Their judgement is based on the instructions given to them in the form of programs that are written by us (human beings)

## Slide 7: Evolution of Computers
Charles Babbage is considered to be the father of
modern digital computers
He designed “Difference Engine” in 1822
He designed a fully automatic analytical engine in
1842 for performing basic arithmetic functions
His efforts established a number of principles that
are fundamental to the design of any digital
compute

## Slide 8: Computer Generations
Generation (Period) | Key hardware technologies | Key software technologies | Key characteristics | Some representative systems
First (1942-1955) | Vacuum tubes Electromagnetic relay memory Punched cards secondary storage | Machine and assembly languages Stored program concept Mostly scientific applications | Bulky in size Highly unreliable Limited commercial use and costly Difficult commercial production Difficult to use | ENIAC EDVAC EDSAC UNIVAC I IBM 701
Second (1955-1964) | Transistors Magnetic cores memory Magnetic tapes Disks for secondary storage | Batch operating system High-level programming languages Scientific and commercial applications | Faster, smaller, more reliable and easier to program than previous generation systems Commercial production was still difficult and costly | Honeywell 400 IBM 7030 CDC 1604 UNIVAC LARC

## Slide 9
Generation (Period) | Key hardware technologies | Key software technologies | Key characteristics | Some rep. systems
Third (1964-1975) | ICs with SSI and MSI technologies Larger magnetic cores memory Larger capacity disks and magnetic tapes secondary storage Minicomputers; upward compatible family of computers | Timesharing operating system تقاسم Standardization of high-level programming languages فصل Unbundling of software from hardware | Faster, smaller, more reliable, easier and cheaper to produce Commercially, easier to use, and easier to upgrade than previous generation systems Scientific, commercial and interactive on- line applications | IBM 360/370 PDP-8 PDP-11 CDC 6600

## Slide 10
Generation (Period) | Key hardware Technologies | Key software technologies | Key characteristics | Some rep. systems
Fourth (1975-1989) | ICs with VLSI technology Microprocessors; semiconductor memory اشباه الموصلات | Operating systems for PCs with GUI and multiple windows on a single terminal screen Multiprocessing OS with concurrent programming languages UNIX operating system with C programming language Object-oriented design and programming كائنية التوجه PC, Network-based, and supercomputing applications | Small, affordable, reliable, and easy to use PCs More powerful and reliable mainframe systems and supercomputers Totally general purpose machines Easier to produce commercially Easier to upgrade Rapid software development possible | IBM PC and its clones Apple II TRS-80
 | Larger capacity hard disks as in-built secondary storage Magnetic tapes and floppy disks as portable storage media |  |  | VAX 9000 CRAY-1 CRAY-2 CRAY-X/MP
 | Personal computers |  |  | 
 | Supercomputers based on parallel vector المتجهprocessing and symmetric multiprocessing technologies |  |  | 
 | Spread of high-speed computer networks انتشار شبكات الكمبيوتر |  |  | 

## Slide 11
Generation (Period) | Key hardware technologies | Key software technologies | Key characteristics | Some rep. systems
Fifth (1989- Present) | ICs with ULSI technology Larger capacity main memory, hard disks with RAID support Optical disks as portable read-only storage media Notebooks, powerful desktop PCs and workstations Powerful servers, supercomputers Internet Cluster computing العنقودية | Micro-kernel based, multithreading, distributed OS نظام تشغيل موزع متعدد الخيوط، قائم على نواة دقيقة، برمجة متوازية Parallel programming libraries like MPI & PVM JAVA World Wide Web Multimedia, Internet applications More complex supercomputing applications | Portable computers Powerful, cheaper, reliable, and easier to use desktop machines Powerful supercomputers High uptime due to hot-pluggable components وقت تشغيل مرتفع بسبب المكونات القابلة للتوصيل السريع Totally general purpose machines Easier to produce commercially, easier to upgrade Rapid software development possible | IBM notebooks Pentium PCs SUN Workstations IBM SP/2 SGI Origin 2000 PARAM 10000

## Slide 12: Electronic Devices Used in Computers of Different Generations
A Vacuum Tube
A Transistor
  An IC Chip

## Slide 13: The Five Basic Operations of a Computer System
Inputting
Inputting. The process of entering data and instructions into the computer system
Storing
Storing. Saving data and instructions to make them readily available for initial or additional processing whenever required
Processing
Processing. Performing arithmetic operations (add, subtract, multiply, divide, etc.) or logical operations (comparisons like equal to, less than, greater than, etc.) on data to convert them into useful information
Outputting
Outputting. The process of producing useful information or results for the user such as a printed report or visual display
Controlling
Controlling. Directing the manner and sequence in which all of the above operations are performed

## Slide 14
Central Processing Unit (CPU)
Storage Unit
Secondary Storage
Primary Storage
Control Unit
Arithmetic Logic Unit
Input Unit
Output Unit
Program and Data
Information (Results)
Indicates flow of instructions and data
Indicates the control exercised by the control unit
Basic Organization/Components of a Computer System

## Slide 15
Input Unit
An input unit of a computer system performs the following functions:
It accepts (or reads) instructions and data from outside world
It converts these instructions and data in computer acceptable form
It supplies the converted instructions and data to the computer system for further processing

## Slide 16
Output Unit
An output unit of a computer system performs the following functions:
It accepts the results produced by the computer, which are in coded form and hence, cannot be easily understood by us
It converts these coded results to human acceptable (readable) form
It supplies the converted results to outside world

## Slide 17: Storage Unit
The storage unit of a computer system holds (or stores) the following :
Data and instructions required for processing (received from input devices)
Intermediate results of processing
Final results of processing, before they are released to an output device

## Slide 18: Two Types of Storage
Primary storage
  Used to hold running program instructions
  Used to hold data, intermediate results, and results of ongoing processing of job(s)
  Fast in operation
  Small Capacity
  Expensive
  Volatile (looses data on power dissipation)

## Slide 19: Two Types of Storage
Secondary storage
  Used to hold stored program instructions
  Used to hold data and information of stored jobs
  Slower than primary storage
  Large Capacity
  Cheaper than primary storage
  Retains data even without power

## Slide 20
Arithmetic Logic Unit (ALU)
Arithmetic Logic Unit of a computer system is the place where the actual executions of instructions takes place during processing operation

## Slide 21
Control Unit
Control Unit of a computer system manages and coordinates the operations of all other components of the computer system

## Slide 22
Central Processing Unit (CPU)
Arithmetic Logic Unit (ALU)
Control Unit (CU)
=
Central Processing Unit (CPU)
+
It is the brain of a computer system
It is responsible for controlling the operations of all other units of a computer system

## Slide 23
The System Concept
A system has following three characteristics:
A system has more than one element
All elements of a system are logically related
All elements of a system are controlled in a manner to achieve the system goal
A computer is a system as it comprises of integrated components (input unit, output unit, storage unit, and CPU) that work together to perform the steps called for in the executing program