## Slide 1
Al-Mustaqbal University College of Engineering & Technology Computer Engineering Department
Computer Fundamentals
Lecture 3
Fundamentals of Computer Architecture

## Slide 2: The von Neumann Model
The invention of stored-program computers is credited to mathematician John von Neumann, who lived during the same time period as Mauchley and Eckert.
Stored-program computers have become known as von Neumann Architecture systems.

## Slide 3: Central Processing Unit (CPU)
The CPU consists of the following features:
  CPU is considered as the brain of the computer.
  CPU performs all types of data processing operations.
  It stores data, intermediate results, and instructions (programs).
  It controls the operation of all parts of the computer.
Notes: Just like the brain controls all functions of the body, the CPU controls all operations of the computer, such as executing programs and managing resources.
For example, when you type on a keyboard, the CPU processes the keystrokes and displays them on the screen.
When you save a document, the CPU stores the data on the computer's hard drive. Similarly, when running a calculation, the CPU stores intermediate results in its memory.
For instance, when you click on an icon to open a program, the CPU coordinates with other components like the memory and storage to execute the program and display it on the screen.

## Slide 4: CPU Block Diagram

## Slide 5: CPU Phases
Memory Unit
Control Unit
ALU Unit

## Slide 6: Memory Unit
This unit can store instructions, data, and intermediate results.
It supplies information to the other units of the computer when needed.
It is also known as the internal storage unit, main memory, primary storage, or random access memory (RAM).
Its size affects speed, power, and capability. Primary memory and secondary memory are two types of memories in the computer.

## Slide 7: Memory Unit
Functions of the memory unit are:
  It stores all the data and instructions required for processing.
  It stores intermediate results of processing.
  It stores final results of processing before these results are released to an output device.
  All inputs and outputs are transmitted through main memory.

## Slide 8: Memory Classification

## Slide 9: Random Access Memory (RAM)
RAM is a type of computer memory that stores data temporarily. It allows the processor to quickly access the data it needs.
RAM is volatile, meaning it loses its stored data when the power is turned off.
Data in RAM is stored randomly, and the processor can access it in any order.
RAM typically holds data from the computer's operating system and applications.
When you turn off the computer, RAM loses all its stored information, but data remains on the hard disk.
Some of the earliest computers used delay-line format of computer storage. Most modern computers use an embedded RAM circuitry on the motherboard which reads data in bursts.
So, modern RAM devices are not random memory devices as such; they are burst memory access devices, but the term RAM has stuck in everyday usage.

## Slide 10: Random Access Memory (RAM)
There are mainly two types of RAM: Static RAM (SRAM) and Dynamic RAM (DRAM).

## Slide 11: Static Random Access Memory (SRAM)
The term "static" means it does not need to be periodically refreshed, SRAM uses bistable latching circuitry (i.e., flip-flops) to store each bit. Each bit is stored as a voltage.
Each memory cell requires six transistors, giving the chip low density but high speed.
However, SRAM is still volatile in the conventional sense that data is lost when powered down.
Disadvantages include being more expensive and consuming more power than DRAM.
In high-speed processors, such as Pentium, SRAM is known as cache memory and is included on the processor chip.
However, additional high-speed cache memory is sometimes added externally to the processor to improve total performance.

## Slide 12: Dynamic Random Access Memory (DRAM)
DRAM has a structural advantage over SRAM: it only requires one transistor (MOSFET gates) and a capacitor to store each bit, compared to six transistors in SRAM.
This simplicity allows DRAM to achieve very high density, meaning it can store a lot of data in a small space.
Additionally, DRAM consumes less power and is often cheaper than SRAM (Except when the system size is less than 8 kilobytes).
The disadvantage, DRAM stores bit information as electrical charge, which gradually leaks away over time.
To prevent data loss, DRAM needs to be refreshed every few milliseconds. This refreshing process requires extra circuitry, adding to the overall cost of the system.
Notes: DRAM stores data as electrical charge in its memory cells, but this charge gradually leaks away over time. To prevent data loss, DRAM requires periodic refreshing, where the stored data is read and immediately rewritten. This process adds extra circuitry and cost to the system.

## Slide 13: Read-Only Memory (ROM)
(ROM) serves as nonvolatile memory found in computers and electronic devices.
Often referred to as firmware, ROM is an integrated circuit pre-programmed with specific data during production.
Essential startup instructions for computers are embedded within ROM chips.
ROM chips are not exclusive to computers but are also utilized in various electronic gadgets.
Data stored in ROM cannot be changed, ensuring permanent and secure storage
Notes: DRAM stores data as electrical charge in its memory cells, but this charge gradually leaks away over time. To prevent data loss, DRAM requires periodic refreshing, where the stored data is read and immediately rewritten. This process adds extra circuitry and cost to the system.

## Slide 14: Read-Only Memory (ROM)
However, a manufacturing error renders a ROM chip unusable, with template creation being the most expensive phase.
Duplicating ROM chips is straightforward and budget-friendly when a template is accessible.
Unlike volatile memory, ROM retains data even when the power is off.
ROM operates at electronic speeds and is considered a semiconductor memory.
For instance, the BIOS (Basic Input/Output System) in computers is often stored in ROM, ensuring essential startup functions are readily available.
Notes: DRAM stores data as electrical charge in its memory cells, but this charge gradually leaks away over time. To prevent data loss, DRAM requires periodic refreshing, where the stored data is read and immediately rewritten. This process adds extra circuitry and cost to the system.

## Slide 15: Examples of ROM
Notes: DRAM stores data as electrical charge in its memory cells, but this charge gradually leaks away over time. To prevent data loss, DRAM requires periodic refreshing, where the stored data is read and immediately rewritten. This process adds extra circuitry and cost to the system.

## Slide 16: ROM Classification
Notes: DRAM stores data as electrical charge in its memory cells, but this charge gradually leaks away over time. To prevent data loss, DRAM requires periodic refreshing, where the stored data is read and immediately rewritten. This process adds extra circuitry and cost to the system.

## Slide 17: Programmable Read-Only Memory (PROM)
PROM, a memory chip on which data can be written only once.
Once a program has been written onto a PROM, it remains there forever. Unlike RAM, PROMs retain their contents when the computer is turned off.
The difference between a PROM and a ROM is that a PROM is manufactured as blank memory, whereas a ROM is programmed during the manufacturing process.
To write data onto a PROM chip, you need a special device called a PROM programmer or PROM burner.
The process of programming a PROM is sometimes called burning the PROM.
Notes: DRAM stores data as electrical charge in its memory cells, but this charge gradually leaks away over time. To prevent data loss, DRAM requires periodic refreshing, where the stored data is read and immediately rewritten. This process adds extra circuitry and cost to the system.

## Slide 18: Erasable Programmable Read-Only Memory (EPROM)
EPROM is a special type of memory that retains its contents until it is exposed to ultraviolet light.
The ultraviolet light clears its contents, making it possible to reprogram the memory.
To write to and erase an EPROM, you need a special device called a PROM programmer or PROM burner.
Notes: DRAM stores data as electrical charge in its memory cells, but this charge gradually leaks away over time. To prevent data loss, DRAM requires periodic refreshing, where the stored data is read and immediately rewritten. This process adds extra circuitry and cost to the system.

## Slide 19: Electrically Erasable Programmable Read-Only Memory (EEPROM)
EEPROM, which stands for Electrically Erasable Programmable Read-Only Memory, is a special type of PROM.
EEPROM can be erased by exposing it to an electrical charge.
Like other types of PROM, EEPROM retains its contents even when the power is turned off.
However, EEPROM is not as fast as RAM.
Notes: DRAM stores data as electrical charge in its memory cells, but this charge gradually leaks away over time. To prevent data loss, DRAM requires periodic refreshing, where the stored data is read and immediately rewritten. This process adds extra circuitry and cost to the system.

## Slide 20: Cache Memory
Also known as CPU memory, is random access memory (RAM) that a computer microprocessor can access more quickly than regular RAM. This memory is typically integrated directly with the CPU chip or placed on a separate chip that has a separate bus interconnect with the CPU.

## Slide 21: Cache Memory
The basic purpose of cache memory is to store program instructions that are frequently referenced by software during operation.
Fast access to these instructions increases the overall speed of the software program.
As the microprocessor processes data, it first looks in the cache memory. If it finds the instructions there from a previous reading of data, it does not have to perform a more time-consuming reading of data from larger memory or other data storage devices.
Most programs use very few resources once they have been opened and operated for a time, mainly because frequently referenced instructions tend to be cached.
This explains why measurements of system performance in computers with slower processors but larger caches tend to be faster than measurements of system performance in computers with faster processors but more limited cache space.
Multi-tier or multilevel caching has become popular in server and desktop architectures, with different levels providing greater efficiency through managed tiering.
Notes: - For example, frequently used mathematical functions or common commands in an operating system.
- For instance, if a web browser needs to render a webpage, accessing cached images and scripts can significantly speed up the loading time.
- An example would be a video game accessing cached textures or game assets during gameplay.
- For instance, in a word processing program, commonly used formatting options may be cached to speed up document editing.
- For example, a computer with a slower CPU but a larger cache may perform better in tasks involving repetitive calculations or data processing.
- An example would be a server system with multiple levels of cache memory, each catering to different types of data access patterns for improved performance.

## Slide 22: Control Unit
This unit controls the operations of all parts of the computer but does not carry out any actual data processing operations. Its functions include:
  It is responsible for controlling the transfer of data and instructions among other units of a computer.
  It manages and coordinates all the units of the computer.
  It obtains the instructions from the memory, interprets them, and directs the operation of the computer.
  It communicates with input/output devices for the transfer of data or results from storage.
  It does not process or store data.
Notes: - For example, frequently used mathematical functions or common commands in an operating system.
- For instance, if a web browser needs to render a webpage, accessing cached images and scripts can significantly speed up the loading time.
- An example would be a video game accessing cached textures or game assets during gameplay.
- For instance, in a word processing program, commonly used formatting options may be cached to speed up document editing.
- For example, a computer with a slower CPU but a larger cache may perform better in tasks involving repetitive calculations or data processing.
- An example would be a server system with multiple levels of cache memory, each catering to different types of data access patterns for improved performance.

## Slide 23: Arithmetic Logic Unit
An ALU, is an integrated circuit within a CPU or GPU that performs arithmetic and logic operations. Its tasks include:
  Addition
  Subtraction
  Shifting operations
  Boolean comparisons such as AND, OR, XOR, and NOT operations

## Slide 24: Arithmetic Logic Unit
ALUs are designed for integer calculations and commonly handle multiplication as well. However, they typically do not perform division operations due to potential fraction or floating-point results. Instead, division operations are managed by the Floating-Point Unit (FPU), which also handles non-integer calculations. While the ALU is a fundamental component of all processors, its design and functionality may vary among different processor models. For example:
  Some ALUs only perform integer calculations.
  Others are designed to handle floating-point operations as well.
  Some processors contain a single ALU, while others include several arithmetic logic units that work together to perform calculations.

## Slide 25
Thank You for Listening Questions ?