## Slide 1: Ministry of Higher Education and Scientific Research Al-Mustaqbal University Radiology Techniques Department
The Lower Limbs
Radiography
BY
A.T. Mustafa Kh. Alhussainy

## Slide 2: Toes : AP
Position
Supine or seated on table with knee flexed, plantar surface of foot resting on ID, CR angled 10°–15° to calcaneus
Direction and Centering of the X-ray Beam
The vertical central ray is directed over the third metatarsophalangeal joint, perpendicular to the cassette if all the toes are to be imaged.
For single toes, the vertical ray is centered over the metatarsophalangeal joint of the individual toe and collimated to include the toe either side.
ID: 8*10” , Out Bucky
SID: 40″ (100cm)

## Slide 3: Toes : AP

## Slide 4: Toes : Oblique
Position of Patient and Cassette
From the basic dorsi-plantar position (AP), the affected limb is allowed to lean medially to bring the plantar surface of the foot approximately 45 degrees to the cassette.
A 45-degree non-opaque pad is placed under the side of the foot for support, with the opposite leg acting as a support.
Direction and Centering of the X-ray Beam
The vertical ray is centered over the first metatarso-phalangeal joint if all the toes are to be imaged and angled sufficiently to allow the central ray to pass through the third metatarsophalangeal joint.
For single toes, the vertical ray is centered over the metatarsophalangeal joint of the individual toe, perpendicular to the cassette.
SID: 40″ (100 cm)
ID: 8*10” , Out Bucky

## Slide 5: Toes : Oblique

## Slide 6: Toes : Lateral
Position of Patient and Cassette
The patient lies on the table, and the medial aspect of the affected leg and foot is placed in contact with the table.
The cassette is placed under the foot to include the phalanges of the Toes and the distal part of the first metatarsal.
Direction and Centering of the X-ray Beam
Centre with the vertical ray perpendicular to the cassette, over the first metatarso-phalangeal joint.
SID: 40” (100cm).
ID: 8*10” , Out Bucky

## Slide 7
Toes : Lateral

## Slide 8: Toes : Sesamoids Axial
Position of Patient and Cassette
There is a choice of two positions for this projection:
1: The patient is positioned as for the lateral projection of the foot. The foot is raised on a support and the cassette is supported vertically and well into the instep. A horizontal beam is used in this case.
2: The patient sits on the X-ray table, with legs extended. The hallux is then dorsiflexed with the aid of a bandage and held by the patient. The cassette is raised on a support and positioned firmly against the instep.
Direction and Centering of the X-ray beam
Centre to the sesamoid bones with the central ray projected tangentially to the first metatarso-phalangeal joint.
SID: 40” (100cm).
ID: 8*10” , Out Bucky

## Slide 9: Sesamoids

## Slide 10: Sesamoids

## Slide 11: Foot :AP
Position of Patient and Cassette
The patient is seated on the X-ray table, supported, if necessary, with the affected hip and knee flexed.
The plantar aspect of the affected foot is placed on the cassette and the lower leg is supported in the vertical position by the other knee.
Alternatively, the cassette can be raised on a 15-degrees foam pad for ease of positioning.
Direction and Centering of the X-ray Beam
The central ray is directed over the cuboid-navicular joint, midway between the palpable navicular tuberosity and the tuberosity of the fifth metatarsal.
The X-ray tube is angled 15 degrees cranially when the cassette is flat on the table.
The X-ray tube is vertical when the cassette is raised on a 15-degree pad.
SID: 40″ (100 cm).
ID: 10*12” , Out Bucky

## Slide 12: Foot :AP

## Slide 13: Foot : Oblique
Position of Patient and Cassette
From the basic dorsi-plantar position, the affected limb is allowed to lean medially to bring the plantar surface of the foot approximately 30–45 degrees to the cassette.
A non-opaque angled pad is placed under the foot to maintain the position, with the opposite limb acting as a support.
Direction and Centering of the X-ray Beam
The vertical central ray is directed over the cuboid-navicular joint.
SID: 40” (100cm)
ID: 10*12”, ,Out Bucky

## Slide 14: Foot : Lateral
Position of Patient and Cassette
From the dorsi-plantar position, the leg is rotated outwards to bring the lateral aspect of the foot in contact with the cassette.
A pad is placed under the knee for support.
The position of the foot is adjusted slightly to bring the plantar aspect perpendicular to the cassette.
Direction and Centering of the X-ray Beam
The vertical central ray is centered over the navicular cuneiform joint.
SID: 40” (100cm)
ID: 10*12”, ,Out Bucky

## Slide 15
Foot : Lateral & Oblique

## Slide 16: Calcaneus : Axial
Position of Patient and Cassette
The patient sits or lies supine on the X-ray, table with both limbs extended.
The affected leg is rotated medially until both malleoli are equidistant from the film.
The ankle is dorsiflexed The position is maintained by using a bandage strapped around the forefoot and held in position by the patient.
The cassette is positioned with its lower edge just distal to the plantar aspect of the heel.
Direction and Centering of the X-ray Beam
Centre to the plantar aspect of the heel at the level of the tubercle of the fifth metatarsal.
The central ray is directed cranially at an angle of 40 degrees to the plantar aspect of the heel.
SID: 40” (100cm)
ID: 8*10”, Out Bucky

## Slide 17: Calcaneus : Axial

## Slide 18: Calcaneus : Lateral
Position of Patient and Cassette
From the supine position, the patient rotates on to the affected side.
The leg is rotated until the medial and lateral malleoli are superimposed vertically.
A 15-degree pad is placed under the anterior aspect of the knee and the lateral border of the forefoot for support.
The cassette is placed with the lower edge just below plantar aspect of the heel.
Direction and Centering of the X-ray Beam
Centre 2.5 cm distal to the medial malleolus, with the vertical central ray perpendicular to the cassette.
SID: 40” (100cm)
ID: 8*10”, Out Bucky

## Slide 19: Calcaneus : Lateral

## Slide 20: Ankle : AP
Position of Patient and Cassette
The patient is either supine or seated on the X-ray table with both legs extended.
A pad may be placed under the knee for comfort.
The lower edge of the cassette is positioned just below the plantar aspect of the heel.
Direction and Centering of the X-ray Beam
Centre midway between the malleoli with the vertical central ray at 90 degrees to an imaginary line joining the malleoli.
SID: 40” (100cm)
ID: 8*10”, Out Bucky

## Slide 21: Ankle : AP

## Slide 22: Ankle : Mortise
Position of Patient and Cassette
The patient is either supine or seated on the X-ray table with both legs extended.
A pad may be placed under the knee for comfort.
The affected ankle is supported in dorsiflexion by a firm 90-degree pad placed against the plantar aspect of the foot.
The limb is rotated medially (approximately 20 degrees) until the medial and lateral malleoli are equidistant from the cassette.
The lower edge of the cassette is positioned just below the plantar aspect of the heel.
Direction and Centering of the X-ray Beam
Centre midway between the malleoli with the vertical central ray at 90 degrees to an imaginary line joining the malleoli.
SID: 40” (100cm)
ID: 8*10”, Out Bucky

## Slide 23: Ankle : Mortise

## Slide 24: Ankle : Lateral
Position of Patient and Cassette
With the ankle dorsiflexed, the patient turns on to the affected side until the malleoli are superimposed vertically and the tibia is parallel to the cassette.
Direction and Centering of the X-ray Beam
Centre over the medial malleolus, with the central ray at right-angles to the axis of the tibia.
SID: 40” (100cm)
ID: 8*10”, Out Bucky

## Slide 25: Ankle : Lateral

## Slide 26: Ankle : Oblique
Position of Patient and Cassette
The patient lies supine on the X-ray table with the affected limb extended.
The ankle joint is dorsiflexed and the malleoli are equidistant from the film.
The leg is internally rotated through 45 degrees.
A pad is placed under the knee for support.
The lower edge of the cassette is placed at the level of the plantar aspect of the heel.
Direction and Centering of the X-ray Beam
Centre 2.5 cm distal to the lateral malleolus with the following cranial angulations:
10 degrees Posterior part of the posterior articulation.
20–30 degrees Middle part of the posterior articulation and the middle articulation.
40 degrees Anterior part of the posterior articulation.
SID: 40” (100cm)
ID: 8*10”, Out Bucky

## Slide 27: Ankle : Oblique

## Slide 28: Leg (Tibia-Fibula): AP
Position of Patient and Cassette
The patient is either supine or seated on the X-ray table, with both legs extended.
The ankle is supported in dorsiflexion by a firm 90-degree pad placed against the plantar aspect of the foot.
The limb is rotated medially until the medial and lateral malleoli are equidistant from the cassette.
The lower edge of the cassette is positioned just below the plantar aspect of the heel.
Direction and Centering of the X-ray Beam
Midway between The Knee Joint and the Ankle Joint.
SID: 40” (100cm)
ID: 14*17”, Out Bucky

## Slide 29: Leg (Tibia-Fibula): AP

## Slide 30: Leg : Lateral
Position of Patient and Cassette
From the supine/seated position, the patient rotates on to the affected side.
The leg is rotated further until the malleoli are superimposed vertically.
The tibia should be parallel to the cassette.
pad is placed under the knee for support.
The lower edge of the cassette is positioned just below the plantar aspect of the heel.
Direction and Centering of the X-ray Beam
Midway between The Knee Joint and the Ankle Joint.
SID: 40” (100cm)
ID: 14*17”, Out Bucky

## Slide 31: Lateral Leg (Tibia-Fibula)

## Slide 32: Knee : AP
Position of Patient and Cassette
The patient is either supine or seated on the X-ray table, with both legs extended.
The affected limb is rotated to centralize the patella between the femoral condyles, and sandbags are placed against the ankle to help maintain this position.
The cassette should be in close contact with the posterior aspect of the knee joint, with its center level with the upper borders of the tibial condyles.
Direction and Centering of the X-ray Beam
Centre 2.5 cm below the apex of the patella through the joint space, with the central ray at 90 degrees to the long axis of the tibia.
SID: 40” (100cm)
ID: 8*10”, Out Bucky

## Slide 33: Knee : AP

## Slide 34: Knee : Lateral
Position of Patient and Cassette
The patient lies on the side to be examined, with the knee flexed at 90 degrees.
The other limb is brought forward in front of the one being examined and supported on a sandbag.
A sandbag is placed under the ankle of the affected side to bring the long axis of the tibia parallel to the cassette.
The position of the limb is now adjusted to ensure that the femoral condyles are superimposed vertically.
The center of the cassette is placed level with the medial tibial condyle.
Direction and Centering of the X-ray Beam
Centre to the middle of the superior border of the medial tibial condyle, with the central ray at 90 degrees to the long axis of the tibia.
SID: 40” (100cm)
ID: 8*10”, Out Bucky

## Slide 35: Knee : Lateral

## Slide 36: Knee: Skyline View
Position of Patient and Cassette
The patient lies prone on the X-ray table, with the cassette placed under the knee joint and the knee flexed through 90 degrees.
A bandage placed around the ankle and either tethered to a vertical support or held by the patient may prevent unnecessary movement.
Direction and Centering of the X-ray Beam
Centre behind the patella, with the vertical central ray angled approximately 15 degrees towards the knee, avoiding the toes.
SID: 40” (100cm)
ID: 8*10”, Out Bucky

## Slide 37
Knee: Skyline View

## Slide 39: Knee: Skyline View

## Slide 40: Knee: Skyline View

## Slide 41: Femur: AP
Position of Patient and Cassette
The patient lies supine on the X-ray table, with both legs extended.
The affected limb is rotated to centralize the patella over the femur.
Sandbags are placed below the knee to help maintain the position.
The cassette is positioned in the Bucky tray immediately under the limb, adjacent to the posterior aspect of the thigh to include both the hip and the knee joints.
Alternatively, the cassette is positioned directly under the limb, against the posterior aspect of the thigh to include the knee joint.
Direction and Centering of the X-ray Beam
Centre to the middle of the cassette, with the vertical central ray at 90 degrees on the midway between Hip joint and Knee joint.
SID: 40” (100cm)
ID: 14*17”, In Bucky or Out Bucky

## Slide 43: Femur: Lateral
Position of Patient and Cassette
From the AP position, the patient rotates on to the affected side, and the knee is slightly flexed.
The pelvis is rotated backwards to separate the thighs.
The position of the limb is then adjusted to vertically superimpose the femoral condyles.
Pads are used to support the opposite limb behind the one being examined.
The cassette is positioned in the Bucky tray under the lateral aspect of the thigh to include the knee joint and as much of the femur as possible.
Alternatively, the cassette is positioned directly under the limb, against the lateral aspect of the thigh, to include the knee joint.
Direction and Centering of the X-ray Beam
Centre to the middle of the cassette, with the vertical central ray parallel to the imaginary line joining the femoral condyles.
SID: 40” (100cm)
ID: 14*17”, In Bucky or Out Bucky

## Slide 46: Hip : AP
Position of Patient and Cassette
The patient lies supine and symmetrical on the X-ray table, with the median sagittal plane perpendicular to the tabletop.
The midline of the patient must coincide with the centered primary beam and table Bucky mechanism.
If the patient remains on a trolley, ideally, they should be positioned down the midline and adjusted to achieve an optimum projection dependent on their degree of mobility.
To avoid pelvic rotation, the anterior superior iliac spines must be equidistant from the tabletop. A non-opaque pad placed under a buttock can be used to make the pelvis level. The coronal plane should now be parallel to the tabletop.
The limbs are slightly abducted and internally rotated to bring the femoral necks parallel to the cassette.
Sandbags and pads are placed against the ankle region to help maintain this position.

## Slide 47: Hip : AP
Direction and Centering of the X-ray Beam
Centre in the midline, with a vertical central beam.
The center of the cassette is placed midway between the upper border of the symphysis pubis and anterior superior iliac spine for the whole of the pelvis and proximal femora.
The upper edge of the cassette should be 5 cm above the upper border of the iliac crest to compensate for the divergent beam and to ensure that the whole of the bony pelvis is included.
The center of the cassette is placed level with the upper border of the symphysis pubis for the hips and upper femora.
SID: 40” (100cm)
ID: 14*17”, In Bucky

## Slide 49: Hip : Lateral
Warning: Do not attempt with possible fracture of hip area.
Position of Patient and Cassette
The patient lies supine on the X-ray table, with the legs extended. The median sagittal plane coincides with the long axis of the table Bucky.
The patient rotates through 45 degrees on to the affected side, with the hip abducted 45 degrees and flexed 45 degrees, and is supported in this position by non-opaque pads.
The knee is flexed to bring the lateral aspect of the thigh into contact with the tabletop. The knee falls into a lateral position.
The opposite limb is raised and supported behind the limb being examined.
Direction and Centering of the X-ray Beam
Centre to the femoral pulse in the groin of the affected side, with the central ray perpendicular to the cassette.
The long axis of the primary beam is adjusted by turning the light beam diaphragm (LBD) to coincide with the long axis of the femur.
The primary beam needs to be collimated to the area under examination.
SID: 40” (100cm)
ID: 10*12” , In Bucky

## Slide 50: Hip : Lateral

## Slide 51: Hips: Lateral (Frog’s Legs Position)
Position
No rotation evident by symmetry of pelvic bones.
Lesser trochanters equal in size.
Minimal distortion of femoral neck.
Greater trochanters superimposed over femoral necks.
SID: 40” (100cm)
ID: 14*17”, In Bucky

## Slide 52: Hips: Lateral (Frog’s Legs Position)

## Slide 53: Pelvis : AP

## Slide 55: Pelvis : AP