## Slide 1: Fluorescent Microscopy
What Is Fluorescent Microscopy?

## Slide 2
A fluorescence microscope is an optical microscope that uses fluorescence and phosphorescence instead of, or in addition to, reflection and absorption to study organic or inorganic substances.
Fluorescence is the emission of light by a substance that has absorbed light or other electromagnetic radiation.
The fluorescence microscope was devised in the early part of the twentieth century by August Köhler, Carl Reichert, and Heinrich Lehmann.

## Slide 4
Principle of Fluorescence Microscopy
Most cellular components are colorless and cannot be clearly distinguished under a microscope. The basic premise of fluorescence microscopy is to stain the components with dyes.
Fluorescent dyes, also known as fluorophores or fluorochromes, are molecules that absorb excitation light at a given wavelength (generally UV), and after a short delay emit light at a longer wavelength.

## Slide 5
The emission light can then be filtered from the excitation light to reveal the location of the fluorophores.
Fluorescence microscopy uses a much higher intensity light to illuminate the sample. This light excites fluorescence species in the sample, which then emit light of a longer wavelength.
The image produced is based on the second light source or the emission wavelength of the fluorescent species rather than from the light originally used to illuminate, and excite, the sample

## Slide 6
Parts of Fluorescence Microscope
1- Fluorescent dyes (Fluorophore)
  A fluorophore is a fluorescent chemical compound that can re-emit light upon light excitation.
  Fluorophores typically contain several com
  bined aromatic groups, or plane or cyclic molecules with several π bonds.
  Many fluorescent stains have been designed for a range of biological molecules.
  Some of these are small molecules that are intrinsically fluorescent and bind a biological molecule of interest. Major examples of these are nucleic acid stains like DAPI and Hoechst, phalloidin which is used to stain actin fibers in mammalian cells.

## Slide 7
2- A light source
  Four main types of light sources are used, including xenon arc lamps or mercury-vapor lamps with an excitation filter, lasers, and high- power LEDs.
  Lasers are mostly used for complex fluorescence microscopy techniques, while xenon lamps, and mercury lamps, and LEDs with a dichroic excitation filter are commonly used for wide-field epifluorescence microscopes.
3-The excitation filter
  The exciter is typically a bandpass filter that passes only the wavelengths absorbed by the fluorophore, thus minimizing the excitation of other sources of fluorescence and blocking excitation light in the fluorescence emission band.

## Slide 8
4- The dichroic mirror
  A dichroic filter or thin-film filter is a very accurate color filter used to selectively pass light of a small range of colors while reflecting other colors.
5-The emission filter.
  The emitter is typically a bandpass filter that passes only the wavelengths emitted by the fluorophore and blocks all undesired light outside this band – especially the excitation light.
  By blocking unwanted excitation energy (including UV and IR) or sample and system autofluorescence, optical filters ensure the darkest background.

## Slide 9
Applications of Fluorescence Microscope
To identify structures in fixed and live biological samples.
Fluorescence microscopy is a common tool for today’s life science research because it allows the use of multicolor staining, labeling of structures within cells, and the measurement of the physiological state of a cell.

## Slide 10: Electron microscope
Electron microscope definition:- An electron microscope is a microscope that uses a beam of accelerated electrons as a source of illumination.
It is a special type of microscope having a high resolution of images, able to magnify objects in nanometres, which are formed by controlled use of electrons in vacuum captured on a phosphorescent screen.
Ernst Ruska (1906-1988), a German engineer and academic professor, built the first Electron Microscope in 1931, and the same principles behind his prototype still govern modern EMs.

## Slide 12: Principle of Electron microscope
1- The electron gun generates electrons.
2-Two sets of condenser lenses focus the electron beam on the specimen and then into a thin tight beam.
3-To move electrons down the column, an accelerating voltage (mostly between 100 kV-1000 kV) is applied between tungsten filament and anode.
4-The specimen to be examined is made extremely thin, at least 200 times thinner than those used in the optical microscope. Ultra-thin sections of 20-100 nm are cut which is already placed on the specimen holder.

## Slide 13
5-The electronic beam passes through the specimen and electrons are scattered depending upon the thickness or refractive index of different parts of the specimen.
6-The denser regions in the specimen scatter more electrons and therefore appear darker in the image since fewer electrons strike that area of the screen.
7-The electron beam coming out of the specimen passes to the objective lens, which has high power and forms the intermediate magnified image.
8-The ocular lenses then produce the final further magnified image.

## Slide 14: Types of Electron microscope
1- The transmission electron microscope (TEM)
The transmission electron microscope is used to view thin specimens through which electrons can pass generating a projection image.
TEM is used, among other things, to image the interior of cells (in thin sections), the structure of protein molecules (contrasted by metal shadowing.

## Slide 15: The scanning electron microscope (SEM)
Conventional scanning electron microscopy depends on the emission of secondary electrons from the surface of a specimen.
Because of its great depth of focus, a scanning electron microscope is the EM analog of a stereo light microscope.
TEM. It can also be used for particle counting and size determination, and for process control.
It is termed a scanning electron microscope because the image is formed by scanning a focused electron beam onto the surface of the specimen in a raster pattern

## Slide 17: Parts of Electron microscope
1- Electron gun
2- Electromagnetic lenses
3- Specimen Holder
4- Image viewing and Recording System

## Slide 18: Applications
1-Electron microscopes are used to investigate the ultrastructure of a wide range of biological and inorganic specimens including microorganisms, cells, large molecules.
2-Industrially, electron microscopes are often used for quality control and failure analysis.
3-Modern electron microscopes produce electron micrographs using specialized digital cameras and frame grabbers to capture the images.
4-. Study of microorganisms like bacteria, virus and other pathogens .

## Slide 19: Cleaning the Eyepieces
  1-Turn off the microscope- .
  2-Unplug the microscope from power source- .
  3-Remove dust before wiping lens Clean the eyepieces with a cotton swab
  4-moistened - with lens cleaning solution Wipe in a circular motion inside out
  5-Dry with lens
  6- cleaning and drying if required.

## Slide 20: Replacing the Microscope Bulb
Replacing the Microscope Bulb
-Turn off the microscope
-Unplug the microscope from power source
-Find location of bulb
-Follow manufacturer’s instructions to remove the – bulb

## Slide 21: Maintenance of Microscope
Maintenance of Microscope:-
1-Never disassemble the microscope as doing so may cause electric shock or damage to the microscope.
2- Allow the halogen bulbs to cool before touching. Halogen bulbs become hot and may cause burns if touched.
3-To avoid electric shock or damage to the instrument, unplug the microscope before replacing the bulb.
4-Use only the halogen or fluorescent bulb
5-Turn off and unplug the microscope before moving.

## Slide 22
Storage of Microscope:-
1- Always cover the microscope with the supplied dust cover when not in use
2-Store in a dry place
3- In humid or moist environments, it is advisable to store the microscope in a waterproof container with a drying agent.
4- Do not touch the optical lens with bare fingers
5- Do not store the microscope in direct sunlight